## Slide 1: Small-Scale Variability of Discrete Soil Sample Data Part 2: Implications for Environmental Investigations
Hot Spots
vs
Hot Areas
TSCA…
Bias vs Precision
Inliers and Outliers
95% UCL
October 21, 2015
Roger Brewer, John Peard, Jordon Nakayama, (Hawai’i Dept of Health)
Marvin Heskett (Element Environmental)
Contact: roger.brewer@doh.Hawaii.gov

## Slide 2
Too many people to count…
Acknowledgements
The following is a compilation of experience, thoughts and ideas for new approaches based on talks with many people over the past ten years. This is an evolving field and we anticipate many more discussions and new discoveries to come.

## Slide 3
1. *Small-Scale Variability of Discrete Soil Sample Data (June 2015):
Part 1: Field Investigation of Discrete Sample Variability,
Part 2: Causes and Implications for Use in Environmental Investigations
2. Technical Guidance Manual (2009, updates in progress)
Hawai′i Department of Health, Hazard Evaluation and Emergency Response: http://eha-web.doh.hawaii.gov/eha-cma/Org/HEER/
References
*Current Posting: “What’s New” (July 2015)
All data available on web page in Excel format

## Slide 4
Multi Increment Sampling
Just Another Tool in the Tool Box?

## Slide 5
Perhaps the sentiments contained in the following pages, are not yet sufficiently fashionable to procure them general Favor; a long habit of not thinking a Thing wrong gives it a superficial appearance of being right, and raises at first a formidable outcry in defense of Custom. But the Tumult soon subsides. Time makes more Converts than Reason.
Thomas Paine, 1776 (Common Sense, on succession and independence of the new United States from Great Britain)
Change Can Be Disrupting…

## Slide 6: Small-Scale Variability of Discrete Soil Sample Data Part 1: Field Investigation of Discrete Sample Variability
October 7, 2015
Roger Brewer, John Peard, Jordan Nakayama, (Hawai’i Dept of Health)
Marvin Heskett (Element Environmental)
Contact: roger.brewer@doh.Hawaii.gov
If I had one hour to solve the problems of the world I would spend 59 minutes on explaining the problem and 1 minute on explaining the answer.
Albert Einstein

## Slide 7
“When there is little distance between points it is expected that there will be little variability between points.”
USEPA 1989: Methods for Evaluating the Attainment of Cleanup Standards
“The implicit assumption (that…) contamination is… likely to be (uniformly) present anywhere within the sampling area is reasonable.”
“The PCB level is assumed to be uniform within (a contamination zone/spill area) and zero outside it.”
USEPA 1985: Verification of PCB Spill Cleanup (basis of TSCA regulations and guidance)
1980s Origin of Discrete Soil Sampling Methods
(based on testing of industrial chemicals and waste)

## Slide 8
Metals
PCBs
Study Question: How variable are contaminant concentrations in co-located, discrete soil samples?
1. Intra-Sample Variability
(one sample tested ten times)
3 feet
2. Inter-Sample Variability
(five MIS processed samples tested)
Total 15 concentrations obtained per grid point

## Slide 9
Discrete Sample Variability Field Study - Results
Study Site A
(arsenic in wastewater)
Study Site B
(lead in incinerator ash)
Study Site C
(PCBs transformer oil)
24 grid points designated at each site;
Discrete surface soil samples collected (average 0-4”);
Variability within single samples and between co-located samples evaluated;
Triplicate Multi Increment samples also collected.
60’
120’
N
1
2
3
4
5
6
7
8
9
24
23
22
21
17
15
13
13
20
19
18
17
12
11
10
30’
50’
N
150’
90’

## Slide 10
Study Site A (Arsenic)
-Estimated Total Discrete Sample Variability-
(quartiles plus minimum, median and maximum)
Data for discrete soil sample collected at grid point can be highly random;
Any given sample unlikely to be representative of grid area mean.
*Arsenic bioavailability at site very low (<10%), minimal exposure risk.
Chart: *Arsenic (mg/kg)
 | 170 | 120 | 290 | 380 | 310 | 290 | 94 | 190 | 200 | 300 | 300 | 340 | 290 | 310 | 240 | 210 | 120 | 170 | 110 | 140 | 240 | 140 | 200 | 140
 | 10 | 20 | 10 | 30 | 20 | 0 | 16 | 40 | 90 | 30 | 30 | 10 | 20 | 40 | 10 | 10 | 30 | 10 | 0 | 10 | 20 | 0 | 0 | 20
 | 10 | 90 | 50 | 0 | 10 | 0 | 20 | 0 | 10 | 0 | 0 | 20 | 0 | 30 | 10 | 80 | 0 | 0 | 10 | 0 | 0 | 10 | 30 | 10
Median Max:Min = 2.0X
Maximum Max:Min = 4.0X
(lumpy porridge)
Notes: Study Site A Summary Notes:
-XRF data average 31% higher than 6010B data (inefficient extraction of arsenic at lab)
-Relatively low variability within and between co-located samples
-Variability is random, no distinct increasing/decreasing trends toward adjacent grid points
-Magnitude of variability similar within and between co-located samples
-Processing sample (e.g., dry, sieve, subsample) will minimize intra-sample variability (i.e., data reasonably representative of sample) but does not address inter-sample variability.

## Slide 11
Chart: Lead mg/kg
 | 150 | 84 | 320 | 500 | 95 | 270 | 240 | 300 | 96 | 140 | 240 | 300 | 180 | 200 | 220 | 340 | 320 | 270 | 370 | 490 | 170 | 190 | 150 | 250
 | 70 | 26 | 10 | 180 | 1 | 30 | 0 | 80 | 2 | 40 | 50 | 110 | 0 | 40 | 10 | 30 | 10 | 40 | 110 | 70 | 0 | 10 | 10 | 20
 | 70 | 110 | 80 | 10 | 64 | 0 | 20 | 10 | 12 | 20 | 10 | 90 | 20 | 10 | 20 | 130 | 10 | 70 | 30 | 30 | 70 | 60 | 20 | 30
Study Site B (Lead)
-Estimated Total Discrete Sample Variability-
(quartiles plus minimum, median and maximum)
200 mg/kg
(HDOH)
400 mg/kg
(USEPA)
Potential discrete samples above and below 200 mg/kg at 23 of 24 grid points;
Potential discrete samples above and below 400 mg/kg at 20 of 24 grid points.
Median Max:Min = 7.5X
Maximum Max:Min = 42X
(house salad)
Notes: Study Site B Summary Notes:
-XRF data average -7% lower than 6010B data (moisture effects?)
-Relatively high variability within samples but lower between samples
-Variability is random, no distinct increasing/decreasing trends toward adjacent grid points
-Different handfuls of the same salad, highly variable with a sample but similar to nearby samples
-Discrete samples above and below 200 mg/kg at 23 or 24 grid points

## Slide 12
N
Study Site B (Lead)
Fraction of Intra-Sample Data
Above and Below 200 mg/kg

## Slide 13
Chart: 
 | 0.94 | 14 | 63 | 420 | 93 | 37 | 0.15 | 0.24 | 7.4 | 24 | 9.9 | 600 | 0.24 | 0.18 | 3.6 | 14 | 16 | 29 | 0.05 | 0.43 | 19 | 27 | 1.8 | 6
 | 0.56 | 1 | 147 | 1580 | 3 | 4 | 0.03 | 0.08 | 2 | 2 | 8.1 | 380 | 0.13 | 0.02 | 0 | 2 | 0 | 4 | 0.004 | 0.57 | 7 | 12 | 3.4 | 1.7
 | 0.3 | 0 | 270 | 300 | 14 | 4 | 0 | 0.14 | 6.6 | 11 | 24 | 120 | 0.23 | 0.06 | 0 | 2 | 24 | 3 | 0.007 | 0.2 | 6 | 1 | 2.3 | 6.3
Study Site C (PCBs)
-Estimated Total Discrete Sample Variability-
(quartiles plus minimum, median and maximum)
1.1 mg/kg
50 mg/kg
Median Max:Min = 39X
Maximum Max:Min = >1,000X
Degree of variability similar between high and low concentration areas;
Suggest presence of PCB “nuggets” in soil.
Log Scale
(salad bar)
PCBs mg/kg
Notes: Study Site C Summary Notes:
-Very high variability within samples but lower between samples
-Variability is random, no distinct increasing/decreasing trends toward adjacent grid points
-Any given concentration random, like randomly selecting multi-colored gumballs from a jar
-PCBs above and below potential screening levels at majority of points.

## Slide 14
Study Site C (PCBs)
A True Hot “Spot”
4.9 mg/kg
7.7 mg/kg
6.0 mg/kg
91 mg/kg
14 mg/kg
3 feet
Intra-Sample Test Average
2,400! mg/kg
Grid Pt VOA-24
Take home Point: Concentration reported for any given discrete sample is random within a potentially significant large range of possibilities.
*Processed samples; variability for unprocessed samples would be even greater.

## Slide 15
Nugget Effect and Discrete Sample Variability
(aka “Distributional Heterogeneity”)
PCB-Infused Tar Balls?
1mm
Study Site C
Arsenic-Infused Clumps of Iron Hydroxide
Study Site A
Variability within and between samples reflects “distributional heterogeneity;”
“Maximum” concentration is always either 0% or 100%;
Pre-designation of mass (area/volume) of soil targeted for estimation of mean concentration critical (i.e., “Decision Unit”);
Risk-based screening levels apply to mean for the targeted mass (e.g., exposure area), not discrete samples within this area.
Study Site B
Small pockets of
concentrated ash
(visible in field)
Cutler 2011

## Slide 16
Discrete Samples are too SMALL to Capture and Represent Small-Scale Variability in Soil
2010s Reality
Sample collection method and mass very important
1980s Wishful Thinking
Sample collection method and mass not important
Lab Subsamples

## Slide 17
What Soil Contamination Would
Look Like if You Could Actually See It
Jackson Pollock
splatter painting
Spilled milk following low areas
Can’t be reliably characterized using discrete samples
Discrete Samples
(actual size)

## Slide 18
Small-scale, random variability of contaminant concentrations over a few inches or feet;
Concentration reported for any given discrete sample is largely random;
Statistics can’t fix bad data.
Concentrations highly variable around any given grid point
Problem Can’t be Fixed by Collecting More Discrete Samples

## Slide 19
“When there is little distance between points it is expected that there will be SIGNIFICANT variability between points.”
2015 update to USEPA 1989: Methods for Evaluating the Attainment of Cleanup Standards
“The implicit assumption (that…) contamination is… likely to be (uniformly) present anywhere within the sampling area IS NOT reasonable.”
“The PCB level CANNOT assumed to be uniform within (a contamination zone/spill area) and zero outside it.”
2015 update to USEPA 1985: Verification of PCB Spill Cleanup (basis of TSCA regulations and guidance)
Update to Original Assumptions

## Slide 20
Implications…
This is your last chance…
After this, there is no turning back.
You take the red pill – you stay in Wonderland and (find out) how deep the rabbit hole goes.
Morpheus (starting Neo on his journey in The Matrix )

## Slide 21
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.
Part 2 - Implications

## Slide 22
Metals: 1g
Representativeness of Laboratory Data
No standard laboratory protocol for “homogenization” of soil samples;
Fines settle to bottom with stirring;
Bulk soil samples can’t be efficiently “homogenized” without grinding;
Single, random, 1-30g subsample unlikely to be representative bulk sample (if entire sample mass could be tested).
“…mixing should be performed as needed or feasible to homogenize the sample until the subsampling variance is less than the data quality objectives (SW 846 Chapter 3, USEPA 2007).”
VOCs: 5g
Organics: 10-30g

## Slide 23
Sample air dried and sieved (preserved in methanol for VOCs);
30-50+ increment subsample collected for analysis;
Preserves field representativeness of original bulk sample;
Test precision of subsampling laboratory replicates;
Labs have been recommending this for decades but not pushed by regulators (plus added cost).
Laboratory Processing and Subsampling
Notes: Evenly distribute prepped materials onto a tray covered with Aluminum foil, butcher paper or other inert cover. The sample layer should have a depth similar to the depth of the rectangular scoop that will be used for sampling.
For inorganic metals digestion, use a smaller scoop to sub-sample an aliquot size of 10g or more and store in a pre-cleaned container. For organic extraction, use a rectangular metal scoop to obtain an aliquot size of at least 30g in a pre-cleaned container.
Perform the sub-sampling by taking random scoops from the sample on the tray. The scoop should be taken evenly from the top to the bottom of the soil. A stratified random approach should be used. Each scoop must represent approximately 1/30th of the desired target mass of 0.33g or 1 g respectively. Practice on a few scoops before proceeding on the entire sample by measuring the weight of one scoop of soil. This may be done less frequently with knowledge of the type of soil. Once the desired amount is achieved, take scoops to represent the entire area of the tray in a random fashion. Record the final weight, which should be at least 10 or 30g. If the final amount is less than the required amount, take a few more scoops. If the amount is much greater than the desired amount, it may be necessary to recombine the sub-sample and start over.

## Slide 24
Part 2 - Implications
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
  Effects of randomness in discrete data;
  Examples mapping errors;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 25
In an Ideal World…
Apparent
“Hot Area” Identified
Discrete Soil Samples
Subsample
Randomly Selected and Tested by Lab
What you hope is happening…
Ideal
Field sample and lab subsample mass not important;
Discrete sample are representative of surrounding area;
Laboratory data are representative of sample submitted.

## Slide 26
Reality
What is really happening…
Discrete Soil Samples
“Uniformly” heterogeneous contamination across area
  Randomness of Discrete Sample Data;
Subsample
Randomly Selected and Tested by Lab
Field sample and lab subsample mass very important;
Discrete samples are random specimens of field heterogeneity;
Laboratory data are random specimens of sample heterogeneity.

## Slide 27
Soil is a very heterogeneous material. Samples with very small support volume… may vary from zero to very high concentrations.
USEPA 1989. Soil Sampling Quality Assurance User’s Guide
The so-called grab sample is not really a sample but a specimen of the material that may or may not be representative of the sampling unit. Great care must be exercised when interpreting the meaning of these samples.
USEPA 1992, Preparation of Soil Sampling Protocols
Not a New Discovery…

## Slide 28
Part 2 - Implications
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
  Effects of randomness in discrete data;
  Examples mapping errors;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 29
Encountering False Negatives and Positives is Unavoidable
Exposure Area A
(mean fails)
Exposure Area C
(mean passes)
Exposure Area B
(mean fails)
What’s Really Happening…
Large Areas of Contaminated Soil Left
Unnecessary Removal of Soil
Progression of Investigation
Over Time
Inliers, Outliers and Misinterpretation of Discrete Data
Assume clean boundaries

## Slide 30: Former Pesticide Mixing Area Discreet Sample Data (>100 *samples)
50’
Contamination <3’bgs (ave. 1.5’ bgs; est. 1,300 yds3)
Contamination >3’-10’bgs (est. 2,000 yds3)
*All sample points not shown
Dioxins and Arsenic
After ITRC (2014)
For Example Only
Notes: Speaker Notes
Long-scale heterogeneity is the spatial scale at which differences in concentration are expected.
Sampling programs are generally designed to search for variation in concentrations at this scale.

## Slide 31
Perimeter DUs
Contamination <3’bgs (est. 2,000 yds3)
Contamination >3’-10+’bgs (est. 5,500 yds3)
<Screening Levels
MIS-DU Investigation Results
(significantly more contamination identified)
Lateral and vertical extent of contamination underestimated by discrete data
50’
For Example Only

## Slide 32: Why DUs (and ISM) are Important (Discrete Sample Data)
>Action Level
<Action Level
100’
PCB sample aliquot = 30 grams (one spoonful of soil)
Discrete data: Estimated 10,000 ft2 soil
?
After ITRC (2014)
PCBs
Discrete Sample
Notes: No associated notes.

## Slide 33: Why DUs (and ISM) are Important (ISM Sample Data)
> Action Levels
< Action Levels
MIS Data: Estimated 25,000+ ft2 soil
(perimeter DUs pending)
Perimeter DUs
PCBs
After ITRC (2014)
100’
Notes: No associated notes.

## Slide 34: Why DUs (and ISM) are Important (ISM Sample Data)
> Action Levels
< Action Levels
Perimeter DUs
PCBs
After ITRC (2014)
2015 Status Update:
Higher concentrations of PCBs reported using MIS;
Reversion to discrete sampling currently being required by USEPA under TSCA (almost 1,000 samples!);
USEPA scientists aware of problem;
Working with USEPA attorneys (and HDOH) to develop regulatory pathway forward (e.g., Risk-Based Option.)
The best way to get a bad law (or policy) repealed is to enforce it strictly.
Abraham Lincoln
Notes: No associated notes.

## Slide 35
Part 2 - Implications
*For example only. Parties associated with examples provided are aware of data interpretation limitations
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
*Interpretation of isoconcentration maps;
  Heterogeneity and artificial “hot spots”;
  Example over-interpretation of data;
Exposure concentrations and risk assessments;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 36
Chart: Lead mg/kg
 | 150 | 84 | 320 | 500 | 95 | 270 | 240 | 300 | 96 | 140 | 240 | 300 | 180 | 200 | 220 | 340 | 320 | 270 | 370 | 490 | 170 | 190 | 150 | 250
 | 70 | 26 | 10 | 180 | 1 | 30 | 0 | 80 | 2 | 40 | 50 | 110 | 0 | 40 | 10 | 30 | 10 | 40 | 110 | 70 | 0 | 10 | 10 | 20
 | 70 | 110 | 80 | 10 | 64 | 0 | 20 | 10 | 12 | 20 | 10 | 90 | 20 | 10 | 20 | 130 | 10 | 70 | 30 | 30 | 70 | 60 | 20 | 30
Study Site B: Estimated Total Grid Pt Variability
(quartiles plus minimum, median and maximum)
200 mg/kg
(HDOH)
400 mg/kg
(USEPA)
Potential discrete samples above and below 200 mg/kg at 23 of 24 grid points;
Potential discrete samples above and below 400 mg/kg at 20 of 24 grid points.
What Does Random, Discrete Sample Variability Look Like on a Map?
Grid Pt #21
103-419 mg/kg
Notes: Study Site B Summary Notes:
-XRF data average -7% lower than 6010B data (moisture effects?)
-Relatively high variability within samples but lower between samples
-Variability is random, no distinct increasing/decreasing trends toward adjacent grid points
-Different handfuls of the same salad, highly variable with a sample but similar to nearby samples
-Discrete samples above and below 200 mg/kg at 23 or 24 grid points

## Slide 37
165
Random Map Patterns and Artificial “Hot Spots”
>800 mg/kg
>400 mg/kg
>200 mg/kg
<200 mg/kg
Study Site B (lead): Random lead concentration assigned within estimated range for grid point
Grid Pt #21
103-419 mg/kg
401
Notes: Isolated “hot spots” and “cold spots” are an artificial reflection of small-scale, random heterogeneity.

## Slide 38
How to Make Artificial “Hot Spots” with Cards
Ace
Face Card
7-10
2-6
Deck of cards placed on each grid point;
Every grid point is identical (no isolated “spots”);
Randomly drawn card creates artificial patterns.
Pick a Card…
Notes: Isolated “hot spots” and “cold spots” are an artificial reflection of small-scale, random heterogeneity.

## Slide 39
>250 mg/kg
>50 mg/kg
>1.1 mg/kg
<1.1 mg/kg
145
Grid Pt #24
1.6-215 mg/kg
38
Large-Scale Patterns Can be Real: Study Site C (PCBs)
Consistent, large-scale pattern in upper area;
Random small-scale patterns within.
Notes: Isolated “hot spots” and “cold spots” are an artificial reflection of small-scale, random heterogeneity.

## Slide 40
Part 2 - Implications
*Parties associated with examples provided are aware of data interpretation limitations
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
*Interpretation of isoconcentration maps;
  Heterogeneity and artificial “hot spots”;
  Example over-interpretation of data;
Exposure concentrations and risk assessments;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 41
500km
N
Real Large-Scale Patterns and
Artificial Small-Scale “Hot Spots”
Arsenic in US Surface Soil (USGS 2014)
OK
NC
Based on approximately 4,000, 1m2 ground samples

## Slide 42
US Geologic Map
Felsic igneous?
Basin & Range volcanics
Coastal Plain
Blue Ridge & Piedmont MM & igneous rocks
Glacial cover
Floodplain deposition from upper watershed and/or As from rice farms?
Paleozoic black shales, coal, etc.
Large-scale arsenic map patterns correlate well with regional geology
Rocky Mountains

## Slide 43
125km
Approximately 300 samples collected from 400K km2 area;
Large-scale patterns likely tied to geologic provinces, etc.;
Small-scale “hot spots” and “cold spots” within larger areas likely reflect random, small-scale heterogeneity;
Similar small-scale patterns if samples recollected but in different locations.
False Resolution Within Large-Scale Patterns
(Oklahoma/Texas)
Notes: Structures removed. No obvious spill areas observable in the field.

## Slide 44
25km
Artificial 2,400 km2 Arsenic “Hot Spot” in NC
Based on single, 1m2 discrete soil sample,
Heterogeneous, metamorphic geologic terrane;
Sample likely collected from random, narrow mineralized zone;
Significant over interpretation of discrete sample data.
X
Discrete sample location
Notes: Structures removed. No obvious spill areas observable in the field.

## Slide 45
500km
N
Small Print: “The resulting data sets are not appropriate for the accurate estimation of the concentration of a given element or mineral at a site where a sample was not collected (USGS 2014).”
More Realistic Resolution of USGS As Data
(example only, not included in report)

## Slide 46: Former Pesticide Mixing Area - Arsenic
Field XRF and tight grid of discrete samples used to identify spill area;
Large-scale patterns likely real;
Transition zone marked by small, likely artificial “hot spots” and “cold spots”;
Reflects random, small-scale variability above and below screening level.
Field discrete samples
9 acres
For example only
C
Heterogeneity Range below Screening Level
Heterogeneity Range Above Screening Level
A
Heterogeneity Range overlaps Screening Level
B
B
Isolated
“Hot Spots”
Notes: Structures removed. No obvious spill areas observable in the field.

## Slide 47: Realistic Screening Level Data Resolution
9 acres
For example only
C
B
Moderate
Contamination
Most defensible interpretation of discrete sample data;
Boundaries between “contaminated zones” very fuzzy;
Upfront removal of heavily contaminated area possible;
Passage or failure of Zone B uncertain;
Designation of DU and collection of MI confirmation required.
C
A
B
B
Heavy Contamination
Low/No
Contamination
Notes: Structures removed. No obvious spill areas observable in the field.

## Slide 48: Same Confusion at Depth…
0’
1
2
3
4
5
6
7
8
9
Borings
Discrete samples identify multiple contaminated areas;
Meaning of isolated “hot spots” at depth uncertain;
Excavation plan developed.
-5’
-10’
-15’
Above Screening Level
Below Screening Level
Discrete
Sample

## Slide 49: Fooled Again by Heterogeneity…
0’
A
B
B
C
C
Heterogeneity Zones
1
2
3
4
5
6
7
8
9
Borings
Reported concentrations for discrete samples are random within an unknown range;
Isolated “hot spots” and “cold spots” reflect heterogeneity;
Discretes catch core but miss contamination in Zone B .
-5’
-10’
-15’
Above Screening Level
Below Screening Level

## Slide 50
Part 2 - Implications
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
  Comparison of data to screening levels;
  What are we looking for?
  Representativeness of discrete data sets;
  Interpretation of “outlier” data;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 51: 1st Red Flag: Risk-Based Screening Levels Do Not Apply to Individual Discrete Samples
“The concentration term in the intake equation is the arithmetic average of the concentration that is contacted over the exposure period.”
USEPA 1989: Methods for Evaluating the Attainment of Cleanup Standards
For Superfund assessments, the concentration term in the intake equation (used to generate the RSLs) is an estimate of the arithmetic average concentration for a contaminant based on a set of site sampling results.
USEPA 1992: A Supplemental Guidance to RAGS: Calculating the Concentration Term

## Slide 52
“Risk estimates (are) developed for a particular exposure area and time period….
The mean concentration (should) be less than the cleanup standard and… (the) area of contaminated soil (should not) be larger than a specified size (e.g., target exposure area)…”
“Although this concentration does not reflect the maximum concentration that could be contacted at any one time, it is regarded as a reasonable estimate of the concentration likely to be contacted over time.”
USEPA 1989. Risk Assessment Guidance for Superfund, Volume I, Human Health Evaluation Manual
Exposure Area Means

## Slide 53: Risk Assessment vs Field Mapping
Sampling data from Superfund sites have shown that data sets with fewer than 10 samples per exposure area provide poor estimates of the mean concentration.
USEPA 1992: A Supplemental Guidance to RAGS: Calculating the Concentration Term
Small numbers of discrete soil samples routinely used to define edges of contamination;
Unlikely to be representative of true contaminant mean in those areas;
Can result in over or under estimation of contamination above levels of potential concern.

## Slide 54
Side Thought: Evolution of Environmental Data
Individual
Discrete Samples
Statistical Analysis of Discrete Data Sets
Environmental
Field Investigations
Environmental
Risk Assessment
Mineral Exploration, Agriculture, etc.
*Multi Increment Sampling Methods
mid 1980s
mid 1980s
late 1980s
Pre-1950s?
1960-1980s?
1980s-1990s
2000s
2000s
*First sampling theory methods published in 1950s. US Army Corps initiated use of DU-MIS methods for environmental investigations in 1990s
X

## Slide 55
Part 2 - Implications
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
  Comparison of data to screening levels;
  What are we looking for?
  Representativeness of discrete data sets;
  Interpretation of “outlier” data;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 56: Decision Units (DUs) – Nothing New
DU: Area and volume of soil you would send to the lab as a single sample, if you could.
Exposure Area DUs
Source Area DUs
Notes: Refer to ITRC ISM-1 Section 3.3.1 Exposure Area Decision Units and
ITRC ISM-1 Section 3.3.2 Source Area Decision Units

## Slide 57
Historical information on production, discharge or storage of chemicals of potential concern can be used to identify separate (hot spot) areas (for characterization).
USEPA 1991: Guidance for Data Usability in Risk Assessment
Early Concepts of “Spill Area Decision Units”

## Slide 58
“When choosing a sampling plan, one must know the concentration patterns likely to be present (within the investigation area). Advance information on these patterns is used… An example is to divide a heterogeneous (investigation area) into more homogeneous parts (i.e., “DUs”)… and to select samples independently within each part.”
Gilbert 1987. Statistical Methods for Environmental Pollution Monitoring
Grid Spacing Based on Anticipated Spill Area Size
“To apply this (grid-based discrete sampling) method, the following assumptions are required… The shape and size of the contaminated zone must be known at least approximately.”
USEPA 1987: Data Quality Objectives for Remedial Response Activities

## Slide 59: The Search for BIG “Hot Spots”
If the particles (of contaminants) were all concentrated in the soil so that they formed a “hot spot” of perhaps the top ten cm of one acre…, it would be important to locate the hot spot (i.e., the one-acre area) so that remedial action could be taken.
USEPA 1989: Soil Sampling Quality Assurance User’s Guide
The (person setting the grid spacing) must determine… the acceptable probability of not finding an existing contaminated zone in the suspected area. For instance, it might be determined that a 20 percent chance of missing a 100ft-by-100ft (10,000ft2) contaminated zone is acceptable but only a 5 percent chance of missing a 200ft-by-200ft (40,000ft2) zone is acceptable.
USEPA, 1987, Data Quality Objectives for Remedial Response Activities

## Slide 60
Part 2 - Implications
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
  Comparison of data to screening levels;
  What are we looking for?
  Representativeness of discrete data sets;
  Interpretation of “outlier” data;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 61
Sampling data from Superfund sites have shown that… data sets with 20 to 30 samples provide fairly consistent estimates of the mean.
USEPA 1992: A Supplemental Guidance to RAGS: Calculating the Concentration Term
Are 20 to 30 samples really enough?

## Slide 62
Estimation of Means from Random Discrete Data Sets
Study Site A
(arsenic in wastewater)
Study Site B
(lead in incinerator ash)
Study Site C
(PCBs transformer oil)
60’
120’
N
1
2
3
4
5
6
7
8
9
24
23
22
21
17
15
13
13
20
19
18
17
12
11
10
30’
50’
N
150’
90’
Hypothetical data sets generated by random selection of grid points and intra-sample data;
  Purely random 10-point data sets;
  Random data for 24-point grid;
  20 iterations each scenario;
ProUCL used to calculate 95% mean.

## Slide 63
Purely Random Intra-Sample Data Sets
(10 grid points, 20 iterations)
Study Site | Range 95% UCL (mg/kg) | Range RSD
Site A (arsenic) | 403 to 776 | 34% to 67%
Site B (lead) | 201 to 439 | 20% to 86%
Site C (PCBs) | 9.4 to >1,000,000 | 124% to 315%
Ten samples not consistent

## Slide 64
Random Intra-Sample Data Sets for Full Grid
(24 grid points, 20 iterations)
Study Site | Range 95% UCL (mg/kg) | Range RSD
Site A (arsenic) | 395 to 492 | 39% to 54%
Site B (lead) | 280 to 394 | 49% to 80%
Site C (PCBs) | 652 to 8,884 | 251% to 434%
*24 samples more consistent;
Moderate to high RSD at arsenic and lead sites;
Very high RSD with 24 samples at PCB site;
*Representativeness of 24-point grid unknown.

## Slide 65
Study Site Multi Increment Data
Triplicate 50- to 60-increment MI samples collected from each study site;
Most reliable data for estimation of mean contaminant within targeted area and decision making.
Study Site A
(arsenic in wastewater)
Study Site B
(lead in incinerator ash)
Study Site C
(PCBs transformer oil)

## Slide 66
Study Site A
(arsenic in wastewater)
Study Site A | 
Triplicate MI Sample Data | 
Sample A: | 220 mg/kg
Sample B: | 250 mg/kg
Sample C: | 230 mg/kg
RSD: | 6.5%
Mean: | 233 mg/kg
*95% UCL: | 259 mg/kg
*Student's t | 
Study Site A (Arsenic) MI Triplicates
60-increment MI samples;
Very good precision (<35%);
Exceeds default arsenic background of 24 mg/kg;
Obtain bioaccessibility data for highest sample (SBRC-g) for comparison to BA Arsenic action level (23 mg/kg).

## Slide 67
Study Site B
(lead in incinerator ash)
Study Site B | 
Triplicate MI Sample Data | 
Sample A: | 240 mg/kg
Sample B: | 270 mg/kg
Sample C: | 350 mg/kg
RSD: | 20%
Mean: | 287 mg/kg
*95% UCL: | 346 mg/kg
*Student's t | 
55-increment MI samples;
Reasonably good precision (<35%);
Exceeds HDOH action level of 200 mg/kg.
Study Site B (Lead) MI Triplicates

## Slide 68
Study Site C
(PCBs transformer oil)
Study Site C | 
Triplicate MI Sample Data | 
Sample A: | 270 mg/kg
Sample B: | 24 mg/kg
Sample C: | 19 mg/kg
RSD: | 138 %
Mean: | 104 mg/kg
*95% UCL: | 467 mg/kg
*Chebyshev | 
60-increment MI samples;
Very poor precision (>100%);
Retest of samples at lab showed good precision (field error);
Reliability of sample mean and 95% UCL low;
Subdivide original DU into smaller DUs, increase increment count (75+) and sample mass and recharacterize.
Study Site C (PCBs) MI Triplicates

## Slide 69
Study Site | Discrete Data (24 Grid Points ave) |  | MIS Data (triplicate samples) | 
 | Range 95% UCL (mg/kg) | Range RSD | 95% UCL (mg/kg) | RSD
Site A (arsenic) | 395 to 492 | 39% to 54% | 259 | 6.5%
Site B (lead) | 280 to 394 | 49% to 80% | 346 | 20%
Site C (PCBs) | 652 to 8,884 | 251% to 434% | 467 | 138%
Who’s Right?
Multi Increment vs Discrete Sample Data
Multi Increment data provide far better statistical precision.

## Slide 70
Multi Increment vs Discrete Sample Data
-Sample Support-
Sampling Method | Number of DU Points | Total Mass of Soil Represented (grams) | Total Number of Analyses
Discrete Sample Data (24): | 24 | 24 | 24
MI Sample Data (Triplicates): | 180 | 4,500 | 3
Multi Increment data provide far better sample support.

## Slide 71
How do you know if a set of discrete samples is representative of targeted area? (Ideas needed)
Statistical evaluation of single data set only addresses precision with respect to test used and data set provided;
Field representativeness of single data set can’t be directly evaluated in absence of replicate data sets (?);
Samples must also meet Sampling Theory requirements for sufficient mass, distribution, shape, subsampling, etc. (i.e., test every increment).
Notes: 1. Mean and 95% UCL based on use of lowest, mean, median and maximum concentration reported for each grid point.
2. ProUCL Version 5.0 (recommended UCL noted)

## Slide 72
Part 2 - Implications
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
  Comparison of data to screening levels;
  What are we looking for?
  Representativeness of discrete data sets;
  Interpretation of “outlier” data;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 73
Seek and Yee Shall Find…
The more (discrete) samples collected, the more likely that one sample will exceed a cleanup standard (i.e., “outliers” will be identified).
USEPA, 1989, Methods for Evaluating the Attainment of Cleanup Standards
Also:
The smaller mass tested, the more likely that one sample will exceed a cleanup standard (e.g., 30g vs 10g vs 1g);
The maximum concentration of a contaminant in soil (at a small enough scale) is always 0% or 100%.

## Slide 74
Disruptive Outliers?
Outliers distort… statistics of interest. Therefore, it is desirable to… not to compute… statistics by accommodating a few low probability outliers.
USEPA 2013. ProUCL User Guide.
Delete the “outliers” after you find them?
Statisticians often get stuck with un-interpretable data…

## Slide 75
“Outliers” are Important
All data not known to be in error should be considered valid… High concentrations are of particular concern for their potential health and environmental impact.
USEPA 1989. Methods for Evaluating the Attainment of Cleanup Standards
All the constituents of the lot (DU) to be sampled must be given an equal probability… of being selected and preserved as part of the sample (data).
Pitard 2005
Keep outlier data…

## Slide 76
Forced to Fit In
A common error has been to reject “outliers” that cannot be made to fit (a statistical) model...
The tendency… has been to make the data fit a preconceived model instead of searching for a (more appropriate way to collect samples).
Pitard 2009
(Improper) sampling protocol (for particulate matter) introduces an enormous fundamental error (in the data set) that confuses the interpretation of the data (and) subsequent geostatistical studies.
Pitard 1993.
Outlier data for soil are artifacts of improper sampling.

## Slide 77
Improving Performance by Ignoring Data…
(Study Site C – Mean Intra-Sample Data)
Calculation Method | 95% *UCL (mg/kg | RSD
With “Outliers” | 1,851 | 328%
Without “Outliers” | 41 | 133%
20 “Good” Discrete Samples
4 “Bad” “Outliers”?
Study Site C
X
X
X
X
*Chebyshev

## Slide 78
Capturing and representing distributional heterogeneity within a targeted area/volume of soil (or rock) is critical to correct sampling;
“Outlier” areas of higher concentrations often drive decision making;
Entire DU eventually dug up and extracted (ultimate test of sample representativeness);
It’s the sampling method, not the statistical models.
Gold Miners Love Outliers!
What is the mean concentration of gold in this ore body?
Outliers Are Golden

## Slide 79
>250 mg/kg
>50 mg/kg
>1.1 mg/kg
<1.1 mg/kg
145
38
Excavating “Outliers” Isn’t The Answer Either
“Hot spots” can be random artifacts of heterogeneity;
Removing grid point “hot spots” misleading;
Resampling of full area required to re-estimate mean.
Surprise! Bouncing Hot Spots!
X
X
Hot Spots IDd
Study Site C
Notes: Isolated “hot spots” and “cold spots” are an artificial reflection of small-scale, random heterogeneity.

## Slide 80
I know what you’re thinking…
I know what you're thinking, 'cause right now I'm thinking the same thing. Actually, I've been thinking it ever since I got here:
Why oh why didn't I take the BLUE pill?
Cypher (to Neo in The Matrix )

## Slide 81: Solution: Sampling Theory -Decision Units & Multi Increment Samples-
Sometimes the questions are complicated and the answers are easy.
Dr Seuss
Particulate sampling theory is new to most environmental investigators even though the techniques used to apply the theory to soil sampling are familiar.
USEPA 1992, Preparation of Soil Sampling Protocols

## Slide 82
Part 2 - Implications
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
Sampling Theory and DU-MIS investigations;
  Sampling Theory explained with salad;
Regulatory hurdles.

## Slide 83
Sampling Theory – Detailed Details…
Causes of Erroneous Data:
Fundamental Error;
Grouping & Segregation Error;
Increment Delimitation Error;
Increment Extraction Error;
Periodic Error;
Preparation Error;
Analytical Error; etc.

## Slide 84: Sampling Theory Explained With Salad
Wrong Questions:
What is the maximum concentration of tomato in this salad?
What is the concentration of tomato at point “X”?
Primary Concern:
Long-term exposure to tomatoes

## Slide 85: Step 1: Define Objectives and Designate Decision Units
Right Question:
What is the mean concentration of tomato in this salad?
Random bits of salad to be eaten over a lifetime;
Entire salad represents the “Exposure Area” DU.

## Slide 86
Step 2. Collect a Representative Sample
Collect evenly spaced increments collection from targeted DU Area;
Sample must capture representative # of “hot spots” and “cold spots”;
Minimum 30 (low heterogeneity) to 75+ (high heterogeneity) points.
Increments
Incremental Sample

## Slide 87: Sampling Theory - Collect a BIG Sample (in order to capture and represent random, small-scale variability)
Soil Samples: Typical 30-50g increments and minimum 1-2+kg bulk MI sample
Capture the “outliers,” don’t toss them!

## Slide 88: Step 3: Laboratory Processing and Subsampling -Repeat Method Used in Field-
Bulk soil IS sample dried and sieved;
Subsampling process repeated to collect aliquot for testing (minimum 30 increments);
Preserves field quality of original sample;
Minimum 10-30g mass tested (normal metals = 1g).
Aliquot
Tested
by Lab

## Slide 89: Step 4. REPEAT Two More Times and Compare Data to Test Precision (“Triplicates”)
Analysis
Analysis
Analysis
1
2
3

## Slide 90: Increase Resolution of Data as Needed
Use smaller DUs to isolate and test suspected “hot areas;”
Optimizes “remediation” and quickly clears “clean” areas;
Designated optimal DU sizes at start of investigation.
*Suspected “hot” spill area and “clean” perimeters tested separately
DU-1
DU-2
DU-3
Perimeter DUs
Suspect Spill Area

## Slide 91: Sampling Theory Training
Envirostat, Inc.: Chuck Ramsey (www.envirostat.org)
Four-day, detailed introduction to sampling theory and Multi-Increment Sample® (MIS) site investigations.
ITRC: Incremental Sampling Methodology (ISM) Introduction to basics of sampling theory and incremental sampling (guidance + semi-annual webinars)
http://itrcweb.org/ism-1/
Hawai’i DOH Technical Guidance Manual & Workshops
Implementation of DU-MIS investigations in the field (1st edition 2009, updates in preparation)
http://eha-web.doh.hawaii.gov/eha-cma/Org/HEER/

## Slide 92
Sampling theory;
Decision Unit examples;
Multi Increment samples;
Use and limitations of discrete samples;
Common mistakes and problems;
Field implementation (tools, etc.)
Volatile contaminants;
Excavations;
Stockpiles;
Trenches;
Subsurface investigations;
Ecological investigations; etc.
Hawaii DOH Technical Guidance Manual
(draft updates to be posted by end of 2015)

## Slide 93
Details, Details (see HDOH TGM)
Field Tools (vary with soil type & depth)
Good
Not good
Increment Shape
Core wedges
Plugs (+/- COH4)
Subsample cores
Notes: Kea`au Middle School garden

## Slide 94
Part 2 - Implications
Outline:
Representativeness of laboratory data;
Mapping extent of contamination;
Interpretation of isoconcentration maps;
Exposure concentrations and risk assessments;
Sampling Theory and DU-MIS investigations;
Regulatory hurdles.

## Slide 95
Agency Policies and Regulations
No specific regulatory prohibition against use of Multi Increment (“Incremental”) sampling methods;
Innovation and improvement in efficiency of site investigations methods generally encouraged;
Current hurdles primarily due to lack of awareness of discrete sample unreliability and lack of experience with DU-MIS approaches;
Similar situation in Hawai’i in early 2000s.

## Slide 96
DU-MIS and PCBs Under TSCA
Discrete sampling approaches developed in mid 1980s;
Based on erroneous assumption of contaminant “uniformity” in soil;
Risk assessment guidance concurrently being developed;
Confusion over applicability of risk-based screening levels to any testable mass of soil (no) vs mean PCB concentration over a targeted, exposure area (yes).
Future changes in EPA policy may invalidate some of the discussions in this (guidance).
USEPA 1985: Verification of PCB Spill Cleanup

## Slide 97
“The implicit assumption (that…) contamination is… likely to be (uniformly) present anywhere within the sampling area (contaminated zone) is reasonable.”
USEPA 1985: Verification of PCB Spill Cleanup
Discrete Sample Grids Spaced to ID Spill Areas
“Any (single discrete) sample located within the contaminated zone will identify the contamination.”
USEPA 1987: Data Quality Objectives for Remedial Response Activities
“To apply this (grid-based discrete sampling) method… the shape and size of the contaminated zone must be known at least approximately.”
USEPA 1987: Data Quality Objectives for Remedial Response Activities

## Slide 98
Original grid spacing guidance based on assumed size of spill areas (100s-1,000’s ft2);
Single discrete sample assumed representative;
Spill area DU size can’t exceed Exposure Area DU.
The Search for PCB Spill Areas Under TSCA
40 CFR 761.61(a) Self-implementing on-site cleanup and disposal of PCB remediation waste;
Default grid spacings presented (basis unclear).
Example Spill Area Size

## Slide 99
MI Samples Improve Data Representativeness
X
X
X
X
DUs designated DUs based on suspect spill areas, assumed clean perimeters, exposure areas etc;
MI sample collected across entire DU;
Samples processed, subsampled and tested.
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X

## Slide 100
Intentional combination of anticipated PCB spill areas with anticipated clean areas for testing may violate “anti-dilution” clause in TSCA (40 CFR761.1(b)(5)):
  “"No person may avoid any provision specifying a PCB concentration by diluting the PCBs unless otherwise provided”;
Requires careful designation of Spill (Source) Area DUs in coordination with overseeing regulatory agency.
*DU-MIS and “Dilution” Under TSCA
*HDOH interpretation of TSCA intent

## Slide 101
Limited “Compositing” and “Dilution” Allowed Under TSCA to Save on Lab Costs
Soil combined across different DUs are composites;
Potential dilution of higher concentration in localized spill areas;
Laboratory result divided by number of discrete samples included in composite for comparison to cleanup level;
Ensures that no single “sampling area” (DU) exceeds target cleanup level.
Potential Spill Area
Composite

## Slide 102
Theoretical Compositing of Multi Increment Samples From Separate DUs
A single MI sample collected within a single DU is not a composite (i.e., of multiple DU samples);
Compositing of MI samples not allowed under HDOH guidance.
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Potential Spill Area
X
X
X
X
X
X
X
X
X
X
X
Composite

## Slide 103
Better understanding of “hot spots” and “Decision Units” (e.g., “Spill/Source” Areas and risk-based “Exposure Areas”);
Multi Increment (“incremental”) sample rather than discrete sample required to characterize a targeted DU area;
Replicate MI samples used to test precision (not required for discrete sampling);
Greater upfront time and cost but ultimately more reliable, faster and cost-effective.
DU-MIS Improvements to TSCA

## Slide 104
40 CFR 761.61(c)(1) Risk-based disposal approval:
“Any person wishing to sample, cleanup, or dispose of PCB remediation waste in a manner other than prescribed in paragraphs (a) or (b) of this section… must apply in writing to the EPA Regional Administrator in the Region.”
Proposed Path Forward: Incorporation of DU-MIS (ISM) Under TSCA “Risk-Based” Option
Hawai‘i DOH has proposed a formal agreement with USEPA IX for use of DU-MI sample data at PCB sites that come under joint oversight in accordance with HDOH guidance (currently in discussions).

## Slide 105: Summary
Concentrations of contaminants within and between co-located discrete soil samples can randomly vary by orders of magnitude over short distances;
This is predictable from Sampling Theory;
Laboratory data are not reliably representative of the discrete sample provided;
Discretes samples are not reliably representative of the area where they were collected;
This results in unnecessary delays and added cost to site cleanup;
DU-MIS approaches are designed to address these deficiencies and improve reliability and efficiency of environmental investigations.

## Slide 106
Discrete Sampling
Multi Increment Sampling
NOT Another Tool in the Tool Box…
It’s an entirely new and improved set of tools.
DU-MIS investigation methods were specifically developed to address well-known, serious deficiencies in traditional, discrete sampling methods.

## Slide 107
Questions?
The only real learning results from hangups, where instead of expanding the branches of what you already know, you have to stop and drift laterally for a while until you come across something that allows you to expand the roots of what you already know.
Robert Pirsig (Zen and the Art of Motorcycle Maintenance)