## Slide 1: Risk-Based Investigation and Characterization of Contaminated Soil and Sediment
Let me tell you why you’re here. You’re here because you know something. What you know you can’t explain. But you felt it. You felt it your entire life. That there’s something wrong with the world. You don’t know what it is, but it’s there. Like a splinter in your mind – driving you mad.
Morpheus (The Matrix )
Roger Brewer, PhD, Senior Environmental Scientist
Hawai´i Department of Health, Honolulu, Hawai´i, USA (roger.brewer@doh.hawaii.gov)
February 20, 2019

## Slide 2
HDOH, 2016, Technical Guidance Manual: Hawai‘i Department of Health, Office of Hazard Evaluation and Emergency Response, http://www.hawaiidoh.org/
References
HDOH, 2017, Evaluation of Environmental Hazards at Sites with Contaminated Soil and Groundwater: Hawai‘i Department of Health, Office of Hazard Evaluation and Emergency Response,
www.hawaii.gov/health/environmental/hazard/eal2005.html

## Slide 3: Six-Part Webinar Training Series (2017, recorded)
Site Investigation Design;
Decision Unit Designation;
Decision Unit Characterization (sampling theory);
Field Implementation of DU-MIS Methods;
Laboratory Processing;
Environmental Hazard Evaluation (aka “risk assessment”).
Hawaii DOH Webinar Webpage:
http://eha-web.doh.hawaii.gov/eha-cma/Leaders/HEER/Webinar

## Slide 4
Terminology
Risk Assessment Basics
Origin of Discrete Soil Sampling Methods
Field Study of Discrete Sample Data Reliability
“Decision Unit” and “Multi Increment” Sample Site Investigation Methods (DU-MIS)
Case studies
Regulatory transition from discrete to DU-MIS
Webinar Topics
If I had one hour to solve the problems of the world I would spend 59 minutes on explaining the problem and 1 minute on explaining the answer.
Albert Einstein

## Slide 5
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Discrete
Sample
(100-200g)
Decision Unit (DU)
DU-4
DU-3
DU-1
DU-2
?
?
Multi Increment® Sample
(1-2+kg)
Terminology
DU: Area/volume of soil you would collect and test as a single mass, if you could…;
Discrete Sample (used since 1980s):
  Collected from a single point within a targeted area (“single increment sample”);
  Mass collected based on laboratory needs (typically 100-200 grams).
Multi Increment Sample (relatively “new” idea):
  Collected from multiple points (“increments”) within a targeted area;
  Mass and # of “increments” included in sample based on Gy’s sampling theory.
Multi Increment is a registered trademark of EnviroStat, Inc.

## Slide 6
“Composited” Discrete Samples
(as defined in TSCA and other regulations)
Original: Separate decision to be made on each, separate “DU” sample collection area;
Soil from different areas “composited” in order to save on laboratory costs;
Potential under-representation of higher concentration area(s) by composite data;
Laboratory result multiplied by number of “DU areas” (i.e., discrete samples) included in composite for comparison to cleanup level.
“Composited”
Discrete
Samples
DU-4
DU-3
DU-1
DU-2

## Slide 7
A single MI sample collected within a single DU area is not a composite under TSCA and other USEPA regulations;
Compositing of MI samples not allowed under HDOH guidance;
Avoid use of term “composite” in reports.
Theoretical Compositing of Multi Increment Samples
(not allowed!)
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
“Composited”
Multi Increment
Samples
DU-4
DU-3
DU-1
DU-2

## Slide 8
Direct
Exposure
Groundwater
Leaching
Gross
Contamination
Ecotoxicity
Stream
Stream
Discharge to
aquatic habitats
Free Product
Dissolved plume
Leaching
Drinking Water
Vapor
Intrusion
Soil
Residential
Commercial
Industrial
Risk based on average daily exposure to low concentrations of contaminants over many years (chronic risk);
Requires collection of sample data representative of assumed exposure.
Air
Risk Assessment Basics (Training Series Part 6)
Notes: Also referred to as “Exposure Pathways.” Other potential problems include uptake of contaminants in plants or animals used for food.

## Slide 9: Assessment of Chronic Health Risk (similar for air, water, soil, food, etc.)
The concentration term in the (chronic risk) intake equation is an estimate of the arithmetic average concentration for a contaminant (in a defined, exposure area) based on a set of site sampling results.
USEPA 1992: A Supplemental Guidance to RAGS: Calculating the Concentration Term
=
Cancer/Noncancer
Risk
Ave Exposure
Concentration
x
Exposure
Factors
x
Toxicity
Simplified Risk Equation:

## Slide 10
RBSL = Allowable, average contaminant concentration for targeted area & volume of soil;
Key part of 1990s Risk-Based Corrective Action (RBCA);
Significantly expedites risk assessment process;
Problem: Lack of guidance for equivalent, “Risk-Based Site Characterization.”
Calculation of Risk-Based Screening Levels
(similar for air, water, soil, food, etc.)
=
Risk-Based
Screening Level
Acceptable Risk
Exposure
Factors
x
Toxicity
Simplified RBSL Equation:

## Slide 11
Ideal: Risk as well as potential remediation questions and needs to be considered upfront in site characterization design;
Reality: Risk assessors and remediation specialists often get stuck with inadequate, after-the-fact data and no time or money to collect additional samples.
Incorporation of Risk in Site Investigations
(HDOH Training Series Part 1)
Every Spot?
Each Playground?
The Entire Park?
What are the primary environmental concerns?
What are the Site Investigation Objectives (aka “DQOs”)?
What data resolution is needed to meet the SIOs?
How can representative samples be collected?

## Slide 12
“When there is little distance between points it is expected that there will be little variability between points.”
USEPA 1989: Methods for Evaluating the Attainment of Cleanup Standards
“The… level is assumed to be uniform within (a contaminated area) and zero outside it.”
USEPA 1985: Verification of PCB Spill Cleanup
Are “Discrete" Soil Samples “Representative”?
If true:
A few samples collected from single points across site under investigation adequate to characterize contamination and assess risk;
Allows direct comparison of individual, discrete samples to risk-based screening levels.

## Slide 13
“How’s that working for you?”
“Highly variable” data and failed confirmation samples
Remediated sites later found to still be contaminated
Need for multiple remobilizations and “step-out” investigations

## Slide 14
Every wonder...
Soil samples cannot be reliably “homogenized” to the scale of a laboratory subsample (1-30g);
Discrete sample data can only be assumed to represent the actual mass of soil tested.
Metals:
0.5-1.0 grams
VOCs:
5 grams
PCBs, Pesticides, TPH, PAHs:
10-30 grams
“What if I moved my sample point over a few feet?
“What if the lab tested a different aliquot of soil?”

## Slide 15
So did we… Discrete Soil Sample Variability Field Study
Study Site A
(arsenic in wastewater)
Study Site B
(lead in incinerator ash)
Study Site C
(PCBs transformer oil)
1,500 ft2 area
13,500 ft2 area
6,000 ft2 area
Three known-contaminated sites studied;
24 grid points designated at each site;
Hundreds of discrete samples collected;
Multi Increment samples (triplicates) collected from same areas.

## Slide 16
Metals
(1g)
PCBs
(10g)
Metals: Portable XRF analysis in lab;
PCBs: Discrete sample split into ten subsamples for individual analysis.
Evaluation of Intra-Sample Variability
(variability within single sample)
Single discrete sample tested ten times
3 feet

## Slide 17
3 feet
Samples “MIS (ISM)” processed for testing (dried, sieved and subsampled);
Data assumed representative of sample.
Five “co-located” discrete samples tested at each grid point
Evaluation of Inter-Sample Variability
(variability between co-located samples)

## Slide 18: Field Study Results
Roger Brewer, John Peard & Marvin Heskett (2017)
A critical review of discrete soil sample reliability:
Part 1 – Field study results
Part 2—Implications
Journal of Soil and Sediment Contamination.
Part 1: DOI: 10.1080/15320383.2017.1244172
http://dx.doi.org/10.1080/15320383.2017.1244171
Part 2: DOI: 10.1080/15320383.2017.1244172 http://dx.doi.org/10.1080/15320383.2017.1244172
2015 Field report and recorded webinars posted to HEER webpage
http://eha-web.doh.hawaii.gov/eha-cma/Leaders/HEER/Webinar

## Slide 19
“Low” Intra-Sample Variability at Arsenic Study Site
(arsenic-contaminated wastewater, fine-grained soils)
172 mg/kg
196mg/kg
199 mg/kg
204 mg/kg
141 mg/kg
161 mg/kg
165 mg/kg
165 mg/kg
169 mg/kg
172 mg/kg
Average Max:Min = 1.5X
Maximum Max:Min = 2.5X
Grid Pt #2
Variability within a single sample
Intra-Sample Variability

## Slide 20
“Low” Inter-Sample Variability at Arsenic Study Site
(arsenic-contaminated wastewater, fine-grained soils)
140
mg/kg
120 mg/kg
230
mg/kg
260
mg/kg
120
mg/kg
Grid Pt #2
Variability between co-located samples
Inter-Sample Variability
3 feet
Average Max:Min = 1.4X
Maximum Max:Min = 2.2X

## Slide 21
244 mg/kg
269 mg/kg
225 mg/kg
234 mg/kg
176 mg/kg
219 mg/kg
222 mg/kg
224 mg/kg
231mg/kg
232 mg/kg
Average Max:Min = 4X
Maximum Max:Min = 15X
Hawai’i Lead EAL = 200 mg/kg
Grid Pt #1
3 feet
Variability within a single sample
Intra-Sample Variability
“Moderate” Intra-Sample Variability at Lead Study Site
(lead-contaminated ash in fill soil)

## Slide 22
120 mg/kg
290 mg/kg
300
mg/kg
220
mg/kg
150 mg/kg
3 feet
Grid Pt #1
Average Max:Min = 2X
Maximum Max:Min = 7X
Hawai’i Lead EAL = 200 mg/kg
Inter-Sample Variability
“Moderate” Inter-Sample Variability at Lead Study Site
(lead-contaminated ash in fill soil)
Variability between co-located samples

## Slide 23
“High” Intra-Sample Variability at PCB Study Site
(waste electric oil dumped on bare soil)
2,700 mg/kg
3,100 mg/kg
3,200 mg/kg
5,700 mg/kg
810 mg/kg
910 mg/kg
1,000 mg/kg
1,400 mg/kg
2,600 mg/kg
2,700 mg/kg
Grid Pt #24
Average Max:Min = 17X
Maximum Max:Min = 116X
Average = 2,400 mg/kg
Intra-Sample Variability

## Slide 24
4.9 mg/kg
7.7 mg/kg
6.0 mg/kg
91 mg/kg
14 mg/kg
3 feet
Average Max:Min = 11X
Maximum Max:Min = 490X
2,400! mg/kg
Grid Pt #24
Inter-Sample Variability
“High” Inter-Sample Variability at PCB Study Site
(waste electric oil dumped on bare soil)

## Slide 25
Concentration #1
(whole sample)
2mm
1mm
1cm
PCB-Infused Tar Balls and “Distributional Heterogeneity”
The Myth of “Maximum” Contaminant Concentrations in Soil
Reported concentration varies with volume/mass of soil tested;
Maximum concentration always either
0 % (absent) or 100% (present);
Risk-based objective is always the mean for a specified sample/area/volume of soil.
Concentration #2
(single nugget)
Concentration #3
(PCB matrix)
10s ppm
1,000s ppm
10,000s ppm

## Slide 26
Particles with High Loadings are Called “Nuggets” (“nugget effect”)
Arsenic (whitish color) sorbed to iron hydroxide particles
“the iron in a cubic yard of soil [1-1.5 tons] is capable of adsorbing 0.5 to 5 lbs of soluble metals …or organics” (Vance 1994).
Photo courtesy of Roger Brewer, HDOH
Contaminants adsorbed to distinct particles form “nuggets” of high concentration
ITRC, ISM-1, Section 2.2 hyperlinks
Notes: Speaker Notes
Particulate iron minerals, such as oxides, are very good at binding contaminants.
One researcher stated that the Fe in a cubic yard of soil can adsorb ½ to 5 lbs of soluble metals or organics.
The photomicrograph shows microscopic iron hydroxide grains coated with arsenic. The arsenic appears as a light-colored deposit covering Fe-OH grains (see red arrow).
Silicate minerals make up most of the soil mass in the photo. Arsenic does not adsorb to those minerals, so they are dark gray.
Photo provided by Roger Brewer with the Hawaii Dept. of Health
Supplemental Information
See ISM-1 Section 2.2 hyperlinks
--------------------------------------------------------
Quote from the journal article: “Given the average concentration in soil, the iron in a cubic yard of soil is capable of adsorbing from 0.5 to 5 pounds of soluble metals as cations, anionic complexes, or a similar amount of organic[s].” (Vance, 1994). [Reference = David B. Vance. “Iron – The Environmental Impact of a Universal Element,” National Environmental Journal, May/June. 1994 Vol.4 No. 3 page 24-25. see also URL = http://2the4.net/iron.htm]

## Slide 27
Conclusion: Discrete sample data are random within a (largely) unknown range…
Total Discrete Sample Variability

## Slide 28
Think About the Implications…
You take the red pill – you stay in Wonderland and (find out) how deep the rabbit hole goes.
Morpheus (starting Neo on his journey in The Matrix )
Five Stages of Grief:
Denial Anger Bargaining Depression Acceptance
ITRC ISM 2012

## Slide 29
“Failed” confirmation samples…;
Need for repeat investigations with no clear endpoint…, etc.
Problem can’t be fixed by collecting more discrete samples;
Problem can’t be fixed by statistical evaluation of discrete sample data.
Lab data not reliably representative of sample;
Sample not reliably represented of area where it was collected.

## Slide 30
165
Fake, Discrete “Hot Spot” & “Cold Spot” Patterns
>800 mg/kg
>400 mg/kg
>200 mg/kg
<200 mg/kg
Study Site B (lead): Random lead concentration assigned within estimated range for grid point
Grid Pt #21
103-419 mg/kg
401
Notes: Isolated “hot spots” and “cold spots” are an artificial reflection of small-scale, random heterogeneity.

## Slide 31
Which Lead Pattern is “Real”? (Hint: None…)
(results of area-wide DU-MIS investigation)
Entire, 10-acre property is contaminated with lead;
False negatives would be quickly reached (50/50 chance);
Unavoidable, premature termination of initial site investigation;
Failed confirmation samples and/or premature termination of cleanup efforts.
Study Area C
10 acres

## Slide 32: Large-Scale Patterns Can Be Real
Field XRF and tight grid of discrete samples used to identify spill area;
Large-scale patterns likely real;
Zone B marked by small, likely artificial “hot spots” and “cold spots”;
Removal of isolated “hot spots” in Zone B will not significantly reduce risk.
Field discrete samples
9 acres
For example only
C
Discrete Sample Range below Screening Level
Discrete Sample Range Above Screening Level
A
Discrete Sample Range overlaps Screening Level
B
B
Isolated
“Hot Spots”
Notes: Structures removed. No obvious spill areas observable in the field.

## Slide 33
A Simple Problem…
Discrete Soil Samples are too SMALL to overcome
small-scale, distributional heterogeneity
Metals:
0.5-1.0 grams
VOCs:
5 grams
PCBs, Pesticides, Dioxins, TPH, PAHs:
10-30 grams
Discrete Sample Data Only Represent Mass Tested

## Slide 34
What Soil Contamination Would
Look Like if You Could Actually See It
Jackson Pollock
splatter painting
Spilled milk following low areas
Can’t be reliably characterized using discrete samples
Discrete Samples
(actual size)

## Slide 35
The so-called grab sample is not really a sample but a specimen of the material that may or may not be representative of the sampling unit (DU). Great care must be exercised when interpreting the meaning of these samples.
USEPA 1992, Preparation of Soil Sampling Protocols
Multiple Early Warnings
About Discrete Sample Data Unreliability…
(refer to Part 2 and supplement to Brewer et al. 2017)

## Slide 36
Risk Assessors Got it Right (almost…)
Discrete sample data can be highly variable within a targeted area;
Mean (true) concentration used to calculate risk or compare to risk-based screening levels.
Targeted Exposure Area
Front Yard Exposure Area:
Area: 400 ft2
Depth: 4”

## Slide 37
Ideal: 1) Excavate and send the entire volume of exposure area soil to lab for testing; 2) Use data to assess risk.
Entire mass of soil extracted by laboratory;
Single concentration of contaminant “X” reported;
Represents the “true” mean;
Not practical…
Targeted Exposure Area

## Slide 38
Alternative: 1) Collect 10+ discrete samples; 3) Test each sample individually; 4) Use statistical test to estimate mean.
Problems:
Risk assessors not involved in sampling design;
10+ samples rarely available for single area (“use maximum”);
High laboratory analytical costs;
Representativeness of sample set and estimated mean unknown;
Statistical analysis only evaluates the precision of the statistical test employed to estimate a mean for the data provided.
Targeted Exposure Area

## Slide 39
Study Site | Range 95% UCL (mg/kg) | Range RSD
*Site A (arsenic) | 403 to 776 | 34% to 67%
*Site B (lead) | 201 to 439 | 20% to 86%
Site C (PCBs) | 9.4 to >1,000,000 | 124% to 315%
Are Discrete Sample Data 95% UCLs “Real”?
Estimation of Mean Based on Multiple Sets of “Replicate” Discrete Sample Data (10 samples, 20 iterations)
Concentration within predicted range for 10 randomly picked grid points used to estimate mean;
Estimated mean is random within an unknown range;
Representativeness of single, 10-sample data sets unknown.
*XRF data (not directly comparable to MIS 6010B data)

## Slide 40
Study Site | Range 95% UCL (mg/kg) | Range RSD
*Site A (arsenic) | 395 to 492 | 39% to 54%
*Site B (lead) | 280 to 394 | 49% to 80%
Site C (PCBs) | 652 to 8,884 | 251% to 434%
Concentration within predicted range for full suite of 24 grid points used to estimate mean;
Estimated means more consistent for Sites A & B;
Consistency does not equal accuracy;
Representativeness of 24-sample data sets unknown.
Are Discrete Sample Data 95% UCLs “Real”?
Estimation of Mean Based on Multiple Sets of “Replicate” Discrete Sample Data (24 grid points, 20 iterations)
*Discrete sample XRF data (not directly comparable to MI Sample 6010B data)

## Slide 41
Better Approach: 1) Combine all “samples” into a single, bulk sample; 2) Process thoroughly; 3) Report ONE concentration.
Large, single sample collected from multiple points (“increments”) within defined “Decision Unit” area (“Multi Increment” sample);
Sample carefully processed and subsampled for testing;
Replaces need for statistical analysis of individual, discrete samples;
??? How many increments should the final, MI sample include?
??? What is the minimum, required mass of the final, MI sample?
Targeted Exposure Area
Targeted Exposure Area

## Slide 42
Gy’s Sampling Theory for “Infinite Particle” Media
and the Collection of Representative Soil Sample
(Training Series Part 3)
Considerations for Representative Samples:
Sample Mass;
Sample Increments;
Sample Collection;
Sample Processing & Subsampling;
Subsample Analysis (least error);
Bottom Line: 1-2kg sample, 50-increments for <2mm soil and ppm data resolution.
Variables:
Particle size/shape/density
Desired concentration resolution, etc.
Acceptable total error (FE)
Used in mining and agriculture industries since 1950s.

## Slide 43: Sampling Theory Training Courses
Envirostat, Inc.: Chuck Ramsey (www.envirostat.org)
Four-day, detailed introduction to sampling theory and Multi Increment Sample site investigations;
Francis Pitard Sampling Consultants, LLC: Francis Pitard (www.fpscsampling.com)
Advanced statistical sampling concepts with a focus on optimization of sampling protocols and mining exploration.

## Slide 44
Gy’s Sampling Theory Explained with a Salad
(DU-MIS Training Series Part 3)
Primary Concern: Long-term, chronic exposure to tomatoes
(assume salad eaten over a lifetime)
Wrong Questions:
What is the maximum concentration of tomato in this salad?
What is the concentration of tomato at point “X”?
Right Question:
What is the mean/true concentration of tomato in this salad?

## Slide 45
DU-1
DU-2
DU-3
Suspect Spill Area
A
B
C
Assume ahead of time that salad will likely fail for tomatoes;
One Multi Increment Sample collected from each DU area (e.g., 50 pts);
“Triplicate” samples collected in DU-2 to test data precision (three total).
Gy’s Sampling Theory Explained with a Salad
(DU-MIS Training Series Part 3)
Option 1: Test entire salad as a single Decision Unit;
Option 2: Divide salad into smaller Decision Units based on suspect “spill areas”, suspect clean areas, etc.
Sample representative of targeted area

## Slide 46: Laboratory Processing and Subsampling -Repeat Method Used in Field-
Sample spread out into thin layer;
Subsample collected in systematic random method for testing (minimum mass required by sampling theory);
Subsample representative of original sample;
Compare replicates to test precision.
Aliquot
Tested
by Lab

## Slide 47
Sample air dried and sieved (preserved in methanol for VOCs);
30-50+ increment subsample collected for analysis;
Minimum 10g subsample for <2mm particles;
Collect laboratory replicates to test subsampling precision;
Labs have been recommending this for decades but not pushed by regulators (plus added cost).
Soil Sample Processing and Subsampling
(DU-MIS Training Series Part 4)
40
Laboratory data representative of sample submitted
Notes: Evenly distribute prepped materials onto a tray covered with Aluminum foil, butcher paper or other inert cover. The sample layer should have a depth similar to the depth of the rectangular scoop that will be used for sampling.
For inorganic metals digestion, use a smaller scoop to sub-sample an aliquot size of 10g or more and store in a pre-cleaned container. For organic extraction, use a rectangular metal scoop to obtain an aliquot size of at least 30g in a pre-cleaned container.
Perform the sub-sampling by taking random scoops from the sample on the tray. The scoop should be taken evenly from the top to the bottom of the soil. A stratified random approach should be used. Each scoop must represent approximately 1/30th of the desired target mass of 0.33g or 1 g respectively. Practice on a few scoops before proceeding on the entire sample by measuring the weight of one scoop of soil. This may be done less frequently with knowledge of the type of soil. Once the desired amount is achieved, take scoops to represent the entire area of the tray in a random fashion. Record the final weight, which should be at least 10 or 30g. If the final amount is less than the required amount, take a few more scoops. If the amount is much greater than the desired amount, it may be necessary to recombine the sub-sample and start over.

## Slide 48
Study Site Multi Increment Sample Data
Triplicate 50- to 60-increment MI samples collected from each study area (1-2+ kg);
Processed and subsampled in accordance with Gy’s sampling theory.
Study Site A
(arsenic in wastewater)
Study Site B
(lead in incinerator ash)
Study Site C
(PCBs transformer oil)

## Slide 49
Study Site | MIS Data (average of triplicates) | 
 | (mg/kg) | RSD
*Site A (arsenic) | 233 | 6.5%
*Site B (lead) | 287 | 20%
Site C (PCBs) | 104 | 138%
MI Sample Data for Study Sites
RSD Interpretation | 
<35% | Good precision
>35% to <50% | Moderate precision (discuss errors)
>50% to <100% | Poor precision (consider 95% UCL)
>100% | Very poor precision (consider retesting)
*Method 6010B data (not directly comparable to discrete XRF data)

## Slide 50
Discrete vs Multi Increment Sample Data
-Sample Support-
Sampling Method | Number of DU Points | Total Mass of Soil Represented (grams) | Total Number of Analyses
Discrete Sample Data (24): | 24 | 24 (240) | 24
MI Sample Data (Triplicates): | 180 | 4,500+ | 3
Multi Increment data provide far better sample support.

## Slide 51: Are Discrete Sample Data Ever Useful? (Yes!)
Initial identification of contaminants of potential concern;
Initial estimate of risk;
Initial removal of large areas of contaminated;
Designation of DUs for MI sample confirmation;
Always confirm initial conclusions with DU-MIS data.
DU-1
DU-2
DU-3
DU-4
DU-5
DU-6
DU-7
DUs 8-17
Example arsenic site

## Slide 52
Front Yard:
Area: 400 ft2
Depth: 4”
But what about “acute” risk?
Risk Question:
Does the concentration of “X” in any (potential) discrete soil sample collected from the yard exceed “Y” mg/kg? (hypothetical acute toxicity)
Sampling Considerations:
Total Soil Mass: 1,800 kg
Discrete Sample Mass: 100g
Lab Aliquot Mass: 1g (metals)
Unanswerable Question (in terms of cost and field feasibility):
1,800,000 potential 1 gram “samples” (laboratory aliquot);
9,000,000 potential 200 mg “samples” (default child soil ingestion rate);
180,000 potential 10 gram “samples” (pica child ingestion rate);
Minimum 59 samples to attain 95% confidence that 95% of untested “samples” do not exceed maximum level reported;
Testing for acute risk with a reasonable degree of uncertainty is not practical;
Acute toxicity factors not available for most chemicals;
If a real concern then remove or cap suspect soil.

## Slide 53: It’s All About the Decision Units (Training Series Part 1,2)
DU = An area and volume of soil you would send to the laboratory as a single sample for testing, if you could;
Set DUs to size adequate for decision making (minimize retesting)!
Exposure Area DUs
Spill Area DUs
Boundary DUs

## Slide 54
Field Collection of MI Samples
(Training Series Part 4)
Site preparation
DU demarcation
Soil type vs sampling tools
Surface soils
Subsurface soils
Excavations
Stockpiles
Sediment
Sampling for VOCs
Equipment decontamination
Notes: Kea`au Middle School garden

## Slide 55
Where to Start???
Start with ONE DU
Not acceptable for redevelopment or remediation (too large);
Progressively subdivide site into smaller DUs until all site investigation objectives will be met.
Hypothetical Industrial Complex Redevelopment
100m
Is the 50-acre area as a whole contaminated above risk-based screening levels?

## Slide 56
Subdivide Site Based on Past Use
Industrial Operations
Residential Housing
Office Buildings
100m
Site subdivided into three areas based on historical land use;
Testing of former office building area as a single, Exposure Area DU might be acceptable (assumed clean);
Further subdivision of housing and industrial operations areas required.
Are the individual, past use areas as a whole impacted above screening levels?

## Slide 57
Subdivide Based on Age of Housing and
Individual Factory Areas
WH-1
WH-2
WH-3
WH-4
WH-5
OB-1
FA-1
FA-2
FA-3
FA-4
FA-5
100m
Four housing areas defined (based on construction time) and five factory areas defined (based on past operations);
Still too large to designate as exposure area DUs and assess risk;
Factory areas known to be heavily contaminated (optimize remediation).
Are the individual neighborhoods and factory areas impacted above screening levels?
Multiple Chemicals
Lead Paint, Termiticides?

## Slide 58
Worker Housing: What’s Your Question?
Test fraction of building lots in each neighborhood;
Assume present at all buildings within neighborhood if identified and manage soil appropriately (i.e., assume entire neighborhood contaminated).
WH-1
WH-3
WH-5
OB-1
FA-1
FA-2
FA-3
FA-4
FA-5
100m
WH-4
WH-2
Were termiticides or lead-based paint used at worker housing buildings?
Lead Paint, Termiticides?

## Slide 59
Worker Housing: What’s Your Question?
Half-acre areas designated as Exposure Area DUs (e.g., risk-based resolution of data required for redevelopment by overseeing regulatory agency).
Entire former worker housing area ultimately tested (total 36 DUs).
WH-1
WH-3
WH-5
OB-1
FA-1
FA-2
FA-3
FA-4
FA-5
100m
WH-4
WH-2
Do half-acre DU areas within the former worker housing areas exceed screening levels?
Lead Paint, Termiticides?

## Slide 60
Individual Factory Areas: Remediation Required
Designate DUs based on known/suspect spills, tanks, dumps, storage areas, assumed clean areas, etc.;
Small DUs used to isolate contaminated soil and optimize remediation;
Max DU size = default, ½ acre exposure area (agency required resolution);
Concurrent testing of surface and subsurface soils DUs;
Data use to prepare remedial action plan.

## Slide 61
Entire site subdivided and tested based on needs for risk assessment and optimization of remedial actions;
Minimized need for retesting after one or two mobilizations for sample collection;
Initial soil removal confirmed with DU-MIS data;
Requires more time upfront but expedites reliable completion of project.
Complex Sites – But a Clear End Point

## Slide 62
Baseline Investigation:
Isolate and separately test suspected localized areas of heavy contamination;
Divide field into large DUs based on past crop history, pesticide use, soil type, topography, development plans, etc.;
MI sample collected in each DU (10% triplicates);
Requires walk through of entire site;
Use to select primary COPCs;
Evaluate large-scale buildup of pesticides;
Worth proceeding for redevelopment?
Lot-Scale Investigation:
Test 59+ random, hypothetical, one-acre lots.
“Did you test my yard?”
“No but we tested your neighborhood and a random number of lots.”
DU-MIS for Very Large Areas (former ag field being redeveloped for homes)
Notes: Here’s an example of neighborhood-size decision units across a 400-acre former ag land site being considered for residential housing.
Advantages to screening at the neighborhood scale:
-Walk entire area (identify additional brownfield areas - dumps, abandoned buildings, etc.)
-Narrow down list of target contaminants for yard-scale investigation. Only test for initial contaminants of potential concern if detected during screening level investigation.
-Answer the question: “Did you test my yard? No, but we tested your neighborhood and a random selection of lots.”

## Slide 63: Hawaii’s Transition from Discretes to DU-MIS (2005-2009)
  Completed Projects:
  Retesting of past, completed investigations not required;
  Some properties being retested as part of new property transactions.
  Currently Active Projects:
  Existing discrete sample can be used for initial remedial actions;
  DU-MIS data required for confirmation.
  New Projects:
  Discrete sample data sometimes used for screening and DU designation (e.g., metals and portable XRF);
  DU-MIS data normally used to complete investigation and design final remedial actions;
  DU-MIS data required for confirmation.

## Slide 64
Questions?
Wrong Question: “When are DU-MIS methods applicable?”
Right Question: “Knowing what we now know, when are discrete sampling methods still acceptable?”
NOT Just Another Tool in the Tool Box…
Discrete Sample
Investigation Methods
DU-MIS
Investigation Methods
It’s an entirely NEW and IMPROVED set of tools.