## Slide 1
TPH and the Assessment of Petroleum Risk
Roger Brewer (Hawaii DOH, roger.brewer@doh.Hawaii.gov)
WRRC, University of Hawai′i
April 1, 2022

## Slide 2
  BTEX(MN): Benzene, Toluene, Ethylbenzene and Xylenes +/- naphthalene and methylnaphthalenes
  PAHs: Polyaromatic Hydrocarbons (e.g., naphthalene, benzo(a)pyrene;
  TPH: Total Petroleum Hydrocarbon – Remaining mixture of non-specific hydrocarbons and (for now) hydrocarbon-related degradation compounds;
  HOPs (new): Hydrocarbon Oxidation Products. Assumed to have the same toxicity as the parent hydrocarbons.
  Action Level: Concentration of a contaminant in a media at or below which no adverse health or other environmental affects are anticipated.
  Risk Driver: Compound(s) in a mixture that poses the greatest risk to human health and the environment (e.g., would still exceed an action level when action levels for all other compounds are met).
Terminology

## Slide 3
1. TPH is only useful as a qualitative screening tool.
TPH and hydrocarbon-related degradation compounds often dominant contamination and must be quantitatively evaluated as part of an environmental hazard evaluation (risk assessment).
2. Methods are not available to quantitatively assess risk posed by TPH compounds.
  TPH risk can be quantitatively assessed in the same manner as individual chemicals like BTEX and PAHs (available since the 1990s).
3. TPH only needs to be considered if benzene and other individually targeted compounds are not detected.
  The TPH component of petroleum can still pose a risk when concentrations of BTEX and PAHs meet target risks or action/screening levels.
  4. Pre-approved TPH Environmental Action Levels are not necessary.
  Efficient assessment of 100s of thousands of release sites requires pre-approved action levels.
Petroleum Risk Misconceptions

## Slide 4
Hawai’i DOH TPH References
Above Refs: https://health.hawaii.gov/heer/guidance/ehe-and-eals/
HDOH Recorded Webinars: https://health.hawaii.gov/heer/guidance/heer-webinars/
Risk-Based TPH Action/Screening Levels (similar to CalEPA ESLs):
HIDOH, 2017, Evaluation of Environmental Hazards at Sites with Contaminated Soil and Groundwater (Fall 2017): Hawai’i Department of Health, Office of Hazard Evaluation and Emergency Response.
TPH Risk Case Studies:
HIDOH, 2018, Collection and Use of Total Petroleum Hydrocarbon Data for the Risk-Based Evaluation of Petroleum Releases - Example Case Studies: Hawaii Department of Health, Hazard Evaluation and Emergency Response Office. August 2018.
Chemistry & Toxicity of Petroleum Vapors:
HIDOH, 2012, Field Investigation of the Chemistry and Toxicity of TPH in Petroleum Vapors: Implications for Potential Vapor Intrusion Hazards: Hawai‘i Department of Health, Office of Hazard Evaluation and Emergency Response
Brewer et al. 2014. Risk-Based Evaluation of Total Petroleum Hydrocarbons in Vapor Intrusion Studies: International Journal of Environmental Research and Public Health, Volume 10, pp 2441-2467.

## Slide 5
Other TPH References
TPHCWG, 1997. Analysis of Petroleum Hydrocarbons in Environmental Media: Total Petroleum Hydrocarbon Criteria Working Groun
MADEP, 1997. Characterizing Risks Posed by Petroleum Contaminated Sites: Implementation of the MADEP VPH/EPH Approach: Massachusetts Department of Environmental Protection,
MADEP, 2003, Updated Petroleum Hydrocarbon Fraction Toxicity Values for the VPH/EPH/EPH Methodology/
WADOE, 2006, Cleanup Levels and Risk Calculations Focus Sheets: Reference Doses for Petroleum Mixtures; Washington Department of Ecology.
USEPA, 2009. Provisional Peer-Reviewed Toxicity Values for Complex Mixtures of Aliphatic and Aromatic Hydrocarbons;
CAEPA, 2016, Petroleum Metabolites Literature Review and Assessment Framework: California Environmental Protection Agency, San Francisco Bay Regional Water Quality Control Board, June 27, 2016.
ITRC, 2018, TPH Risk Evaluation at Petroleum Contaminated Sites.

## Slide 6
Outline
  Environmental Hazard Evaluation basics.
  What is petroleum made of?
  What is “TPH” and how are toxicity and risk evaluated?
  How do individual TPH components partition released to the environment?
  What drives risk – TPH (& HOPs) or BTEXN?
  How are TPH and HOPs tested for?
  Questions

## Slide 7
1. Direct
Exposure
Groundwater
Prevailing Wind
Direction
Leaching
7. Gross
Contamination
2. Ecotoxicity
Stream
Stream
6. Discharge to
aquatic habitats
Free Product
Dissolved plume
5. Drinking Water
3. Vapor
Intrusion
Soil
4. Leaching
Commercial
Industrial
Residential
Potential Environmental Concerns Posed by Contaminated Soil and Groundwater
Notes: Also referred to as “Exposure Pathways.” Other potential problems include uptake of contaminants in plants or animals used for food.

## Slide 8
Environmental Hazard Evaluation and
Environmental Action (Screening) Levels
(aka “risk assessment”)
Separate Models and Approaches:
Direct exposure;
Vapor intrusion;
Leaching;
Gross contamination;
Ecotoxicity (site-specific).
Example Information Needs:
Toxicity Factors;
Physiochemical Constants;
Exposure Assumptions;
Soil and groundwater properties.

## Slide 9: Benzene Risk-Based Action Levels (residential setting, HDOH 2017)
Aquatic Habitats
71 µg/L
Terrestrial
Habitats
(site specific)
Leaching: 0.30 mg/kg
INDOOR AIR
SOIL GAS
Gross Cont.
170 µg/L
Gross Cont. 500 mg/kg
Vapor Intrusion 0.77 mg/kg
Human Health
Drinking Water
5 µg/L
Human Health
Direct Exposure
1.2 mg/kg
SOIL
GROUNDWATER
Vapor Intrusion
2,300 µg/L
0.36 µg/m3
720 µg/m3

## Slide 10: Toxicity Factors and Risk-Based Action Levels
Chemical | 1Chronic Toxicity Factor (maximum long-term safe dose) | 3Health Effect
Water | a few gallons/day (adult) | Acute Hyponatremia
Aspirin | 81 mg/day (“minitabs”) | Gastro-intestinal affects
2Barium | 3 mg/day (Two 1mm grains/day) | Multiple noncancer
2Arsenic | 0.0045 mg/day (One 1mm grain/two years) | Multiple noncancer
1. For example only. Average daily exposure over many years (“chronic”) that is predicted to not result in an adverse health effect. Varies with route of exposure, target cancer risk and noncancer hazard, child vs adult, etc. Exceedance warrants further evaluation.
2. Examples reflect daily exposure of children (BW 15kg) and noncancer hazard.
3. Must consider cumulative routes of exposure, other sources, similar contaminants, etc.
Silver Maximum Daily Dose = 75 µg/day
Child Water Consumption = 0.78 L/day
Drinking Water Action Level = 96 µg/L
Toxicity
Risk
Assessment
Notes: Point: All chemicals potentially toxic at some dose.
Acute = Health effects instant to within three months.
Chronic = Long-term exposure (30 years).
Maximum Daily Dose without noncancer health effects via ingestion (varies wrt to route of exposure)
Potential unacceptable chronic health risk (noncancer) when maximum daily dose is exceeded (based on toxicity studies).
Cancer risks also estimated in a similar manner.
1mm diameter sphere weight (density = 1) =

## Slide 11
 |  | Toxicity | 
 |  | Low | High
Dose | Low | No Risk | Low Risk
 | Med | Low Risk | High Risk
 | High | High Risk | Acute Risk
A high dose of low-toxicity compound (e.g., barium) can pose a greater health risk than a low dose of a high-toxicity compound (e.g., arsenic)
Risk = Toxicity x Dose
Dose = Concentration x Exposure
“Dose makes the poison”
Notes: Exposure to a high concentration of an otherwise low-toxicity chemical can pose an equal or even greater health risk than exposure to a very low concentration of a highly toxic chemical.

## Slide 12: HDOH 2017 Site Investigation and “Environmental Hazard Assessment” Webinar Series
Part 1: Systematic Planning and Site Investigation Design (TGM Section 3)
Part 2: Decision Unit Designation (TGM Section 3)
Part 3: Sampling Theory & DU Characterization (TGM Section 4)
Part 4: Field Implementation of DU-MIS Methods (TGM Sections 5 & 8)
Part 5: Laboratory Processing of MI Samples (TGM Section 4)
Part 6: Environmental Hazard Evaluation (TGM Section 13).
HEER Technical Guidance Manual Webinars:
https://health.hawaii.gov/heer/guidance/heer-webinars/

## Slide 13
Outline
  Environmental Hazard Evaluation basics.
  What is petroleum made of?
  What is “TPH” and how are toxicity and risk evaluated?
  How do individual TPH components partition released to the environment?
  What drives risk – TPH (& HOPs) or BTEXN?
  How are TPH and HOPs tested for?
  Questions

## Slide 14
Laboratory Reporting of TPH
Labs run three different tests to estimate the total concentration of TPH in a sample (e.g., gas chromatography Method 8105M;
A single fuel can overlap several ranges (e.g., kerosenes, diesels)
The sum of the individual ranges represents the Total TPH for the tested sample (e.g., Total TPH = GRO + DRO + RRO);
Compare total the TPH action level specific to that fuel type;
Individually targeted compounds can be subtracted.
C5-C12
C12-C24
C24-C40+
“Residual Range”
Compounds
(RRO/TPHo)
ITRC 2018
“Gasoline Range”
Compounds
(GRO/TPHg)
“Diesel Range”
Compounds
(DRO/TPHd)
Retention Time (boiling point, molecular weight, etc.)
Response
BTEX
PAHs
Heavy Oil, Tar

## Slide 15
Chart: Gasoline (CAEPA LUFT)
| Total BTEXN: | Total Carbon Ranges:
 | 0.22574 | 0.77426
Varies
Fuel dominated by other 100s of other compounds collectively referred to as “Total Petroleum Hydrocarbon (TPH)”
Analytical Technologies, lnc.
Fuel Reference Library
Gasoline Fuel Chromatogram
C10
C12
C16
C8
More Volatile
?
GRO
DRO

## Slide 16
Chart: JP-5 Fuel (DoD Fuel Specs)
| Total BTEXMN: | Total Carbon Ranges:
Total BTEXMN: Total Carbon Ranges: | 0.112 | 0.888
Kerosene Fuel (e.g., JP-5) Chromatogram
Varies
Lower BTEXMN in newer formulations
Analytical Technologies, lnc.
Fuel Reference Library
More Volatile
?
C10
C12
C16
C8
More Volatile
GRO
DRO

## Slide 17
Chart: Diesel Fuel (CAEPA LUFT)
| Total BTEXN: | Total Carbon Ranges:
Total BTEXN: Total Carbon Ranges: | 0.0106 | 0.9917
Diesel Fuel Chromatogram
Varies
Analytical Technologies, lnc.
Fuel Reference Library
More Volatile
?
C10
C12
C16
C8
More Volatile
GRO
DRO

## Slide 18: Useful Moments of Enlightenment! No BTEX = No Risk?
Non BTEX-PAH “TPH” related gasoline vapors also likely posed vapor intrusion toxicity risks to indoor air for future buildings.
Former Gas Station (1990s)
Flammable Gasoline Vapors In Soil
After Passing a BTEX-PAH Risk Assessment

## Slide 19
Outline
  Environmental Hazard Evaluation basics.
  What is petroleum made of?
  What is “TPH” and how are toxicity and risk evaluated?
  How do individual TPH components partition released to the environment?
  What drives risk – TPH (& HOPs) or BTEXN?
  How are TPH and HOPs tested for?
  Questions

## Slide 20
Toxicity of Total Petroleum Hydrocarbons
TPH Working Group (mid/late 1990s)
Additional TPH Toxicity Reviews
Massachusetts DEP (1997+)
ATSDR (1999)
Washington DOE (2006)
California EPA (DTSC 2009)
USEPA (2009)

## Slide 21
TPH = Sum of Aromatics + Aliphatics (excluding BTEX & PAHs)
Risk-Based TPH Aliphatic and Aromatic “Carbon Ranges”
>EC8-12
>EC10-22
>C18-36
>EC12-18
Potential Vapor Phase
C2
C4
C6
C8
C12
C16
C20
C24
C28
C32
C36
C0
>EC8 -10
Gasolines
Middle Distillates
Fuel Oils
Aliphatics
Aromatics
hexane
benzene
EC5-8
EC = Effective Carbon. Related to the boiling point & MW (TPHCWB 1997)
Notes: Benzene (6): EC 6.5
Toluene (7): EC 7.6
Ethylbenzene (8): EC 8.5
Xylenes (8): EC 8.6
Naphthalene (10): EC 11.7
2-Methylnaphthalene (11): EC12.84
1-Methylnaphthalene (11): EC 12.99

## Slide 22
Equivalent Carbon Range Group | MW | VP (atms) | Solubility (µg/L) | H’ | koc (cm3/g) | Diffusion Coefficient (cm2/s) | 
 |  |  |  |  |  | air | water
EC5-8 Aliphatics | 93 | 0.1 | 11,000 | 54 | 2,265 | 0.08 | 1 x 10-5
>EC8-12 Aliphatics | 149 | 8.7 x 10-4 | 70 | 65 | 150,000 | 0.07 | 1 x 10-5
>EC12-18 Aliphatics | 170 | 1.4 x 10-4 | 10 | 69 | 680,000 | 0.07 | 5.0 x 10-6
>EC18-36 Aliphatics | 280 | 1.1 x 10-6 | 0.0000015 | 110 | 4.0 x 10-8 | - | -
>EC8-C10 Aromatics | 120 | 2.9 x 10-3 | 51,000 | 0.33 | 1,778 | 0.07 | 1 x 10-5
>EC10-22 Aromatics | 150 | 3.2 x 10-5 | 5,800 | 0.03 | 5,000 | 0.06 | 1 x 10-5
Carbon Range Physiochemical Constants
HIDOH 2017; after MADEP 2002

## Slide 23
Chemical/ Carbon Range | Oral RfD (mg/kg-day) | Inhalation RfC (µg/m3)
EC5-EC8 Aliphatics | 0.04 | 600
>EC8-EC18 Aliphatics | 0.01 | 100
>EC18-EC36 Aliphatics | 3.0 | na
>EC8 Aromatics | 0.03 | 100
Carbon Range *Toxicity Factors
(HDOH 2017; after MADEP 2002, USEPA 2009)
*Dermal absorption toxicity factors calculated separately.

## Slide 24
Partitioning of Petroleum in the Environment
*Theoretical ratio of vapor-phase mass to dissolved-phase mass at equilibrium. Vapor-phase dominates if H’ >1.0.
Aromatics Prefer to be in the Water
Aliphatics Prefer to be in the Vapors
Chemical/ Carbon Range | Solubility | *Henry’s Constant
EC5-8 Aliphatics | 11,000 | 54
>EC8-12 Aliphatics | 70 | 65
>EC12-18 Aliphatics | 10 | 69
>EC18-36 Aliphatics | 0.0000015 | 110
>EC8-C10 Aromatics | 51,000 | 0.33
>EC10-22 Aromatics | 5,800 | 0.03
Benzene | 1,780 | 0.23
Toluene | 526 | 0.27
Ethylbenzene | 169 | 0.32
Xylenes | 178 | 0.29
Naphthalene | 31 | 0.018
Conc. Gas
Conc. Water

## Slide 25
TPH Carbon Range Composition vs Exposure Pathway
(carbon range makeup can vary with specific fuel formulation)
Chart: 
| BTEXN: | TPH:
BTEXN: TPH: | 0.04 | 0.96
 | 0.08 | 0.92
Air
(mostly aliphatics)
Chart: 
| BTEXN: | TPH:
 | 0.08 | 0.92
Chart: 
| BTEXN: | TPH:
BTEXN: TPH: | 0.06 | 0.94
 | 0.08 | 0.92
GASOLINE
DIESEL
TPH
TPH
TPH
Chart: 
| Total BTEXMN: | Total Carbon Ranges:
Total BTEXMN (Old): Total BTEXMN (New): Total Carbon Ranges: | 0.09 | 0.02 | 0.888
Soil
(fuel - depleted
over time)
Chart: 
| Total BTEXN: | Total Carbon Ranges:
Total BTEXN: Total Carbon Ranges: | 0.0106 | 0.9917
Chart: 
| Total BTEXN: | Total Carbon Ranges:
 | 0.22574 | 0.77426
TPH
TPH
TPH
TPH
Chart: 
| Total BTEXMN: | Total Carbon Ranges:
Total BTEXMN (Old): Total BTEXMN (New): Total Carbon Ranges: | 0.69 | 0.1 | 0.20521
Water
(mostly aromatics)
Chart: 
| Total BTEXN | Total Carbon Ranges
Total BTEXN Total Carbon Ranges | 0.79479 | 0.20521
Chart: 
| Total BTEXN | Total Carbon Ranges
 | 0.84369 | 0.15631
BTEXN
TPH
TPH
TPH
?
BTEXN
(old)
(new)
?
TPH or
BTEXN
?
?
TPH or
BTEXN
Kerosene

## Slide 26
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.25339 | 0.73785 | 0.0087646
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0.61166 | 0.1707 | 0 | 0.21764
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
13% 76% 0.0% 10% | 0.13336 | 0.76457 | 0 | 0.10208
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0 | 0.78653 | 0 | 0.21347
Carbon Range Makeup of TPH in Fuel, Vapors & Water
(For example only; -DOH EALs to be updated in 2022)
Fuel
(published/
measured)
>C8-C18 Aliphatics
C5-C8
Aliphatics
>C8
Aromatics
Vapors
(measured)
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.9877 | 0.0083358 | 0.0039637
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.66598 | 0.32787 | 0.0061475
Dissolved
(measured?)
GASOLINE
DIESEL
?
?
?
JP-8
Kerosene
JP-5
No C5-C8
Aliphatics?
(CAEPA LUFT 2015)
(CAEPA LUFT 2015)
(DoD 1990s Fuel Spec)

## Slide 27
Layer of fresh fuel placed on water (gasoline, diesel, JP-5, JP-8)
Allowed to equilibrate for 20 days;
Water tested for BTEX, PAH and carbon range makeup of dissolved-phase hydrocarbons;
Weighted toxicity factors calculated for mixture;
To be used to develop toxicity-based action levels (e.g., drinking water);
Labs could not reliable separate aliphatic vs aromatic carbon ranges.
HIDOH Dissolved-Phased Petroleum Study
(2019-2021)
Fuel
Air
Water

## Slide 28
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.25339 | 0.73785 | 0.0087646
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0.61166 | 0.1707 | 0 | 0.21764
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
13% 76% 0.0% 10% | 0.13336 | 0.76457 | 0 | 0.10208
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0 | 0.78653 | 0 | 0.21347
Fuel
(published)
>C8-C18 Aliphatics
C5-C8
Aliphatics
>C8
Aromatics
Vapors
(measured)
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.9877 | 0.0083358 | 0.0039637
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.66598 | 0.32787 | 0.0061475
Aliphatics in vapors?
Dissolved
(modeled)
Chart: 
| 0 | 0 | 0 | 0
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0.58336 | 0.0016859 | 0 | 0.41495
Chart: 
| 0 | 0 | 0 | 0
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0.11403 | 0.010387 | 0 | 0.87558
Chart: 
| 0 | 0 | 0 | 0
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0 | 0.011223 | 0 | 0.98878
?
Varies with fuel
GASOLINE
DIESEL
?
?
?
JP-5
JP-8
Kerosene
Varies Between
Sites
Carbon Range Makeup of TPH in Fuel, Vapors & Water
(For example only; -DOH EALs to be updated in 2022)
(CAEPA LUFT 2015)
(CAEPA LUFT 2015)
(DoD 1990s Fuel Spec)

## Slide 29: Carbon Range Based Action Levels? Possible but not practical… (cost-benefit, lab limitations, degraded mixtures, etc.)
Aquatic Habitats
___ µg/L
Terrestrial
Habitats
(site specific)
Leaching: ___ mg/kg
INDOOR AIR
SOIL GAS
Gross Cont.
___ µg/L
Vapor Intrusion ___ mg/kg
Human Health
Drinking Water
___ µg/L
Human Health
Direct Exposure
___ mg/kg
GROUNDWATER
Vapor Intrusion ___mg/L
___ µg/m3
___mg/m3
Gross Cont. ___ mg/kg
SOIL

## Slide 30
Weighted Toxicity of Cookies and TPH Mixtures
(Defined Range of Possible Weighted Calories or Toxicity Factors)
Total Calories (weighted toxicity) Calculated Based on Recipe and calories per mass for individual ingredients;
Possible Caloric Range:
Highest = Pure chocolate (most toxic)
Lowest = Pure flour (least toxic)
Ingredients
Weighted Toxicity
(Harmonic Mean)
Benzene
Toluene
Ethylbenzene
Xylenes
Naphthalene
EC5-8 Aliphatics
>EC8 -18 Aliphatics
>EC18 Aliphatics
>EC8 Aromatics
Ingredients
v
v
v
v

## Slide 31
General Approach (fuel, air, water):
HIDOH, 2017, Evaluation of Environmental Hazards at Sites with Contaminated Soil and Groundwater (Fall 2017): Hawai’i Department of Health, Office of Hazard Evaluation and Emergency Response.
Updated Tapwater Approach (interim draft):
HIDOH, 2022, Recommended Risk-Based Drinking Water Action Levels for Total Petroleum Hydrocarbons (TPH) Associated with Releases of JP-5 Jet Fuel: internal Technical Memorandum to Kathy Ho from Roger Brewer, Hawai’i Department of Health, Office of Hazard Evaluation and Emergency Response, February 12, 2022.
References – Calculation of Weighted Toxicity Factors

## Slide 32
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.25339 | 0.73785 | 0.0087646
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0.61166 | 0.1707 | 0 | 0.21764
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
13% 76% 0.0% 10% | 0.13336 | 0.76457 | 0 | 0.10208
Chart: 
| C5-C8 Aliphatics | >C8-C18 Aliphatics | >C18-C32 Aliphatics | >C8 Aromatics
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0 | 0.78653 | 0 | 0.21347
Calculation of Weighted TPH Toxicity Factors Based on Carbon Range Makeup (DRAFT examples only; to be updated in 2022)
Fuel
(published)
>C8-C18 Aliphatics
C5-C8
Aliphatics
>C8
Aromatics
Vapors
(measured)
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.9877 | 0.0083358 | 0.0039637
Chart: 
| C5-8 Aliphatics: | C9-12 Aliphatics: | C9-10 Aromatics:
 | 0.66598 | 0.32787 | 0.0061475
+ Dremal RfDs
Dissolved
(modeled)
Chart: 
| 0 | 0 | 0 | 0
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0.58336 | 0.0016859 | 0 | 0.41495
Chart: 
| 0 | 0 | 0 | 0
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0.11403 | 0.010387 | 0 | 0.87558
Chart: 
| 0 | 0 | 0 | 0
C5-C8 Aliphatics >C8-C18 Aliphatics >C18-C32 Aliphatics >C8 Aromatics | 0 | 0.011223 | 0 | 0.98878
?
Varies with fuel
GASOLINE
DIESEL
?
?
RfC = 281 µg/m3
RfC = 225 µg/m3
RfC = 126 µg/m3
RfDo = 0.025 mg/kg-day
RfDo = 0.012 mg/kg-day
RfDo = 0.012 mg/kg-day
RfDo = 0.035
RfDd = 0.072
RfC = 195
RfDo = 0.030
RfDd = 0.034
RfC = 111
RfDo = 0.029
RfDd = 0.030
RfC = 100
?
JP-5
JP-8
Kerosene
Varies Between
Sites

## Slide 33: Example TPHmd Action Levels (HIDOH 2017, *DW action levels under revision)
Aquatic Habitats
640 µg/L
Terrestrial
Habitats
(site specific)
Leaching: 940 mg/kg
INDOOR AIR
SOIL GAS
Gross Cont.
500? µg/L
Gross Cont. 500 mg/kg
Vapor Intrusion (use soil gas)
Human Health
*Drinking Water
400 µg/L
Human Health
Direct Exposure
220 mg/kg
SOIL
GROUNDWATER
Vapor Intrusion (use soil gas)
130 µg/m3
260,000 mg/m3

## Slide 34
Outline
  Environmental Hazard Evaluation basics.
  What is petroleum made of?
  What is “TPH” and how are toxicity and risk evaluated?
  How do individual TPH components partition released to the environment?
  What drives risk – TPH (& HOPs) or BTEXN?
  How are TPH and HOPs tested for?
  Questions

## Slide 35
Fuel Type | 1Soil Action Level (mg/kg)
Benzene | 0.30
TPH (gasoline fuels) | 100
TPH (diesel fuels) | 220
TPH (residual fuels) | 500
*Carbon Range-Weighted TPH Action Levels for Soil
(HIDOH 2017)
1TPH action levels based on noncancer Hazard Quotient of 1.0. Benzene action level based on 10-6 cancer risk.
TPH Action Level Exceeded When Benzene
<0.30 mg/kg?

## Slide 36
TPH vs BTEXN as Fuel Risk Driver
(exposure to fuel in soil)
Data Source | Site/Fuel Type | TPH Drives Risk | *BTEXN Drives Risk
Field Studies | Gasoline | (X) | X?
 | Kerosene | X | -
 | Diesel | X | -
“X” Drives risk if 10-6 cancer risk applied to benzene (0.36 µg/m3).
“(X)” Drives risk if 10-5 cancer risk applied to benzene (3.6 µg/m3).
Point: TPH almost ways drives risk for middle distillate releases and can for gasoline releases if a 10-5 cancer risk is used to screen benzene.

## Slide 37
 |  | Toxicity | 
 |  | Low | High
Dose | Low | No Risk | Low Risk
 | Med | Low Risk | High Risk
 | High | High Risk | Acute Risk
Risk = Toxicity x Dose
Dose = Concentration x Exposure
“Dose makes the poison”
TPH
BTEX-PAHs
TPH as the “risk driver”
Notes: Exposure to a high concentration of an otherwise low-toxicity chemical can pose an equal or even greater health risk than exposure to a very low concentration of a highly toxic chemical.

## Slide 38
*Carbon Range-Weighted TPH Action Levels for Air
(HIDOH 2017; Brewer et al 2014)
*Carbon range makeup varies between fuels and between sites. Site-specific data recommended for calculation of weighted toxicity factors and action levels.
Fuel Type | 1Air Action Level (µg/m3)
Benzene | 0.36
TPH (gasoline fuels) | 290
TPH (kerosene fuels) | 230
TPH (diesel fuels) | 130
1TPH action levels based on noncancer Hazard Quotient of 1.0. Benzene action level based on 10-6 cancer risk.
TPH Action Level Exceeded When Benzene
<0.36 µg/m3?

## Slide 39
TPH vs Benzene as Indoor Air Risk Driver
(based on field data in Brewer et al. 2014)
Data Source | Site/Fuel Type | TPH Drives Risk | *BTEXN Drives Risk
Vapors From Fresh Fuel | Gasoline | (X) | X
 | Diesel (varies) | (X) | X?
 | JP-8 (varies) | (X) | X?
Field Studies Aged Releases | USEPA Gasoline Vapor Database | (X) | X?
 | Site C (JP-8) | X (X) | 
 | Site E (diesel) | X (X) | 
“X” Drives risk if 10-6 cancer risk applied to benzene (0.36 µg/m3).
“(X)” Drives risk if 10-5 cancer risk applied to benzene (3.6 µg/m3).
Point: TPH almost ways drives risk for middle distillate releases and can for gasoline releases if a 10-5 cancer risk is used to screen benzene.

## Slide 40
1. For example only (pending review and finalization).
2. USEPA-HIDOH drinking water MCL (10-5 cancer risk).
3. DRAFT-Based on carbon range makeup presented in CAEPA LUFT Manual (2015).
4. DRAFT-Based on carbon range makeup for JP-5 implied in 1990s Military Spec (HIDOH 2022; likely overestimates BTEXN in current fuels).
1Example Carbon Range-Weighted TPH Action Levels
for Tapwater: Fresh (volatile) Plumes
Fuel Type | 1Tapwater Action Level (µg/L)
2Benzene | 5.0
3TPH (gasoline fuels) | 339
4TPH (kerosene fuels) | 211
3TPH (diesel fuels) | 189
1TPH action levels based on noncancer Hazard Quotient of 1.0. Benzene action level based on 10-6 cancer risk.
TPH Action Level Exceeded When Benzene
<5.0 µg/L?

## Slide 41
TPH vs BTEXN as Tapwater Risk Driver
Data Source | Site/Fuel Type | TPH Drives Risk | *BTEXN Drives Risk
*Fresh (volatile) Plumes | Gasoline |  | X
 | Kerosene | X? | X?
 | Diesel | X? | X?
Point: TPH almost ways drives risk for middle distillate releases and can for gasoline releases if a 10-5 cancer risk is used to screen benzene.
*Hydrocarbons in most plumes of contaminated water are at least partially degraded by the time testing takes place.

## Slide 42
Weighted Toxicity of HOPs Mixtures in Water
(mixture of degraded TPH & BTEXN)
Chart: 
| BTEXN: | TPH:
BTEXN: TPH: | 0.04 | 0.96
 | 0.08 | 0.92
Air
(mostly aliphatics)
Chart: 
| BTEXN: | TPH:
 | 0.08 | 0.92
Chart: 
| BTEXN: | TPH:
BTEXN: TPH: | 0.06 | 0.94
 | 0.08 | 0.92
GASOLINE
JP-5
DIESEL
TPH
TPH
TPH
Chart: 
| Total BTEXMN: | Total Carbon Ranges:
Total BTEXMN (Old): Total BTEXMN (New): Total Carbon Ranges: | 0.09 | 0.02 | 0.888
Soil
(fuel depleted
over time)
Chart: 
| Total BTEXN: | Total Carbon Ranges:
Total BTEXN: Total Carbon Ranges: | 0.0106 | 0.9917
Chart: 
| Total BTEXN: | Total Carbon Ranges:
 | 0.22574 | 0.77426
TPH
TPH
TPH
TPH
Chart: 
| Total BTEXMN: | Total Carbon Ranges:
Total BTEXMN (Old): Total BTEXMN (New): Total Carbon Ranges: | 0.69 | 0.1 | 0.20521
Water
(mostly aromatics)
Chart: 
| Total BTEXN | Total Carbon Ranges
Total BTEXN Total Carbon Ranges | 0.79479 | 0.20521
Chart: 
| Total BTEXN | Total Carbon Ranges
 | 0.84369 | 0.15631
BTEXN
TPH
TPH
TPH
?
BTEXN
(old)
(new)
?
TPH or
BTEXN
?
?
TPH or
BTEXN

## Slide 43
Chemistry and Toxicity of
Degraded of Petroleum in Water (HIDOH 2018)
BTEXN
TPH
HOPs
Polar acids/esters, alcohols, ketones, phenols
Reported as “TPH” in absence of silica gel cleanup
Hydrocarbon Oxidation Products
(new term)
Better Test Methods Needed
“It is the mark of an instructed mind to rest easy with the level of precision that the decision requires, and not to try an exactness that is unnecessary for the problem.”
Aristotle (paraphrased)

## Slide 44
1Example Carbon Range +BTEXN Weighted HOPs Action Levels for Tapwater – Degraded (non-volatile) Plumes
Fuel Type | 1Tapwater Action Level (µg/L)
2Benzene | 5.0
3TPH (gasoline fuels) | 190
4TPH (kerosene fuels) | 447
3TPH (diesel fuels) | 232
1TPH action levels based on noncancer Hazard Quotient of 1.0. Benzene action level based on 10-6 cancer risk.
1. For example only (pending review and finalization).
2. USEPA-HIDOH drinking water MCL (10-5 cancer risk).
3. DRAFT-Based on CR + BTEXN makeup presented in CAEPA LUFT Manual (2015).
4. DRAFT-Based on CR + BTEXN makeup for JP-5 implied in 1990s Military Spec (HIDOH 2022; likely overestimates proportion of lower-toxicity xylenes in current fuels and underestimates weighted toxicity of degraded mixture).
Includes degraded benzene
Includes degraded xylenes

## Slide 45
TPH vs BTEXN as Tapwater Risk Driver
Data Source | Site/Fuel Type | TPH/HOPs Drives Risk | *BTEXN Drives Risk
Fresh (volatile) Plumes | Gasoline |  | X
 | Kerosene | X? | X?
 | Diesel | X? | X?
*Degraded (non-volatile) Plumes | Gasoline | X | 
 | Kerosene | X | 
 | Diesel | X | 
Point: TPH and/or HOPs almost always risk for middle distillate releases and can for gasoline releases if a 10-5 cancer risk is applied to benzene.
*Hydrocarbons in most plumes of contaminated water are at least partially degraded by the time testing takes place.

## Slide 46
Outline
  Environmental Hazard Evaluation basics.
  What is petroleum made of?
  What is “TPH” and how are toxicity and risk evaluated?
  How do individual TPH components partition released to the environment?
  What drives risk – TPH (& HOPs) or BTEXN?
  How are TPH and HOPs tested for?
  Questions

## Slide 47
Laboratory Measurement of “TPH” and “HOPs”
TPH Action Levels apply to the total concentration of TPH-related compounds in the mixture (e.g., gasolines, middle distillates, residual fuels, etc.)
Lab would ideally identify the fuel type and report a single concentration for both TPH and HOPs combined (initial screening);
Site-specific carbon range data and action levels can be useful for vapor intrusion investigations (e.g., TPH as sum of C5-12);
Better test methods are needed for both total TPH and total HOPs.
C5-C12
C12-C24
C24-C40+
Total TPH for Sample =
“Gasoline Range” + “Diesel Range” + “Residual Range”
ITRC 2018

## Slide 48
No BTEX-PAHs does not mean No Risk.
Methods are available to assess risk posed by TPH compounds.
TPH always needs to be considered even if benzene and other individually targeted compounds are detected.
TPH-related compounds often drive risk at petroleum-release sites (i.e., TPH compounds can still pose a risk even if concentrations of BTEX and PAHs meet action levels.
Better test methods are needed for both TPH and HOPs.
Carbon range data and site-specific action levels are primarily useful for testing of parent fuel associated with large, fresh releases and testing of indoor air and/or soil gas associated with middle distillate fuels.
Site-specific action levels are allowed but will fall within a narrow range of possibilities.
Summary

## Slide 49
“There are... problems yet to be identified because they only show up after we've learned... to even ask such questions. That's what excites me about the entire, moving frontier of science."
Neil deGrasse Tyson
Decision
Making
Risk
Assessment
Sample
Collection
Laboratory
Analysis
Questions, Comments, Ideas???

## Slide 50
Compound | Fuel/Soil (F&T) | Water (Toxicity) | Vapors (Toxicity)
Benzene | X | X | X
Toluene | X | X | X
Ethylbenzene | X | X | X
Xylenes (total) | X | X | X
Naphthalene | X | X | X
C5-C6 Aliphatics | X | X | X
>C6-C8 Aliphatics | X |  | 
>C8-C10 Aliphatics | X | X | X
>C10-C12 Aliphatics | X |  | 
>C12-C16 Aliphatics | X |  | 
>C16-C18 Aliphatics | X |  | 
>C18-C32 Aliphatics | X | X | 
>C8-C10 Aromatics | X | X | X
>C10-C12 Aromatics | X |  | 
>C12-C16 Aromatics | X |  | 
>C16-C21 Aromatics | X |  | 
>C21-C32 Aromatics | X |  | 
Other targeted compounds, additives, degradation products, etc. |  |  | 
Example Analyses for Site-Specific Studies
Notes: More detailed summary of carbon ranges needed for site-specific testing of fuels and soils in order to predict fate and transport. Testing of water and vapors based primarily on toxicity groupings.

## Slide 51
Petroleum HOPs Toxicity References
1. Zemo et al., 2016, Life Cycle of Petroleum Biodegradation Metabolite Plumes, and Implications for Risk Management at Fuel Release Sites. Integrated Environmental Assessment and Management. DOI: 10.1002/ieam.1848 (based on field studies of fuel degradation in groundwater)
2. HIDOH, 2018, Collection and Use of Total Petroleum Hydrocarbon Data for the Risk-Based Evaluation of Petroleum Releases - Example Case Studies: Hawaii Department of Health, Hazard Evaluation and Emergency Response Office. August 2018. (see Attachment 5: Example Calculation of Metabolite Suite-Weighted, Risk-Based Screening Levels for Tapwater).

## Slide 52
“Metabolite” Tapwater Toxicity in ITRC Case Studies
Roger Brewer, Hawaii Dept of Health
ITRC TPH Risk Team, September 19, 2017
(TPH Risk Case Studies Part 2 https://health.hawaii.gov/heer/guidance/heer-webinars/)
Study #1: Fuel Terminal
Study #2: Gas Station
Study #3: Oil Pipeline
Study #4: Tanker Truck
Study #5: Oil Field

## Slide 53
Similar Weighted Mixture Toxicity Approach Can (in Theory) be Applied to TPH-Related Metabolites in Drinking Water (Case Studies Attachment 5)
Step 1: Designate Metabolite Families and Assign Toxicity Factors
Step 2: Estimate Metabolite Family Makeup of Degraded TPH
Step 3: Calculate Metabolite Suite-Weighted Toxicity Factors
Step 4: Calculate Metabolite Suite-Weighted Screening Levels

## Slide 54
Metabolite Family | Toxicity Ranking | Estimated Range Ingestion RfD (mg/kg-day) | 
 |  | Low | High
Alcohols | Low | 0.1 | 1.0
Acids/Esters | Low | 0.1 | 1.0
*Ketones | Low/Low-Mod | 0.01 | 1.0
Aldehydes | Low to Mod | 0.01 | 0.1
*Phenols | Low/Mod | 0.001 | 1.0
Toxicity Ranking of TPH-Related Metabolites
(Zemo et al. 2016)
Step 1: Metabolite Families & Toxicity Factors
*Estimated toxicity of ketone and phenol mixtures varies between degradation stages.
Oxidized hydrocarbons assumed not significantly volatile;
Focus on ingestion and dermal route of exposure for tapwater.

## Slide 55
Step 2: Degradation Stages vs Metabolite Family Makeup
Transport Direction and/or Increasing Residence Time
Stage 1:
Source Area (dissolved HC + metabolites)
Stage 2:
Smear Zone
(metabolites only, no dissolved HC)
Stage 3:
Transition Zone
(ave Stages 2 & 4)
Stage 4:
Downgradient
(metabolites only and outside of smear zone)
Degradation Stages (Zemo et al. 2016)
Dissolved TPH & BTEXN hydrocarbons in Stage 1 must be evaluated separately and cumulative risk posed by metabolites + hydrocarbons assessed.

## Slide 56
Stage 1
Stage 2
Stage 3
Stage 4
Step 2: Degradation Stage vs Metabolite Makeup
(Zemo et al. 2016)
Phenols
Aldehydes
Ketones
Acids/Esters
Alcohols
Decreasing Toxicity

## Slide 57
Step 3: Metabolite Suite-Weighted Toxicity Factors
*Weighted toxicity of metabolite mixture based on lowest (most conservative) toxicity for individual metabolite families presented in Zemo et al. 2016.
Degradation Stage | Estimated *Weighted Oral RfD (mg/kg-d) (dissolved metabolite mixture) | 
 | Low | High
Stage 1 | 0.02 | 0.20
Stage 2 | 0.04 | 0.37
Stage 3 | 0.05 | 0.55
Stage 4 | 0.07 | 0.69
Fuel Type | Estimated *Weighted Oral RfD (mg/kg-d) (dissolved CR+BTEXN mixture)
Gasoline | 0.035
Kerosene | 0.030
Diesel | 0.029
HIDOH 2018 (after Zemo et al. 2016):
This Presentation:

## Slide 58
Example Drinking Water Screening Levels
for TPH-Related Metabolites
(after Zemo et al. 2016; most conservative toxicity factors applied)
Transport Direction and/or Increasing Residence Time
Stage 1:
*Source Area (+dissolved HC)
<420 µg/L
Stage 2:
Smear Zone
(metabolites only)
<740 µg/L
Stage 3:
Transition Zone
(ave Stages 2 & 4)
<1,100 µg/L
Stage 4:
Downgradient
(metabolites only)
<1,400 µg/L
*Non-degraded, TPH hydrocarbons must be evaluated separately and cumulative risk considered.
Dermal absorption not considered.
Accuracy of toxicity factors?
Taste & Odor Threshold?

## Slide 59
Summary
Weighed carbon range approach to calculate TPH screening levels for drinking water in use for 15+ years;
Similar approach possible for TPH-related degradation compounds (HOPs) in drinking water;
Focus on ingestion & dermal exposure pathway (assumed low volatility);
Most conservative toxicity factors for Degradation Stage 1 & 2 metabolite suites would generate tapwater action levels similar to TPH parent compounds;
Higher action levels potentially applicable to Stage 3 & 4 metabolite suites, assuming proposed toxicity factors appropriate;
Within or above range of likely “TPH” taste and odor threshold levels?