## Slide 1
Field Study of Perfluoroalkyl Substances (PFASs)
In WWTP Influent, Effluent and Biosolids
- Preliminary Data from Hawaii -
Roger Brewer, Senior Environmental Scientist
Dr Diana Felton, State Toxicologist
Hawaii Department of Health
September 22, 2022
USEPA FSTRAC
Influent
Effluent
Biosolids
Crop Irrigation
Drinking Water
Aquatic Habitats
Direct Exposure
Leaching
Plant Update

## Slide 2
PFASs: Interim Soil and Water Environmental Action Levels (EALs) for Perfluoroalkyl and Polyfluoroalkyl Substances (PFASs), April 2021 (and updates): https://health.hawaii.gov/heer/guidance/additional-guidance-documents/
EALs Technical Background: Evaluation of Environmental Hazards at Sites with Contaminated Soil and Groundwater (EALs; HIDOH 2017):
https://health.hawaii.gov/heer/guidance/ehe-and-eals/
Sample Collection, Processing and Testing: Technical Guidance Manual (HIDOH 2021): https://health.hawaii.gov/heer/guidance/specific-topics/decision-unit-and-multi-increment-sampling-methods/
Other: ITRC 2020: Per- and Polyfluoroalkyl Substances (PFAS)
References
HIDOH PFAS Webpage:
https://health.hawaii.gov/heer/environmental-health/highlighted-projects/per-and-polyfluoroalkyl-substances-pfass/
HIDOH Recorded Webinars:
https://health.hawaii.gov/heer/guidance/heer-webinars/

## Slide 3
Wastewater Treatment Plant Study Sites
(samples collected from 3 of 8 WWTPs)
WWTP | 1Influent Rate | 2Biosolids Generation | Notes
A | 1.2 MGD | 30 tons/week | Residential/Commercial Fixed Film Biotower
B | 3.7 MGD | 150 tons/week | Residential/Commercial Secondary treatment design?
C | 2.8 MGD | 40 tons/week | Residential/Commercial Activated Sludge
Landfill leachate not disposed of at noted WWTPs.
Wet weight (average 85% water, density 0.95 tons/cyd).
20 tons
660,00 gal
Pending: Five WWTPs on O’ahu

## Slide 4
Study Objectives and Methods
(“A day in the life of a WWTP”)
Investigation Questions:
“What is the average makeup and concentration of PFAS in the influent, effluent and biosolids during a 24-hour period at the WWTP?”
“Are PFASs significantly leachable from the biosolids generated?”
Data Needs:
Mean concentration of PFASs in the volume of influent, effluent and biosolids generated over a 24-hour period;
Relative amount of PFAS sorbed to biosolids vs leached into solution.
Sample Collection Methods:
Water: 24-hour sampler;
Biosolids: Single, Multi Increment sample (30+ increment, 1-2 kg; air dried and MI subsampled; 5-10 gram subsample tested with added fee);
Laboratory: SGS AXYS Analytical Services.
24hr water sampler
Biosolids MI Sample

## Slide 5: “Decision Unit” & “Multi Increment Sample” Investigation Guidance (DU-MIS)
Six-Part DU-MIS Investigation Training Series;
Field study of discrete sample error;
DU-MIS case studies;
Recorded webinars; etc.
Hawaii DOH DU-MIS Webpage:
https://health.hawaii.gov/heer/guidance/specific-topics/decision-unit-and-multi-increment-sampling-methods/
HDOH, 2021, Technical Guidance Manual: Hawai‘i Department of Health, Office of Hazard Evaluation and Emergency Response, http://www.hawaiidoh.org/

## Slide 6
1Compound | CAS Number | 1Abbreviation
Perfluoro butane sulfonate | 45187-15-3 | PFBS-
Perfluoro hexane sulfonate | 108427-53-8 | PFHxS-
Perfluoro heptane sulfonate | 146689-46-5 | PFHpS-
Perfluoro octane sulfonate | 45298-90-6 | PFOS-
Perfluoro decane sulfonate | 126105-34-8 | PFDS-
Perfluoro butanoate | 45048-62-2 | PFBA-
Perfluoro pentanoate | 45167-47-3 | PFPeA-
Perfluoro hexanoate | 92612-52-7 | PFHxA-
Perfluoro heptanoate | 120885-29-2 | PFHpA-
Perfluoro octanoate | 45285-51-6 | PFOA-
Perfluoro nonanoate | 72007-68-2 | PFNA-
Perfluoro decanoate | 73829-36-4 | PFDA-
Perfluoro undecanoate | 196859-54-8 | PFUnDA-
Perfluoro dodecanoate | 171978-95-3 | PFDoDA-
Perfluoro tridecanoate | 862374-87-6 | PFTrDA-
Perfluoro tetradecanoate | 365971-87-5 | PFTeDA-
Perfluoro octane sulfonate | 45298-90-6 | PFOSA-
2,3,3,3-tetrafluoro-2-(heptafluoropropoxy) propanoate | 122499-17-6 | HFPO-DA-
18 Targeted PFASs with Toxicity Factors
and Physiochemical Constants (HIDOH 2021)
1. Anion form assumed found in the environment listed (affects predicted fate and transport).

## Slide 7
1,2Compound | CAS Number | 1Abbreviation
Perfluoro pentane sulfonate | 175905-36-9 | PFPeS-
6:2 Fluorotelomer sulfonate (ammonium salt) | 59587-39-2 | 6:2 FTS-
8:2 Fluorotelomer sulfonate (ammonium salt) | 149724-40-3 | 8:2 FTS-
N-Methyl-perfluoro octane sulfonamide | 31506-32-8 | N-MeFOSA-
2-(N-Methyl-perfluorooctane sulfonamido) acetate | 909405-48-7 | MeFOSAA-
N-ethyl perfluoro octane sulfonamido acetate | ? | EtFOSAA-
N-Methyl perfluoro octane sulfonamide ethanol | 24448-09-7 | N-MeFOSE-
N-Ethyl-N-(2-hydroxyethyl) perfluoro octane sulfonamide | 1691-99-2 | N-EtFOSE-
5:3 Fluorotelomer carboxylate | 1799325-94-2 | 5:3 FTCA-
7:3 Fluorotelomer carboxylate | ? | 7:3 FTCA-
Additional Detected PFASs without Toxicity
Factors and Physiochemical Constants
1. FTS- compounds: CAS for anionic ammonium salt form noted.
2. Check anion form name and CAS #s (incomplete).

## Slide 8
HDOH Groundwater Action Levels (April 2021)
(parts per trillion)
Compound | 1Drinking Water Toxicity (ng/L) | 2Chronic Aquatic Toxicity (ng/L)
PFBS- | 600 | 130,000,000
PFHxS- | 19 | 10,000
PFHpS- | 20 | -
PFOS- | 40 | 1,100
PFDS- | 20 | -
PFBA- | 7,600 | 830,000
PFPeA- | 800 | -
PFHxA- | 4,000 | 6,300,000
PFHpA- | 40 | -
PFOA- | 40 | 8,300
PFNA- | 4.0 | 8,0000
PFDA- | 4.0 | 10,000
PFUnDA- | 10 | 10,000
PFDoDA- | 13 | 20,000
PFTrDA- | 13 | -
PFTeDA- | 130 | -
PFOSA | 24 | -
HFPO-DA- | 160 | -
1. Assumes: Body Weight=15kg, Relative Source Contribution=0.2; HQ=0.5.
2. Drinking water action level used if aquatic toxicity level not available.

## Slide 9
HDOH Soil Action Levels (April 2021)
(parts per million)
Compound | 1Direct Exposure (mg/kg) | 2Leaching to Drinking Water Aquifer (mg/kg)
PFBS- | 0.38 | 0.003
PFHxS- | 0.012 | 0.002
PFHpS- | 0.013 | 0.004
PFOS- | 0.025 | 0.007
PFDS- | 0.013 | 0.013
PFBA- | 4.8 | 0.099
PFPeA- | 0.51 | 0.003
PFHxA- | 2.5 | 0.013
PFHpA- | 0.025 | 0.0003
PFOA- | 0.025 | 0.001
PFNA- | 0.003 | 0.0008
PFDA- | 0.003 | 0.0005
PFUnDA- | 0.006 | 0.005
PFDoDA- | 0.008 | (use lab test)
PFTrDA- | 0.008 | (use lab test)
PFTeDA- | 0.084 | (use lab test)
PFOSA | 0.015 | 50
HFPO-DA- | 0.10 | 0.0003
1. Noncancer hazard to young children (Body Weight=15kg, Relative Source Contribution=0.2; HQ=0.5).
2. Soil leaching action level calculated based on generic SESOIL model.

## Slide 10
Biosolids Leaching Tests
(samples required filtering of obtain dissolved-phase data)
1. Synthetic Precipitation Leaching Procedure (SPLP)
Requires reliable MI sample data;
SPLP solution does not directly represent leachate (data not directly comparable to screening levels);
Used to estimate sample-specific sorption coefficient (Kd);
Input Kd into equilibrium partitioning model to estimate leachate conc.
Column modified to accommodate MI samples;
Water pumped upwards through media;
Default SOP simulates two-years of infiltrating irrigation water (approx. 120 cm/yr);
Leachate solution data directly comparable to water screening level;
Collect entire volume of leachate and test as a single sample (+/- “first flush” sample?; vs default SOP nine sequential tests).
2. Soil Column
Leaching Test (modified LEAF 1314)
(murky leachate required filtering)

## Slide 11
SPLP Calculation of Sorption Coefficients (Kd)
HDOH, 2017, Use of laboratory batch tests to evaluate potential leaching of contaminants from soil (and updates): Hawai‘i Department of Health, Office of Hazard Evaluation and Emergency Response. https://health.hawaii.gov/heer/guidance/ehe-and-eals/
Not
Significantly
Mobile
Slight
Mod
High
Predicted Mobility in Soil Leachate
*Default
Kd
20
10
1
BaP: 587
Dioxin: 250
DDT, PCBs
Dieldrin
Diesel
MTBE, PCE,
Atrazine
SPLP: Measured Sorption Coefficient (Kd)
(Retardation Factor approaches 100 as Kd approaches 20)
Notes: Retardation Factor = 1+ (Media Bulk Density/Water-Filled Porosity) x Kd (Fetter 1993, Contaminant Hydrogeology)

## Slide 12
Chart: Influent
| 5:3 FTCA- | PFHxA- | PFBA- | PFOS- | PFOA- | Other
 | 0.40976 | 0.2107 | 0.097888 | 0.071329 | 0.070823 | 0.1395
Chart: Effluent
| 5:3 FTCA- | PFHxA- | PFOS- | PFPeA- | PFOA- | Other
 | 0.44885 | 0.21142 | 0.08946 | 0.077697 | 0.063767 | 0.10881
Chart: Biosolids
| 5:3 FTCA- | N-MeFOSE- | 7:3 FTCA- | PFOS- | N-EtFOSE- | Other
 | 0.26407 | 0.1492 | 0.13263 | 0.078865 | 0.073773 | 0.30146
Chart: SPLP Solution
| 5:3 FTCA- | 7:3 FTCA- | PFHxA- | PFPeA- | PFOS- | Other
 | 0.77135 | 0.11225 | 0.045927 | 0.015232 | 0.01431 | 0.040931
WWTP A
Effluent
Biosolids
Other: PFPeA-, 6:2 FTS-, PFHxS-, PFDA-, PFHpA-
Other: PFDA-, PFHxS-, PFBS-, PFHpA-,
MeFOSAA-
Other: MeFOSAA-, PFDS-, EtFOSAA-, PFDoA-, PFHxA-, PFDA-, PFTeDA-, PFTrDA-, PFUnA-, PFOSA-, PFOA-
Other: PFBA-, PFOA-, PFBS-, PFDA-, MeFOSAA-, PFHpA-, PFNA-, PFTrDA-, PFDoA-
Total PFAS: 32 ng/L
Total PFAS: 40 ng/L
Total PFAS:
84 µg/kg
Influent
Leachate
Preliminary Data
For Example Only
Red: Kd >20
(low mobility?)
(no leachate from landfills)

## Slide 13
Chart: Influent
| 5:3 FTCA- | PFHxA- | PFOA- | PFOS- | PFBA- | Other
 | 0.42297 | 0.23632 | 0.087905 | 0.070144 | 0.050124 | 0.13254
Chart: Effluent
| PFPeA- | PFHxA- | 6:2 FTS- | PFOA- | PFOS- | Other
 | 0.31809 | 0.2024 | 0.090924 | 0.082479 | 0.077412 | 0.22869
Chart: Biosolids
| 5:3 FTCA- | PFOS- | 7:3 FTCA- | N-MeFOSE- | MeFOSAA- | Other
 | 0.28585 | 0.13331 | 0.11408 | 0.09101 | 0.069585 | 0.30616
Chart: SPLP Solution
| 5:3 FTCA- | 7:3 FTCA- | PFHxA- | 6:2 FTS- | PFOA- | Other
 | 0.66898 | 0.14262 | 0.077118 | 0.038652 | 0.014611 | 0.058022
WWTP B
Effluent
Biosolids
Other: 6:2 FTS-, PFPeA-, PFDA-, PFHpA-, PFDoA-, PFNA-, PFHxS-
Other: PFBA-, PFBS-, PFHpA-, PFDA-, PFNA-, PFHxS-
Other: N-EtFOSE-, EtFOSAA-, PFDA-, PFDoA-, PFHxA-, PFDS-, 6:2 FTS-, PFTeDA-, PFUnA-, PFTrDA-, PFOA-, PFOSA-, PFBS-, N-MeFOSA-, PFNA-
Other: PFBA-, PFOS-, PFPeA-, PFBS-, PFHpA-, PFDA-, MeFOSAA-, PFHxS-, PFNA-, EtFOSAA-, PFDoA-, PFOSA-
Total PFAS: 36 ng/L
Total PFAS: 66 ng/L
Total PFAS: 182 µg/kg
Influent
Leachate
Red: Kd >20
(low mobility?)
Preliminary Data
For Example Only
FTCA MRL = 10 ng/L
(no leachate from landfills)

## Slide 14
Chart: Influent
| PFHxA- | PFOA- | PFBA- | PFBS- | PFPeA- | Other
 | 0.24893 | 0.14945 | 0.14585 | 0.14315 | 0.11164 | 0.20099
Chart: Biosolids
| 5:3 FTCA- | PFDA- | 7:3 FTCA- | PFOS- | PFDoA- | Other
 | 0.25705 | 0.16219 | 0.13384 | 0.087773 | 0.084365 | 0.27479
Chart: Effluent
| PFPeA- | PFHxA- | PFOA- | PFBS- | PFBA- | Other
 | 0.40184 | 0.34849 | 0.12332 | 0.036512 | 0.025288 | 0.064537
Chart: SPLP Solution
| 5:3 FTCA- | 7:3 FTCA- | PFPeA- | PFHxA- | PFOA- | Other
 | 0.56655 | 0.14941 | 0.073064 | 0.065205 | 0.056396 | 0.089379
Influent
Effluent
WWTP C
Biosolids
Leachate
Other: PFOS-, PFHxS-, PFDA-, PFNA-
Other: PFHpA-, PFOS-, PFDA-, PFHxS-, PFNA-
Other: PFOA-, PFPeA-, PFHxA-, MeFOSAA-, PFTeDA-, EtFOSAA-, PFBS-, PFUnA-, PFTrDA-, PFNA-, N-MeFOSA-, PFHpA-, PFOSA-
Other: PFBS-, PFBA-, PFDA-, PFOS-, PFHpA-, PFNA-, MeFOSAA-, 6:2 FTS-, PFDoA-, PFHxS-, EtFOSAA-, PFUnA-
Total PFAS: 144 ng/L
Total PFAS: 22 ng/L
Total PFAS: 122 µg/kg
Preliminary Data
For Example Only
FTCA MRL = 10 ng/L
Red: Kd >20
(low mobility?)
(no leachate from landfills)

## Slide 15
HIDOH Action Level Exceedances
(draft/preliminary)
WWTP | Water |  | Biosolids | 
 | 1Drinking Water | 1,2Aquatic Toxicity | 1,3Direct Exposure | 1,4Leaching to Groundwater
A | (none) | (none) | (none) | PFDA- (N-MeFOSE-, 5:3 FTCA-, 7:3 FTCA-)
B | (none) | (none) | PFDA- | PFBA-, PFOA-, PFDA-, PFOS- (MeFOSAA-, EtFOSAA-, N-MeFOSE-, N-EtFOSE-, 5:3 FTCA-, 7:3 FTCA-)
C | (none) | (none) | PFDA-, PFDoDA- | PFPeA-, PFHpA-, PFOA-, PFNA-, PFDA-, PFOS- (5:3 FTCA-, 7:3 FTCA-)
Action levels for assumed end point PFAS applied to precursors (not adjusted with respect to molecular weight; ok for direct exposure but not for leaching?).
Data compared to chronic aquatic toxicity action level.
Cumulative Hazard Index likely to be <1 (ignoring other PFAS sources).
Assumes groundwater is a source of drinking water. SPLP batch leaching test run on sample if leaching based soil action level exceeded.

## Slide 16
Chart: Measured Kd (cm3/g)
| 1722.0212765957447 | 6355.0000000000009 | 7168.2086167800453 | 4306.2411347517727 | 19838.156028368798 | 5795.6028368794323 | 805.2788104089218 | 189.40594059405939 | 1297.5675675675677 | 85.930807248764424 | 101.23385939741753 | 189.40594059405939 | 30.59808612440192 | 29.185098952270078 | 58.378378378378379
 | 110400 | 139800 | 51240 | 7553.4 | 2361.6 | 1615.2 | 673.2 | 635.4 | 434.4 | 109.2 | 45.6 | 25.8 | 18.6 | 13.8 | 12
KD=20
Preliminary Data
For Example Only
WWTP A: Biosolids Predicted vs Measured Kd and
Potential Leaching Risk (based on SPLP Batch Test Data)
Other Measured Kd:
5:3 FTCA = 31 cm3/g
7:3 FTCA = 157 cm3/g

## Slide 17
Chart: Measured Kd (cm3/g)
| 1262.7586206896556 | 6280.1145475372286 | 6739.8065556152605 | 2253.0241672109728 | 18144.0146878825 | 3155.7754800590837 | 874.4337811900192 | 315.96059113300504 | 1568.7850467289722 | 96.578483245149911 | 39.777424483306831 | 8.7145242070116868 | 7.7598450613298917 | 22.174940898345156 | 13.433734939759036
PFTrDA- PFTeDA- PFDoDA- PFOSA- PFDS- PFUnDA- PFHpS- PFOS- PFNA- PFDA- PFHxS- PFOA- PFBA- PFHpA- PFBS- PFPeA- PFHxA- HFPO-DA- | 110400 | 139800 | 51240 | 7553.4 | 2361.6 | 1615.2 | 738 | 673.2 | 635.4 | 434.4 | 337.2 | 109.2 | 45.6 | 25.8 | 18.6 | 13.8 | 12 | 7.2
KD=20
Mod
Leaching
Risk
Minimal Leaching Risk
Reduced Leaching Risk
Preliminary Data
For Example Only
Other Measured Kd:
5:3 FTCA = 19 cm3/g
7:3 FTCA = 51 cm3/g
WWTP B: Biosolids Predicted vs Measured Kd and
Potential Leaching Risk (based on SPLP Batch Test Data)

## Slide 18
Chart: Measured Kd (cm3/g)
| 110400 | 139800 | 51240 | 7553.4 | 2361.6 | 1615.2 | 738 | 673.19999999999993 | 635.4 | 434.4 | 337.2 | 109.2 | 45.6 | 25.8 | 18.599999999999998 | 13.799999999999999 | 12 | 7.1999999999999993
 | 7252.7273 | 3754.0113 | 7298.8406 | 2579.5086 | 3727.0726 | 631.6129 | 335.4913 | 879.5215 | 180 | 94.3951 | 20.1408 | 46.9444 | 32.6316 | 36.383 | 26.755
KD=20
Mod
Leaching
Risk
Minimal Leaching Risk
Reduced Leaching Risk
Preliminary Data
For Example Only
Other Measured Kd:
5:3 FTCA = 21 cm3/g
7:3 FTCA = 67 cm3/g
WWTP C: Biosolids Predicted vs Measured Kd and
Potential Leaching Risk (based on SPLP Batch Test Data)

## Slide 19
Summary (in progress)
Data for single day – longer-term studies needed;
Toxicity & physiochemical factors needed for precursor compounds (assume degradation to final PFAS form?);
PFAS makeup of influent variable between WWTPs;
Presence of 5:3 FTCA in influent not related to landfill leachate;
PFAS makeup of effluent reflects WWTP design?
PFAS drinking water action levels not exceeded in influent or effluent;
PFAS aquatic toxicity action levels not exceeded in influent or effluent;
PFAS makeup of biosolids similar;
PFASs in tested biosolids do not appear to pose a significant direct-exposure risk;
Most PFASs appear tightly bound to organic material and not significantly leachable? (Kd >20);
Shorter chain PFASs could be moderately leachable in some cases;
Contamination of groundwater from biosolids-amended fields due to PFASs in water content of biosolids (85% water)?
Further leaching studies planned using soil column tests.

## Slide 20
Additonal Slides

## Slide 21
High Toxicity
High Mobility
Low Toxicity
Low Mobility
Chart: PFASs Predicted Mobility vs Mobility
| PFTrDA- | PFTeDA- | PFDoDA- | PFOSA- | PFDS- | PFUnDA- | PFHpS- | PFOS- | PFNA- | PFDA- | PFHxS- | PFOA- | PFBA- | PFHpA- | PFBS- | PFPeA- | PFHxA- | HFPO-DA-

PFTrDA- PFTeDA- PFDoDA- PFOSA- PFDS- PFUnDA- PFHpS- PFOS- PFNA- PFDA- PFHxS- PFOA- PFBA- PFHpA- PFBS- PFPeA- PFHxA- HFPO-DA- | 6.6667e-06 | 6.6667e-05 | 6.6667e-06 | 1.2e-05 | 1e-05 | 5e-06 | 1e-05 | 2e-05 | 2.2e-06 | 2e-06 | 9.7e-06 | 2e-05 | 0.0038 | 2e-05 | 0.02 | 0.0004 | 0.002 | 8e-05
High
Med
Low
RfD (mg/kg-day)
Koc (cm3/g)
Increasing Toxicity
Increasing Mobility
<1.0E-05
<1.0E-03
Low Toxicity
High Mobility
High Toxicity
Low Mobility
Risk
Migration into Water & Uptake into Plants
Stuck in Soil and Sediment

## Slide 22
PFASs with Toxicity Factors
and Physiochemical Constants
HH Toxicity Factors (main) | Compounds (18)
USEPA (2014, 2016, 2018) | PFBS, PFOS-, PFOA, HFPO-DA
Michigan (2019) | PFHxS-, PFNA
Minnesota (2018) | PFBA-
Texas (2016) | PFOSA- (+RfCs for 8 PFASs)
Europe (RIVM 2018) | PFHpS, PFDS, PFPeA, PFHxA, PFHpA, PFDA, PFUnA, PFDoDA, PFTrDA, PFTeDA
Physiochemical Constants | USEPA, European Chemical Agency, ITRC, etc.

## Slide 23
*Washington State DOE compilation (2020)
*Reference | Compounds (9)
Giesey et al (2010) | PFBS-
Australia (2018) | PFOS-, PFOA-
European Chemical Agency (2018) | PFHxA-
UNDEP (2018) | PFHxS- (assumed = PFOS-)
Various | PFNA-, PFDA-, PFUnDA-, PFDoDA-
Drinking water action level used as temporary surrogate for if aquatic toxicity if latter not available;
Laboratory bioassay tests recommended if exceeded;
Uptake and bioaccumulation in food chain not considered (yet).
Aquatic Toxicity (acute and chronic)
(limited action levels available)