## Slide 1
Biosolids
Soil Amendment
Wastewater
Irrigation
Food Wrappers &
Containers
Fire Training Areas
(AFFF)
Roger Brewer, PhD,
Senior Environmental Scientist
Hawaii Department of Health
roger.brewer@doh.Hawaii.gov
March 12, 2024
Australia PFASs & Sampling
Workshops (February 2024)
Per- and Poly-Fluoroalkyl Substances
- Updates to Hawaii’s PFAS Guidance -

## Slide 2
Hawaii Dept of Health Guidance:
Interim Soil and Water Environmental Action Levels (EALs) for Perfluoroalkyl and Polyfluoroalkyl Substances (PFASs), January 2024 (draft): https://health.hawaii.gov/heer/guidance/additional-guidance-documents/
PFAS Basics:
ITRC 2020: Per- and Polyfluoroalkyl Substances (PFASs)
TOPs Methods:
Ateia et al., 2023, Total Oxidizable Precursor (TOP) Assay Best Practices, Capabilities and Limitations for PFAS Site Investigation and Remediation: Environmental Science and Technology Letters. Vol. 10, pp 292−301.
Other PFAS References
HIDOH PFAS Webpage:
https://health.hawaii.gov/heer/environmental-health/highlighted-projects/per-and-polyfluoroalkyl-substances-pfass/
HIDOH Recorded Webinars:
https://health.hawaii.gov/heer/guidance/heer-webinars/

## Slide 3
PFAS Guidance Update
January 2024 (Draft)
1.0 Terminology, Chemistry, Manufacture and Use
2.0 Sources of PFASs in Soil and Groundwater
3.0 Physiochemical Constants
4.0 Toxicity Factors
5.0 Environmental Fate and Transport
6.0 Environmental Action Levels for Individually Targeted PFASs (indoor air and soil vapor action level added for PFPrA-)
7.0 Assessment of Total PFAS Risk
8.0 Sample Collection and Processing
9.0 Laboratory Test Methods
Limitations
+ Figures & Tables
Hawaii Dept of Health Guidance:
Interim Soil and Water Environmental Action Levels (EALs) for Perfluoroalkyl and Polyfluoroalkyl Substances (PFASs), January 2024 (draft): https://health.hawaii.gov/heer/guidance/additional-guidance-documents/

## Slide 4
January 2024 PFAS Guidance Main Updates
Reference Concentration for 6:2 FTS corrected (MIDEGLE 2020);
Toxicity factors, physiochemical constants and action levels for following compounds added:
  Perfluoropentane sulfonate and Perfluoropropanoate (identified in water samples);
  6:2 fluorotelomer alcohol and 8:2 fluorotelomer alcohol (used to coat food wrappers and compostable food containers); and
  6:2 fluorotelomer thioether amido sulfonate (primary PFAS in modern AFFF);
Target noncancer Hazard Quotient of “1” used to generate soil action levels;
Calculation of cumulative “Hazard Index” required for soil and drinking water data;
Guidance and accompanying Excel spreadsheet added for calculation of sample-specific “Total PFAS Risk.”

## Slide 5
Plant
Uptake
Irrigation

## Slide 6
PFASs Chemistry Basics: Carboxylates & Sulfonates
Octane (C8H18)
Perfluoro Octanoic Acid (perfluoro octanoate)
Older
AFFF
Perfluoro Butanoic Acid (perfluoro butanoate)
Butane (C4H10)
Food
Wrappers
O-
O-
Anionic forms most common in soil and water

## Slide 7
History of PFASs Toxicity Studies
(after EWG: https://www.ewg.org/research/decades-polluters-knew-pfas-chemicals-were-dangerous-hid-risks-public)
PFAS Buildup in Mice
1950s | 1960s | 1970s | 1980s
PFAS Buildup in Humans
Liver & Spleen Damage
Food Packaging Concerns
Toxic to Fish
Food Packaging Concerns
Damage
To Fetuses
Tumors, Immune System
Cancer, etc.
In Workers
1990s | 2000s | 2010s | 2020s
Industry Scientist Concern
Impacted
DW Wells
PFOS Phased Out
PFOA Phased Out
Reduction in Food Packaging
Additional Toxicity Studies
Proposed Drinking
Water Standards
7
First Manufactured in 1930s
Water- & grease-resistant materials

## Slide 8
PFASs Toxicity
(based on references in HIDOH 2024)
Cancer
Metabolic
Hepatic
Cardiovascular
Developmental
Endocrine
Hematologic
Immune
Kidney
Nervous
Reproductive
Skin

## Slide 9
Relative PFAS Toxicity
(based on references in HIDOH PFAS guidance 2024)
PCBs
Arsenic
DDT
TCE
CrVI
PCE
Benzene
Dioxins = 1,000X PFOS
Increasing Toxicity
Short Chain (lower toxicity)
Long Chain (lower toxicity)
Ultrashort Chain

## Slide 10
Terminal Endpoint Compound | # Carbons | Soil-res (µg/kg) | TapWater (ng/L)
Perfluoro butane sulfonate (PFBS-) | 4 | 3,800 | 1,700
Perfluoro pentane sulfonate (PFPeS-) | 5 | 2,000 | 650
Perfluoro hexane sulfonate (PFHxS-) | 6 | 250 | 77
Perfluoro heptane sulfonate (PFHpS-) | 7 | 126 | 38
Perfluoro octane sulfonate (PFOS-) | 8 | 25 | 7.7
Perfluoro decane sulfonate (PFDS-) | 10 | 126 | 38
Perfluoro propanoate (PFPrA-) | 3 | 5,000 | 510
Perfluoro butanoate (PFBA-) | 4 | 48,000 | 15,000
Perfluoro pentanoate (PFPeA-) | 5 | 5,100 | 1,500
Perfluoro hexanoate (PFHxA-) | 6 | 6,300 | 1,900
Perfluoro heptanoate (PFHpA-) | 7 | 250 | 77
Perfluoro octanoate (PFOA-) | 8 | 38 | 12
Perfluoro nonanoate (PFNA-) | 9 | 38 | 12
Perfluoro decanoate (PFDA-) | 10 | 25 | 7.7
Perfluoro undecanoate (PFUnDA-) | 11 | 63 | 19
Perfluoro dodecanoate (PFDoDA-) | 12 | 84 | 26
Perfluoro tridecanoate (PFTrDA-) | 13 | 84 | 26
Perfluoro tetradecanoate (PFTeDA-) | 14 | 840 | 260
18 “Terminal” PFASs Compounds With Toxicity Factors
(2024 Hawaii Dept of Health Action Levels noted)
Ultrashort
Short
Long
Sulfonates
Carboxylates
Method
537/1633

## Slide 11
Assessment of Health Risk
WWTP Biosolids: Standard PFAS Method (537/1633)
Potential Health Risk if Hazard Index >1 (rounded to single significant digit)

## Slide 12
Assessment of Health Risk
AFFF-Impacted Soil: Standard PFAS Method (537/1633)
Potential Health Risk if Hazard Index >1 (rounded to single significant digit)

## Slide 13
Evolution of PFAS Science…
"The aim of science is not to open the door to infinite wisdom, but to set a limit to infinite error."
Bertolt Brecht
Confidence
Knowledge in Field
Huh???
I know everything
There’s more to this
than I thought…
It’s starting to
make sense
high
high
low
low
Ahah…
I’m never going
to understand this
Notes: denial, anger, bargaining, depression and acceptance

## Slide 14
Problem: Hundreds of PFAS “Precursor” Compounds
(not reported by laboratory and/or lack toxicity factors)
AFFF (6:2 FtTAoS-)
Wastewater
(metabolites)
Biosolids
(metabolites)
Food Containers
& Wrappers (6:2FTOH-)

## Slide 15
6:2 FtTAoS
“Precursor” Compounds (color denotes main breakdown products)
Ammonium 4,8-Dioxa-3H-perfluoro nonanoate (ADONA-) ???
2,3,3,3-tetrafluoro-2-(heptafluoropropoxy) propanoate (HFPO DA-, “GenX”) ???
6:2 Fluorotelomer alcohol (6:2 FTOH-)
6:2 Fluorotelomer thioether amido sulfonate(6:2 FtTAoS-)
6:2 Fluorotelomer sulfonate (6:2 FTS-)
Perfluroroctane sulfonamide (PFOSA)
8:2 Fluorotelomer alcohol (8:2 FTOH-)
Seven “Precursor” Compounds With Toxicity Factors
(soil and water action levels included in 2024 HIDOH guidance)
Ultrashort
Short
Long
Breakdown
Products
Method
537/1633

## Slide 16
Standard Lab Method vs Total Oxidizable Precursors (TOPs) Soil Data (AFFF Spill Site)
DU-2
Pre-TOPs: 144 µg/kg
Post-TOPs: 23,839 µg/kg
DU-4A
Pre-TOPs: 16 µg/kg
Post-TOPs: 114 µg/kg
DU-3
Pre-TOPs: 264 µg/kg
Post-TOPs: 22,013 µg/kg
DU-4B
Pre-TOPs: 13 µg/kg
Post-TOPs: 643 µg/kg
TOPs

## Slide 17
2
3
1
4
5
6
7
8
O
OH
2
3
1
4
5
6
7
6:2 Fluorotelomer Thioether Amido Sulfonate
PFAS “Precursor” (since 2005)
6:2 FtTAoS in “Modern” Aqueous Fire Fighting Foam (AFFF)
“Parent” PFAS
“Functional Group”
Added
Perfluoro Heptanoic Acid
Reported by Standard Lab Methods
Dominant PFAS in AFFF since 2005;
Toxicity factors not widely available;
Not Reported by current laboratory methods;
Risk posed by AFFF-contaminated media underestimated.

## Slide 18
Chart: Influent (Filtered)
| 5:3 FTCA- | PFHxA- | PFOA- | PFOS- | PFBA- | Other
 | 0.42297 | 0.23632 | 0.087905 | 0.070144 | 0.050124 | 0.13254
Chart: Effluent (Filtered)
| PFPeA- | PFHxA- | 6:2 FTS- | PFOA- | PFOS- | Other
 | 0.31809 | 0.2024 | 0.090924 | 0.082479 | 0.077412 | 0.22869
Municipal WWTP
Effluent
Biosolids
Other: 6:2 FTS-, PFPeA-, PFDA-, PFHpA-, PFDoA-, PFNA-, PFHxS-
Other: PFBA-, PFBS-, PFHpA-, PFDA-, PFNA-, PFHxS-
Total PFAS: 36 ng/L
Total PFAS: 66 ng/L
Influent
Biosolids
Pre-TOPs Total PFAS: 182 µg/kg
Post-TOPs Total PFAS: 624 µg/kg
Chart: Biosolids
| 5:3 FTCA- | PFOS- | 7:3 FTCA- | N-MeFOSE- | MeFOSAA- | Other
 | 0.28585 | 0.13331 | 0.11408 | 0.09101 | 0.069585 | 0.30616
Other: N-EtFOSE-, EtFOSAA-, PFDA-, PFDoA-, PFHxA-, PFDS-, 6:2 FTS-, PFTeDA-, PFUnA-, PFTrDA-, PFOA-, PFOSA-, PFBS-, N-MeFOSA-, PFNA-
Pre-TOPs Data:
Abundant metabolites
Partial oxidation of precursors
Reported by laboratory but no toxicity factors
Post TOPs Data:
Biosolids: Increase in Total PFASs indicates presence of significant additional PFASs precursors
Water: Minimal increase in water sample data
Highly Oxidized
Pre-TOPs Data
>99.9% of PFAS sorbed to organic matter
Expanded Analyte List

## Slide 19
Evolution of PFAS Science…
"The aim of science is not to open the door to infinite wisdom, but to set a limit to infinite error."
Bertolt Brecht
Confidence
Knowledge in Field
Huh???
I know everything
There’s more to this
than I thought…
It’s starting to
make sense
high
high
low
low
Ahah…
I’m never going
to understand this
Notes: denial, anger, bargaining, depression and acceptance

## Slide 20
Assessment of Precursor PFASs
Manufactured PFAS
PFAS
Metabolites
Convert
Terminal PFASs
Directly
Compare to Action Levels
Precursor Mixture
?

## Slide 21
Natural Oxidation and Breakdown of 6:2 FtTAOS
Natural Biotransformation
of 6:2 FtTAOS
(Marjanoic et al. 2015)
Terminal End PFASs
(anion form likely present)
Metabolites
(partial oxidation)
Mixture of metabolites & Terminal PFASs appears to be common

## Slide 22
Nancy Tseng, Ning Wang, Bogdan Szostek and Shaily Mahendra, 2014, Biotransformation of 6:2 Fluorotelomer Alcohol (6:2 FTOH) by a Wood-Rotting Fungus: Environ. Sci. Technol. 2014, 48, 7, 4012–4020,
Carnero et al., 2021, Presence of Perfluoroalkyl and Polyfluoroalkyl Substances (PFAS) in Food Contact Materials (FCM) and Its Migration to Food: Foods 2021, 10, 1443
Fluorotelomer alcohols… used in materials in contact with food as non-stick agents (e.g., 6:2 FTOH, 8:2 FTOH, 10:2 FTOH)
?
Hawaii tested WWTPs do not receive landfill leachate
Natural Oxidation of FTOHs to Terminal PFASs
Dietary secondary source of PFASs;
Mixtures common.
PFHxA-
PFPeA-
PFBA-

## Slide 23
Total Oxidizable Precursors (TOPs) Method:
  Sample heated with an oxidizing agent under alkaline conditions;
  Strips functional groups from PFAS leaving terminal end products;
  Identifies presence of previously unreported ultrashort-, short- and long-chain PFASs precursor compounds in sample;
  Final terminal end-product mixture minus pre-TOPs mixture assumed to reflect metabolic products of original compound mixture.
Laboratory Breakdown of Precursors and Metabolites to Terminal PFASs using “TOPs” Methods
TOPs
Terminal Compounds
Precursors &
Metabolites
Hidden
PFASs

## Slide 24
Pre- vs Post-TOPs Makeup of WWTP Biosolids
(Pre-TOPs data missed 90% of PFASs in Sample)
Concentration of “Post TOPs PFASs” = Post-Tops minus Pre-TOPs Terminal PFAS data

## Slide 25
Assessment of Post-TOPs PFASs Risk
Biosolids: Standard PFAS Method (537/1633)
Pre-TOPs PFASs + Post-TOPs PFAS HI = 5

## Slide 26
Pre- vs Post-TOPs Makeup of Ansul AFFF
Concentration of “TOPs PFASs” = Post-Tops minus Pre-TOPs Terminal PFAS data;
Excess Post-TOPs PFASs represent oxidation products of PFASs missed by standard laboratory method (>99.9% of PFASs present);
“Non-targeted Analysis (NTA)” identified primary hidden PFAS as 6:2 FtTAoS.

## Slide 27
Pre- vs Post-TOPs Makeup of AFFF-Impacted Soil (DU-2)
(Pre-TOPs data missed 99.9% of PFASs in Sample)
Concentration of “TOPs PFASs” = Post-Tops minus Pre-TOPs Terminal PFAS data;
Additional Post-TOPs PFASs represent oxidation products of PFASs missed by standard laboratory method (>99.9% of PFASs present).

## Slide 28
Pre-TOPs PFASs Hazard + Post-TOPS PFASs Hazard = 0.706
(potential leaching risk being assessed separately)
Assessment of Post-TOPs PFASs Health Risk
AFFF-Impacted Soil: Post-TOPs PFASs Risk (Method 537/1633)

## Slide 29
Evolution of PFAS Science…
"The aim of science is not to open the door to infinite wisdom, but to set a limit to infinite error."
Bertolt Brecht
Confidence
Knowledge in Field
Huh???
I know everything
There’s more to this
than I thought…
It’s starting to
make sense
high
high
low
low
Ahah…
I’m never going
to understand this
?
Notes: denial, anger, bargaining, depression and acceptance

## Slide 30
More Missing PFASs! Excess Organic Fluorine in Water!
Total Organic Fluorine (Method 1621)
Liquids: “Absorbable Organic Fluorine”
Solids: “Extractable Organic Fluorine”
TOF Reported by Laboratory
Concentration of TOF predicted based on fluorine content of
Post-TOPs PFAS
Excess Fluorine
?

## Slide 31
Components of Total PFAS Risk
(Example Mainland Drinking Water Data)
Total PFASs Risk =
Pre-TOPs PFASs Risk +
Post-TOPs PFASs Risk +
Excess Fluorine PFASs Risk
?
Excess fluorine not related to pre- or post-TOPs PFASs primarily identified in water samples (higher detection limit in solids samples)
Limited Non-Targeted Analysis (NTA) analysis typically identifies ultrashort PFASs (e.g., PFPrA-).
O-

## Slide 32
HIDOH 2024 PFPrA- Action Levels:
Soil Direct Exposure = 5,100 µg/kg
Drinking Water/Tapwater AL = 510 ng/L
Excess Fluorine Data:
Assume Excess Fluorine = PFPrA- (C3HF5O2).
Adjust Excess Fluorine Concentration to reflect equivalent concentration of PFPrA-.
Compare to PFPrA- Action Levels.
Calculate Hazard Quotient
Assessment of “Excess Fluorine” PFASs Risk
Excess Fluorine PFASs Concentration:
PFPrA- Molecular Weight (164)
F Atomic Mass (19) x # Fs (5)
= Excess EF Conc. x
= Excess EF Conc. X 1.73
?

## Slide 33
Assessment of Total PFAS Risk
Total PFASs Risk =
Pre-TOPs PFASs Risk +
Post-TOPs PFASs Risk +
Excess Fluorine PFASs Risk
537/1633: Pre-TOPs lab method
TOPs: Total Oxidizable Precursors
TOF: Total Organic Fluorine (AOF, EOF)
Liquids: Absorbable Organic Fluorine
Solids: Extractable Organic Fluorine

## Slide 34
Municipal WWTP Sample Data (report pending)
WWTP | *Sample Type | Units | 1Total PFAS Pre-TOPs | 1Total PFAS Post-TOPs | TOF
#1 | Influent | ng/L | (pending) | (pending) | (pending)
 | Effluent | ng/L | 24 | 22 | <40,000
 | Biosolids | µg/kg | (pending) | (pending) | (pending)
#2 | Influent | ng/L | (pending) | (pending) | (pending)
 | Effluent | ng/L | 834 | 698 | <40,000
 | Biosolids | µg/kg | (pending) | (pending) | (pending)
#3 | Influent | ng/L | (pending) | (pending) | (pending)
 | Effluent | ng/L | 37 | 30 | <40,000
 | Biosolids | µg/kg | 76 | 229 | (pending)
#4 | Influent | ng/L | 17 | - | -
 | Effluent | ng/L | 114 | - | -
 | Biosolids | µg/kg | 131 | - | -
#5 | Influent | ng/L | 66 | - | -
 | Effluent | ng/L | 36 | - | -
 | Biosolids | µg/kg | 183 | 678 | (pending)
#6 | Influent | ng/L | 40 | - | -
 | Effluent | ng/L | 32 | - | -
 | Biosolids | µg/kg | 86 | 945 | (pending)
#7 | Influent | ng/L | 22 | - | -
 | Effluent | ng/L | 144 | - | -
 | Biosolids | µg/kg | 124 | 785 | (pending)
1. Incudes reported precursor compounds if identified

## Slide 35
Total PFAS Risk Calculator
Hawaii Dept of Health January 2024 (public review draft)

## Slide 36
Example Total PFAS Risk:
WWTP Effluent as Hypothetical Drinking Water
Calculated
Total PFAS Risk
*Input Pre-TOPs and Post-TOPs
Terminal Endpoint Compound Concentrations
*AOF = ND (<40 µg/L)

## Slide 37
Example Total PFAS Risk:
WWTP Effluent as Hypothetical Drinking Water
WWTP Effluent | Total Terminal PFAS (ng/L) | Hazard Index | Primary Risk Drivers (>50%, >10% or risk or Top 3 if HI <1)
#1 | 17 | 0.01 | None (Pre-TOPs PFPeA- & PFHxA-)
#2 | 868 | 0.57 | None (Pre-TOPs PFPeA-, PFHxA-)
#3 | 37 | 1.6 | Pre-TOPs PFOS- (+ PFPeA-, PFHxA-)
*#4 | 124 | 3.1 | Pre-TOPs PFOA-, PFDA-
*#5 | 32 | 0.8 | None (Pre-TOPs PFPeA- & PFHxA-)
*#6 | 17 | 0.69 | None (Pre-TOPs PFOS-, PFOA-, PFDA-)
*#7 | 144 | 2.3 | Pre-TOPs PFOA-, PFNA- (+ PFOS-)
*TOPs and TOF data not collected. |  |  | 
No precursor-related, Post-TOPs PFASs identified (all dissolved-phase precursors oxidized prior to discharge);
Excess Fluorine PFASs ND (Reporting Limit = 40 µg/L);
Reported at AFFF sites (ultrashorts estimated >50% of total PFASs);
Great toxicity of long-chain PFASs (>100X) negates likely significant, additional contribution to Total PFAS Risk from TOF-related ultrashorts?

## Slide 38
Example Total PFAS Risk:
Hypothetical Use of WWTP Biosolids as Residential Fill
Calculated
Total PFAS Risk
*Input Pre-TOPs and Post-TOPs
Terminal Endpoint Compound Concentrations
*EOF data pending

## Slide 39
Example Total PFAS Risk:
Direct Exposure to Biosolids
Precursor-related PFASs drive potential direct exposure risk over original (pre-TOPs) terminal endpoint PFASs in samples;
Additional risk posed by any Excess Fluorine-related PFASs present unknown (data pending; toxicity equal to PFPeA-).
*Includes Pre-TOPs and Post-TOPs data (TOF pending)
*WWTP Biosolids | Total Terminal PFASs (µg/kg) | Hazard Index | Primary Risk Drivers (>50%, >10% or risk or Top 3 if HI <1)
#4 | 229 | 1 | PFPeA-, PFBA-, PFHxA- (57% Precursor PFASs)
#5 | 945 | 5 | PFBA-, PFPeA-, PFHxA- (92% Precursor PFASs)
#6 | 678 | 5 | PFBA-, PFPeA-, PFHxA- (72% Precursor PFASs)
#7 | 785 | 5 | PFBA-, PFPeA-, (71% Precursor PFASs)

## Slide 40
HIDOH Total PFAS Risk Guidance (posted January 2024)
Pros:
Allows (forces) consideration of precursor compounds (vs ignoring);
Comes with easy-to-use spreadsheet that calculates Total PFAS risk;
Cancer risk assessed based on subset of well-studied, individual PFAS compounds (e.g., PFOA – to be added in future spreadsheet model);
Similar to combined use of “TPH” and “BTEX-PAHs” for assessment of Total Petroleum risk.
Limitations:
TOPs methods still evolving;
TOPs methods produce similar results but don’t directly mimic biological processes (Too conservative? Not conservative enough?);
Some types of precursors not fully oxidized (e.g., chlorinated PFASs);
Toxicity of non-fluorinated functional group breakdown products not considered (but likely superseded by PFAS risk);
Total PFAS Risk approach does not consider synergistic effects of exposure to PFAS mixtures (common to all risk assessments).

## Slide 41
Questions, Ideas?
Future Research Ideas:
Tiered approach to leaching of PFAS from soil/biosolids (action levels, SPLP batch leaching test, modified Method 1314 Soil Column leaching test);
Bioavailability of PFASs in soil & biosolids;
Uptake of PFASs into food crops;
“Risk-Based” frequency of groundwater monitoring;
Other?
Notes: denial, anger, bargaining, depression and acceptance

## Slide 42
Additional Slides

## Slide 43: Toxicity Factors: “Dose Makes The Poison”
1. Child (15kg), chronic exposure over 6 years (noncancer HQ = 1.0). Toxicity factors typically includes 10-100+ fold safety factor. For example only (safe dose varies with route of exposure, child vs adult, etc.).
Chemical | “1Safe” Average Daily Dose | Chronic Health Effect
Water | One liter?/hour | Hyponatremia
Aspirin | 81 mg/day (“mini-tab”) | G/I tract
Arsenic | 4.5 µg/day (1mm grain/3.5 yrs) | Multiple
PCBs | 300 ng/day (1mm grain/20 yrs) | Multiple
PFOS | 30 ng/day (1mm grain/165 yrs) | Multiple
“All things are poison, and nothing is without poison; the dosage alone makes it so a thing is not a poison.”
Paracelsus, 1538
Notes: Point: All chemicals potentially toxic at some dose.
Acute = Health effects instant to within three months.
Chronic = Long-term exposure (30 years).
Maximum Daily Dose without noncancer health effects via ingestion (varies wrt to route of exposure)
Potential unacceptable chronic health risk (noncancer) when maximum daily dose is exceeded (based on toxicity studies).
Cancer risks also estimated in a similar manner.
Forward vs backward risk assessments.

## Slide 44
Reference Dose (RfD): Long-term, daily exposure predicted to be “safe.”
PFOS RfD: 2.0 nanograms per kilogram of Body Weight per day (2.0 ng/kg-day)
15 kg child: “Tolerable Daily Exposure = 2.0 ng/kg-d x 15kg = 30 ng/day
Calculation of Risk-Based Screening Levels (noncancer)
Child
Exposure:
Screening Level:
Exposure
Allotment:
Soil (20%)
6.0 ng
200 mg/day
6.0 ng PFOS
200 mg Soil
= 30 µg/kg
Water (20%)
6.0 ng
0.78 Liters/day
6.0 ng PFOS
0.78 L Water
= 7.7 ng/L
Diet (60%)
18 ng
500 grams/day
18 ng PFOS
500g Food
= 36 ng/kg
Max Daily Exposure
30 ng/day
(25 µg/kg)