## Slide 1: USE OF RISK-BASED SAMPLING METHODS AND “TOTAL PFAS RISK” TO EXPEDITE ASSESSMENT AND REMEDIATION OF PFAS-CONTAMINATED SITES
Roger Brewer, PhD
(roger.brewer@doh.Hawaii.gov; after November 2024: tosbrewer@yahoo.com)
Hawaii Department of Health, USA
18 September 2024
www.crcCARE.com
ECOS SUMMARY (September 30, 2024)

## Slide 2
Hawai´i Field Study of PFAS and Assessment of “Total PFAS Risk”
(Sample Analyses: Pre-TOPs, Post-TOPs, TOF)
Hawaii Dept of Health Guidance:
Interim Soil and Water Environmental Action Levels (EALs) for Perfluoroalkyl and Polyfluoroalkyl Substances (PFASs), April 2024 (and updates https://health.hawaii.gov/heer/guidance/ehe-and-eals/
Field Study of PFASs Associated with WWTPs, Landfill Leachate and AFFF-Release Sites (November 2024).
Recorded Webinars: https://health.hawaii.gov/heer/guidance/heer-webinars/
PFAS Basics (chemistry, use, general toxicity):
ITRC 2020: Per- and Polyfluoroalkyl Substances (PFASs)
TOPs Methods:
Ateia et al., 2023, Total Oxidizable Precursor (TOP) Assay Best Practices, Capabilities and Limitations for PFAS Site Investigation and Remediation: Environmental Science and Technology Letters. Vol. 10, pp 292−301.
WWTPs (6)
Influent/Effluent
Landfills (5)
Leachate
AFFF Releases (2)
Soil & Groundwater
WWTPs (6)
Biosolids
Anthropogenic
Soil Background (9)

## Slide 3
Designation of PFAS Groups and Calculation of “Total PFAS Risk”
Total PFASs Risk =
Primary Terminal Endpoint PFAS Risk (“Pre-TOPs PFASs”)
+ Precursor PFASs Risk (“Post-TOPs PFASs”)
+ Ultrashort PFASs Risk (“Excess Fluorine PFASs”)
?
?
Assessment of Health Risk:
Focus on noncancer hazard and protection of developing children and pregnant mothers;
Higher confidence in noncancer toxicity factors;
Cancer risk assessed separately (PFOS, PFOA);
Protection against noncancer hazards assumed protective of longer-term, cancer risk.

## Slide 4
Terminal Endpoint Compound | # Carbons | Soil-res (µg/kg) | Tapwater (ng/L)
Perfluoro butane sulfonate (PFBS-) | 4 | 3,800 | 1,700 (2,000)
Perfluoro pentane sulfonate (PFPeS-) | 5 | 2,000 | 650
Perfluoro hexane sulfonate (PFHxS-) | 6 | 25 | 7.7 (10)
Perfluoro heptane sulfonate (PFHpS-) | 7 | 126 | 38
Perfluoro octane sulfonate (PFOS-) | 8 | 25 | 7.7 (*4)
Perfluoro decane sulfonate (PFDS-) | 10 | 126 | 38
Perfluoro ethanoate (PFEtA-) | 2 | pending | pending
Perfluoro propanoate (PFPrA-) | 3 | 5,000 | 510
Perfluoro butanoate (PFBA-) | 4 | 48,000 | 15,000
Perfluoro pentanoate (PFPeA-) | 5 | 5,100 | 1,500
Perfluoro hexanoate (PFHxA-) | 6 | 6,300 | 1,900
Perfluoro heptanoate (PFHpA-) | 7 | 250 | 77
Perfluoro octanoate (PFOA-) | 8 | 38 | 12 (*4)
Perfluoro nonanoate (PFNA-) | 9 | 38 | 12 (10)
Perfluoro decanoate (PFDA-) | 10 | 25 | 7.7
Perfluoro undecanoate (PFUnDA-) | 11 | 63 | 19
Perfluoro dodecanoate (PFDoDA-) | 12 | 84 | 26
Perfluoro tridecanoate (PFTrDA-) | 13 | 84 | 26
Perfluoro tetradecanoate (PFTeDA-) | 14 | 840 | 260
Toxicity Factors & Available for 18+ “Terminal Endpoint” PFASs
(2024 Hawaii Dept of Health Risk-Based Action Levels noted (+MCLs & MCLGs))
Ultrashort
Short
Long
Sulfonates
Carboxylates
“Trifluoroacetate”
(toxicity factors pending)

## Slide 5
2
3
1
4
5
6
7
8
O
OH
2
3
1
4
5
6
7
6:2 Fluorotelomer Thioether Amido Sulfonate
PFAS “Precursor”
“Parent” PFAS
“Functional Group”
Added
Perfluoro Heptanoic Acid
Reported by Standard Lab Methods
Dominant PFAS in AFFF since 2005;
Toxicity factors not widely available;
Not Reported by current laboratory methods;
Risk posed by AFFF-contaminated media potentially underestimated.
The Problem with Precursors…

## Slide 6
Total Oxidizable Precursors (TOPs) Method:
  Sample heated with an oxidizing agent under alkaline conditions;
  Strips functional groups from PFAS leaving terminal end products;
  Identifies presence of previously unreported ultrashort-, short- and long-chain PFASs precursor compounds in sample;
  Final terminal end-product mixture minus pre-TOPs mixture assumed to reflect metabolic products of original compound mixture (matches studies);
  Used to assess overall toxicity of precursor compounds.
Use of “TOPs” Processing to Simulate Metabolism
Of Precursors and Estimate Precursor Mixture Toxicity
TOPs
Terminal Compounds
Precursors &
Metabolites

## Slide 7
Chart: AFFF Site #1 Soil DU-2 (Pre-TOPs) (Total PFAS 144 µg/Kg)
| 6:2 FTS- | PFHxA- | PFBA- | PFPeA- | PFOA- | Other
6:2 FTS- PFHxA- PFBA- PFPeA- PFOA- Other | 0.83513 | 0.098824 | 0.038973 | 0.012527 | 0.0090473 | 0.0054979
Importance of TOPs Processing for Solids (AFFF Release Site #1)
Chart: AFFF Site #1 Soil DU-2 (Post-TOPs) (Total PFAS 23,839 µg/Kg)
| PFPeA- | PFBA- | PFHxA- | PFHpA- | 6:2 FTS- | Other
PFPeA- PFBA- PFHxA- PFHpA- 6:2 FTS- Other | 0.49498 | 0.26888 | 0.2089 | 0.026972 | 9.9416e-05 | 0.00016636
Release of AFFF concentrate in 2022 (“Modern” AFFF);
Obviously impacted soil excavated;
45-Increment, 2kg Multi Increment Sample collected;
Pre-TOPs missed 99.9% of PFASs in soil (NTA = 6:2 FtTAoS).
X
X
Stop the Grab!

## Slide 8
Chart: WWTP #6 EFFLUENT (Pre-TOPs) (Total PFAS 655 ng/L)
| PFPeA- | PFHxA- | PFBS- | PFBA- | PFOA- | Other
PFPeA- PFHxA- PFBS- PFBA- PFOA- Other | 0.59739 | 0.3476 | 0.025581 | 0.017305 | 0.0047249 | 0.0074049
Chart: WWTP #6 INFLUENT (Pre-TOPs) (Total PFAS 250 ng/L)
| 5:3 FTCA- | PFHxA- | PFBA- | PFOS- | PFOA- | Other
PFPeA- PFHxA- PFBS- PFBA- PFOS- Other | 0.58 | 0.3436 | 0.02764 | 0.02192 | 0.0158 | 0.01104
AOF =
2,000 ng/L
AOF =
1,600 ng/L
The Problem with “Excess Organic Fluorine…” (NTA Data = Ultrashorts)
Total PFAS: 49 µg/L
AOF: 190 µg/L
Total PFAS: 8.0 µg/L
AOF: 18 µg/L
Chart: Landfill #1 Leachate E-6 (Pre-TOPs) (Total PFAS 66,664 ng/L)
| 5:3 FTCA- | PFBS- | PFHxA- | PFPeA- | PFOA- | Other
5:3 FTCA- PFBS- PFHxA- PFPeA- PFOA- Other | 0.40208 | 0.2165 | 0.14846 | 0.068044 | 0.049487 | 0.11543
Chart: Landfill #1 Leachate 4-B (Pre-TOPs) (Total PFAS 40,618 ng/L)
| 5:3 FTCA- | PFHxA- | PFBA- | PFPeA- | PFBS- | Other
5:3 FTCA- PFHxA- PFBA- PFPeA- PFBS- Other | 0.20927 | 0.15264 | 0.14279 | 0.10833 | 0.078783 | 0.30819
AOF =
83,000 ng/L
AOF =
51,000 ng/L
Wastewater
Leachate
AFFF Groundwater

## Slide 9
HIDOH 2024 PFPrA- Action Levels:
Soil Direct Exposure = 5,100 µg/kg
Drinking Water/Tapwater AL = 510 ng/L
Estimated Excess Organic Fluorine:
Assume Excess Fluorine = PFPrA- (C3HF5O2).
Adjust Excess Fluorine Concentration to reflect equivalent concentration of PFPrA-.
Compare to PFPrA- Action Levels.
Calculate Hazard Quotient.
Excess Organic Fluorine PFASs Concentration:
PFPrA- Molecular Weight (164)
F Atomic Mass (19) x # Fs (5)
= Excess Organic Fluorine x
= Excess Organic Fluorine Conc. X 1.73
Use of PFPrA- as a Surrogate for Excess Organic Fluorine PFASs Toxicity
?
?
?

## Slide 10
Example Calculation of “Total PFAS Risk”
Total PFASs Risk =
Primary Terminal Endpoint PFAS Risk (“Pre-TOPs PFASs”)
+ Precursor PFASs Risk (“Post-TOPs PFASs”)
+ Ultrashort PFASs Risk (“Excess Fluorine PFASs”)
Assessment of Health Risk:
Focus on noncancer hazard and protection of developing children and pregnant mothers;
Higher confidence in noncancer toxicity factors; Cancer risk assessed separately (PFOS, PFOA);
Protection against noncancer hazards assumed protective of longer-term, cancer risk.

## Slide 11
1. Calculation of Primary PFASs Risk (Pre-TOPs)
- WWTP Biosolids Example -
Potential Health Risk if Hazard Index >1 (rounded to single significant digit)

## Slide 12
2. Calculation of Precursor PFASs Risk (Post-TOPs)
- WWTP Biosolids Example -
Concentration of “Post TOPs PFASs” = Post-Tops minus Pre-TOPs Terminal PFAS data
Pre-TOPs missed 90% of PFASs

## Slide 13
Pre-TOPs PFASs + Post-TOPs PFAS HI = 1.5
2. Calculation of Precursor PFASs Risk (Post-TOPs)
- WWTP Biosolids Example -

## Slide 14
Excess Organic Fluorine:
Predicted TOF = 265 µg/Kg
Measured TOF = 842 µg/Kg
Excess OF = 577 µg/Kg
Unidentified Ultrashorts
3. Calculation of Ultrashorts PFASs Risk (Excess Organic Fluorine)
- WWTP Biosolids Example -
HQ =
577 µg/Kg x 1.73
5,100 µg/Kg
= 0.2
OF = Conc x
F Atomic Mass (19) x # Fs
Compound MW

## Slide 15
Final Total PFAS Risk
- WWTP Biosolids Example -
Total PFASs Risk =
Pre-TOPs PFASs Risk +
Post-TOPs PFASs Risk +
Excess Fluorine PFASs Risk
Total PFASs Risk
= 0.5 + 1.0 + 0.2
= 1.7
= 2 (*noncancer Hazard Index)
*Rounded to single digit

## Slide 16
Hawai’i Total PFAS Risk Calculator:
Example: WWTP Biosolids (residential soil exposure)
Step 1:
Input Sample Information
Step 2:
Select Media Type
(solid or liquid)
Step 3:
Select Exposure Scenario

## Slide 17
Step 4:
Hawai’i Total PFAS Risk Calculator:
Example: WWTP Biosolids (residential soil exposure)

## Slide 18
Total PFAS Risk Calculated
(Hazard Index)
Hawai’i Total PFAS Risk Calculator:
Example: WWTP Biosolids (residential soil exposure)

## Slide 19
HIDOH PFAS Study Observations
Media | Observations
Solids | TOPs Processing: Identified significant, additional short-chain and long-chain precursor PFASs in biosolids and soil (Precursor PFASs drive risk) Total Organic Fluorine: Identified significant, additional ultrashort compounds in biosolids Municipal WWTP Biosolids: Precursor PFASs drive risk AFFF-Impacted Soil: Pre-2005 AFFF: Primary PFASs drive risk Post-2005 AFFF: Precursor PFASs drive risk
Liquids | TOPs Processing: Did not identify significant additional short-chain or long-chain precursor PFASs (Post-TOPs PFASs < Pre-TOPs PFASs) Total Organic Fluorine: Identified significant, additional ultrashort compounds (dominate wastewater, leachate & AFFF impacted groundwater) Municipal WWTP Effluent: Ultrashorts drive risk over Primary PFASs? Landfill Leachate: Primary PFAS drive risk over Ultrashorts? AFFF-Impacted Groundwater: Source Area: Primary PFASs drive risk Distal Plume: Ultrashorts drive risk?

## Slide 20
Questions? Ideas?
Ongoing Research:
Nature and toxicity of apparent ultrashorts;
Leaching of PFAS from soil/biosolids (action levels, SPLP batch test, modified Soil Column test);
Bioavailability of PFASs in soil & biosolids;
Uptake of PFASs into food crops;
PFAS Vapor Intrusion;
Other?
All models are wrong, but some are useful.
George Box
It’s better to be roughly right than precisely wrong.
John Maynard Keynes

## Slide 21
Additional Slides

## Slide 22
Fluorotelomer Alcohols (4:2, 6:2 and 8:2 FTOH)
6:2 Fluorotelomer Thioamido Sulfonate (6:2 FtTAoS)
6:2 fluorotelomer Sulfonate (6:2 FTS)
Additional Precursor Toxicity Factors
(action levels included in HIDOH guidance)
Developed By: Gibb & O’Leary Epidemiology Consulting for Hawaii Dept of Health
(Dr Herman Gibb – former USEPA epidemiologist)

## Slide 23
Natural Oxidation and Breakdown of 6:2 FtTAoS
Natural Biotransformation
of 6:2 FtTAoS
(Marjanoic et al. 2015)
Terminal End PFASs
(anion form likely present)
Metabolites
(partial oxidation)
Mixture of metabolites & Terminal PFASs appears to be common

## Slide 24
Comparison of Relative PFAS Group Makeup (example data)
- Effluent vs Leachate vs AFFF-Impacted Groundwater -
Chart: PFAS Group Relative Makeup
| WWTP Effluent | Landfill Leachate | AFFF Groundwater
Pre-TOPs Primary PFASs | 0.016889 | 0.25774 | 0.30209
Post-TOPs Precursor PFASs | 0.0052223 | 0.037953 | 0.14789
Excess Fluorine PFAS | 0.97789 | 0.70431 | 0.55002
(includes precursors)

## Slide 25
Comparison of Relative PFAS Group Risk (example data)
- Effluent vs Leachate vs AFFF-Impacted Groundwater -
Chart: PFAS Group Relative Risk
| WWTP Effluent | Landfill Leachate | AFFF Groundwater
Pre-TOPs Primary PFASs | 0.35239 | 0.67086 | 0.90612
Post-TOPs Precursor PFASs | 0.0072452 | 0.017826 | 0.052043
Excess Fluorine PFAS | 0.64037 | 0.31132 | 0.041838
(includes precursors)

## Slide 26
Comparison of Relative PFAS Group Makeup (example data)
- Biosolids vs Compost vs AFFF-Impacted Soil -
Pre-TOPs
PFAS 0.1%
Variable
EOF Not Tested

## Slide 27
Comparison of Relative PFAS Group Risk (example data)
- Biosolids vs Compost vs AFFF-Impacted Soil -
Pre-TOPs
PFAS 1.0%
Variable
EOF Not Tested

## Slide 28
Chart: Study Site
| WWTP #1 EFFL | WWTP #2-EFFL | WWTP #6-EFFL | Landfill #1 E-6 | Landfill #1 4B | Landfill #1 ASH | AFFF #2 MW-1 | AFFF #2 MW-2 | AFFF #2 MW-3 | AFFF #2 MW-4 | AFFF #2 MW-5 | AFFF #2 MW-7 | AFFF #2 MW-8 | AFFF #2 MW-9
 | 7.7321 | 7.53 | 5.6974 | 622.5773 | 1040.921 | 84.275 | 109473.6514 | 124456.3954 | 52643.917 | 23569.5933 | 20316.209 | 18651.491 | 21.7304 | 683.5163
Effluent
Leachate
AFFF-Impacted Groundwater
Relative Source Strength in Terms of Risk:
-WWTP Effluent vs Landfill Leachate vs AFFF-Impacted Groundwater-

## Slide 29
Biosolids/Compost
AFFF-Impacted Soil
(Hazard Indices in unremediated
release areas will be much higher)
Relative Source Strength in Terms of Risk:
-Biosolids vs Compost vs AFFF-Impacted Soil
Hazard Index
Chart: Study Site
| WWTP #1 Biosolids | WWTP #2 Biosolids | WWTP #6 Biosolids | WWTP #6 Compost | AFFF #1 DU-2 | AFFF #1 DU-3 | AFFF #1 DU-4a | AFFF #1 DU-4b | AFFF #1 DU5F
Total PFAS Risk | 2.5751 | 2.0639 | 1.7083 | 0.73506 | 5.919 | 6.075 | 0.38905 | 0.41427 | 38.113