## Slide 1: Aloha, The Overview of the EAL Updates and PFAS Field Study Webinar on Wednesday, November 20th, 2024. Presented by Roger Brewer Hawaii Department of Health (HDOH) HEER Office. Will start at 10:00 am, Hawaii Standard Time.
REMINDER: Everyone will be muted during the webinar except the presentation team. Please do not unmute your microphone if you join online or your phone if you call in. Background noise from unmuted mics and phones can disrupt the presentation.
There will be a Question & Answer session via Instant Messaging (Chat) at the end of the presentation. There will not be an option to directly ask questions over the phone lines.
Questions posted during a presentation will be read by the moderator
and discussed by the presenter.
Mahalo!

## Slide 2
Roger Brewer, PhD
Senior Environmental Scientist
Hawaii Department of Health
November 20, 2024
Field Study of PFASs Associated with WWTPs,
Landfills and AFFF-Release Sites in Hawai‘i
PFAS
Groups
Investigation Questions
Analytical
Methods
“Total PFAS Risk”
Multiple Sample Collection Phases
Sample Collection
?
Direct
Exposure
Crop
Uptake
Groundwater Impacts
Leaching
Aquatic
Habitats
WWTP
Effluent?
Landfill
Leachate?
Fire Training
Areas?
WWTP
Biosolids?

## Slide 3
Outline
PFAS Basics
Risk-Based Groupings of PFASs
Estimation of “Total PFAS Risk”
Field Study Results
Comparison of “Relative Source Strengths”
Study Takeaway Points

## Slide 4
Hawaii Dept of Health Guidance:
Field Study of PFASs Associated with WWTPs, Landfill Leachate and AFFF-Release Sites in Hawaii (November 2024).
Interim Soil and Water Environmental Action Levels (EALs) for Perfluoroalkyl and Polyfluoroalkyl Substances (PFASs), November 2024 (and updates): https://health.hawaii.gov/heer/guidance/additional-guidance-documents/
Toxicity review of FTOHs and PFEtA (aka trifluoroacetate): EAL webpage
Technical Guidance Manual (site investigation design): https://health.hawaii.gov/heer/guidance/specific-topics/decision-unit-and-multi-increment-sampling-methods/
PFAS Basics:
ITRC 2020: Per- and Polyfluoroalkyl Substances (PFASs)
TOPs Methods:
Ateia et al., 2023, Total Oxidizable Precursor (TOP) Assay Best Practices, Capabilities and Limitations for PFAS Site Investigation and Remediation: Environmental Science and Technology Letters. Vol. 10, pp 292−301.
References
Other HIDOH PFAS Webpage:
https://health.hawaii.gov/heer/environmental-health/highlighted-projects/per-and-polyfluoroalkyl-substances-pfass/
HIDOH Recorded Webinars:
https://health.hawaii.gov/heer/guidance/heer-webinars/

## Slide 5
Anthropogenic
Background?
Background PFASs in Hawai‘i Soil – Mostly “Non-Detect”
(trace of PFBA- downwind of a town; trace EOF suspect – samples being retested)

## Slide 6
PFASs Chemistry Basics: Carboxylates & Sulfonates
“Terminal PFASs” (“Forever chemicals”)
Octane (C8H18)
Perfluoro Octanoic Acid (perfluoro octanoate)
PFOA/PFOS
(older AFFF, etc.)
O-
Perfluoro Butanoic Acid (perfluoro butanoate)
Butane (C4H10)
PFBA/PFBS
(textiles, paper, etc.)
O-
Anionic forms most common in soil and water

## Slide 7
Relative PFAS Toxicity (19 Terminal PFASs & 5 Precursors)
(noncancer Reference Dose; PFBA- = 1)
PCBs
Arsenic
DDT
TCE
Dioxins = 1,000X PFOS
Increasing Toxicity
Short Chain (lower toxicity)
Long Chain (lower toxicity)
Ultrashort Chain
Naphthalene
CrVI
PCE
Benzene
PFBA-
Precursors (mostly lower toxicity)

## Slide 8
Terminal PFAS Compound | # Carbons | Soil-res (µg/kg) | Tapwater (ng/L)
Perfluoro butane sulfonate (PFBS-) | 4 | 3,800 | 1,700 (2,000)
Perfluoro pentane sulfonate (PFPeS-) | 5 | 2,000 | 650
Perfluoro hexane sulfonate (PFHxS-) | 6 | 25 | 7.7 (10)
Perfluoro heptane sulfonate (PFHpS-) | 7 | 126 | 38
Perfluoro octane sulfonate (PFOS-) | 8 | 25 | 7.7 (*4)
Perfluoro decane sulfonate (PFDS-) | 10 | 126 | 38
Perfluoro ethanoate (PFPrA-, trifluoroacetate) | 2 | 29,000 | 18,000
Perfluoro propanoate (PFPrA-) | 3 | 5,000 | 510
Perfluoro butanoate (PFBA-) | 4 | 48,000 | 15,000
Perfluoro pentanoate (PFPeA-) | 5 | 5,100 | 1,500
Perfluoro hexanoate (PFHxA-) | 6 | 6,300 | 1,900
Perfluoro heptanoate (PFHpA-) | 7 | 250 | 77
Perfluoro octanoate (PFOA-) | 8 | 38 | 12 (*4)
Perfluoro nonanoate (PFNA-) | 9 | 38 | 12 (10)
Perfluoro decanoate (PFDA-) | 10 | 25 | 7.7
Perfluoro undecanoate (PFUnDA-) | 11 | 63 | 19
Perfluoro dodecanoate (PFDoDA-) | 12 | 84 | 26
Perfluoro tridecanoate (PFTrDA-) | 13 | 84 | 26
Perfluoro tetradecanoate (PFTeDA-) | 14 | 840 | 260
19 “Terminal PFAS” Compounds With Toxicity Factors
2024 Hawaii Dept of Health Toxicity-Based Action Levels (HQ=1) (MCLs & MCLGs)
Ultrashort
Short
Long
Sulfonates
Carboxylates

## Slide 9
“Precursors”: Terminal PFAS + Functional Group
(most not reported by laboratory and/or lack toxicity factors)
AFFF (6:2 FtTAoS)
Wastewater
(metabolites)
Biosolids
(metabolites)
Textiles, Carpet.
Food Containers, etc.
(e.g., 6:2 FTOH)

## Slide 10
Natural Oxidation and Breakdown of 6:2 FtTAoS
(after Marjanoic et al. 2015)
6 Carbons Fluorinated
4 & 5 Carbons Fluorinated
6 Carbons Fluorinated
5 Carbons Fluorinated
?
?
“PFAS Debris”
(C-F & C-C bonds broken)
Metabolites
(partial oxidation)
5:3 FTCA
?
?
PFEtA- (TFA)
PFPrA-
Secondary Terminal PFAS
F-
F-

## Slide 11
6:2 FtTAoS
(PFHpA + Functional Group)
Removed by TOPs
Total Oxidizable Precursors (TOPs) Processing
(breaks precursors down to Terminal PFASs)
Originally Present in Sample
Used to Assess Risk
Primary
Terminal PFASs
Primary
Terminal PFASs
PFHpA
Secondary
Terminal PFASs
Precursor PFASs
TOPs
PFPeA-
PFHxA-
+ ultrashorts

## Slide 12
PFAS Groups and Assessment of Total PFAS Risk
(cumulative health risk)
PFAS Groups:
Primary Terminal PFASs: Originally present in sample (direct comparison to action levels).
Secondary Terminal PFASs: Generated by TOPs breakdown of precursors (direct comparison to action levels).
Excess Fluorine PFASs: Additional PFASs identified by Total Organic Fluorine (TOF)
3. Excess
Fluorine
PFAS
Sample Analysis
1. Primary
PFAS
2. Secondary
PFAS
+TOPs
+TOPs
+TOF
NTA data and degradation pathway of precursors suggests Excess Organic Fluorine at least in part associated with ultrashort PFASs.
?

## Slide 13
HIDOH 2024 PFPrA- Action Levels:
Soil Direct Exposure = 5,100 µg/kg
Drinking Water/Tapwater AL = 510 ng/L
Estimation of Health Risk:
Assume All Excess Fluorine = PFPrA- (C3HF5O2).
Convert Excess Fluorine Concentration to equivalent concentration of PFPrA-.
Compare to PFPrA- Action Levels.
Calculate Hazard Quotient.
Excess Organic Fluorine PFASs Concentration:
PFPrA- Molecular Weight (164)
F Atomic Mass (19) x # Fs (5)
= Excess Organic Fluorine x
= Excess Organic Fluorine Conc. X 1.73
Assessment of Excess Organic Fluorine PFASs Health Risk
3. Excess
Fluorine
PFAS
Sample Analysis
1. Primary
PFAS
2. Secondary
PFAS
+TOPs
+TOPs
+TOF

## Slide 14
Total PFAS Risk
- WWTP Biosolids Example -
Total PFASs Risk =
Primary Terminal PFASs Risk +
Secondary Terminal PFASs Risk +
Excess Fluorine PFASs Risk
Laboratory Methods
*Primary Terminal PFASs:
SGS MLA110 or USEPA 1633 or 537M (before TOPs processing)
*Secondary Terminal PFASs:
SGS MLA111 or USEPA 1633 or 537M (after TOPs processing)
Excess Fluorine PFASs:
MLA 119 (TOF: Liquids = AOF; Solids = EOF)
*Ultrashorts: MLA120 (or request with USEPA Method)
3. Excess
Fluorine
PFAS
Sample Analysis
1. Primary
PFAS
2. Secondary
PFAS
+TOPs
+TOPs
+TOF

## Slide 15
Primary Terminal PFAS Noncancer Risk
- Example WWTP Biosolids -
Potential Health Risk if Hazard Index >1 (rounded to single significant digit)

## Slide 16
Calculation of Secondary Terminal PFASs (precursors)
- Example WWTP Biosolids -
Concentration of Secondary PFAS = Post-Tops minus Primary Terminal PFAS data
Pre-TOPs missed 90% of PFASs in sample

## Slide 17
Primary PFASs + Secondary PFAS HI = 1.5
Secondary Terminal PFASs Noncancer Risk (precursors)
- Example WWTP Biosolids -

## Slide 18
Excess Fluorine PFAS Noncancer Risk
- Example WWTP Biosolids -
Excess Fluorine PFASs:
1. PRPrA-equiv = 577 µg/Kg x 1.73
2. PRPrA-equiv = 998 µg/Kg
3. EF PFASs = 998 µg/Kg
Excess Fluorine PFASs
PFPrA- Soil Action Level
HQ =
1,015 µg/Kg
5,100 µg/Kg
HQ =
EF PFASs HQ = 0.2

## Slide 19
Total PFAS Risk
- Example WWTP Biosolids -
Total PFASs Risk =
Pre-TOPs PFASs Risk +
Post-TOPs PFASs Risk +
Excess Fluorine PFASs Risk
Total PFASs Risk
= 0.5 + 1.0 + 0.2
= 1.7
= 2 (*noncancer Hazard Index)
*Rounded to single digit
3. Excess
Fluorine
PFAS
Sample Analysis
1. Primary
PFAS
2. Secondary
PFAS
+TOPs
+TOPs
+TOF
Hazard Index (very simplified interpretation):
<1: No anticipated adverse health risk
>1: Review actual exposure, risk model assumptions, toxicity studies, etc.

## Slide 20
Hawai’i DOH Total PFAS Risk Calculator:
Example: WWTP Biosolids (residential soil exposure)
Step 1:
Input Sample Information
Step 2:
Select Media Type
(solid or liquid)
Step 3:
Select Exposure Scenario
Step 4 (optional):
Input Alternative Excess Fluorine PFASs Action Levels

## Slide 21
Hawai’i Total PFAS Risk Calculator:
Example: WWTP Biosolids (residential soil exposure)
Step 5:

## Slide 22
Hawai’i DOH Total PFAS Risk Calculator:
Example: WWTP Biosolids (residential soil exposure)

## Slide 23
Field Study: WWTPs, Landfills, AFFF-Release Sites
- Sample Collection and Laboratory Analyses -
Sample Collection:
WWTP Influent and Effluent:
24-Hour “Composite” Samplers
WWTP Biosolids and AFFF-Site Soils:
30- to 50-Increment Multi Increment Samples
Landfill Leachate and AFFF-Site Groundwater:
Grab samples (bailer, HydraSleeve)
Sample Analyses
Pre-TOPs: MLA110 (Method 537M )
Post-TOPs: MLA111 (Method 537M+TOPs)
Ultrashorts: MLA120 (+ added to 537M)
Total Organic fluorine: MLA119 (Method 1621)
Liquids: “Absorbable Organic Fluorine”
Solids: “Extractable Organic Fluorine”
Non-Target Analysis (optional)
Six Wastewater Treatment Plants
Five Landfills
Two AFFF Release Sites

## Slide 24
Collection of Multi Increment Soil & Biosolids Samples
Decision Unit area & volume of soil/biosolids designated for collection of a sample (worker exposure area);
Two kilogram, 45-increment sample collected;
Triplicate samples collected to test sampling method precision (not for a 95% UCL);
Sample air-dried & sieved to target particle size (methanol used for VOCs);
Minimum 10-gram MI subsample collected for analysis.
X
X
X
X
X
X
X
X
X
X
X
X
DU-5
A
C
B
X
X
Stop the Grab!
Field Study of Grab/Discrete Sample Reliability
https://health.hawaii.gov/heer/guidance/specific-topics/decision-unit-and-multi-increment-sampling-methods/

## Slide 25
Chart: WWTP #5 Biosolids (Post-TOPs) (Total PFAS 680 µg/Kg)
| PFBA- | PFPeA- | PFHxA- | PFOA- | PFHpA- | Other
PFBA- PFPeA- PFHxA- PFOA- PFHpA- Other | 0.26905 | 0.17936 | 0.13511 | 0.082625 | 0.081155 | 0.2527
Chart: WWTP #5 Effluent (Pre-TOPs) (Total PFAS 36 ng/L)
| PFPeA- | PFHxA- | 6:2 FTS- | PFOA- | PFOS- | Other
PFPeA- PFHxA- 6:2 FTS- PFOA- PFOS- Other | 0.31809 | 0.2024 | 0.090924 | 0.082479 | 0.077412 | 0.22869
Chart: WWTP #5 Influent (Pre-TOPs) (Total PFAS 64 ng/L)
| 5:3 FTCA- | PFHxA- | PFBA- | PFOS- | PFOA- | Other
5:3 FTCA- PFHxA- PFOA- PFOS- PFBA- Other | 0.43965 | 0.24564 | 0.091371 | 0.072909 | 0.0521 | 0.098334
Chart: WWTP #6 Biosolids (Pre-TOPs) (Total PFAS 59 µg/Kg)
Chart: WWTP #5 Biosolids (Pre-TOPs) (Total PFAS 181 µg/Kg)
| 5:3 FTCA- | PFOS- | 7:3 FTCA- | N-MeFOSE- | MeFOSAA- | Other
5:3 FTCA- PFOS- 7:3 FTCA- N-MeFOSE- MeFOSAA- Other | 0.2876 | 0.13413 | 0.11478 | 0.091567 | 0.070011 | 0.30191
Wastewater Treatment Plants (WWTP #5)
AOF = ?
AOF = ?
Total Post-TOPs PFASs less than Total Pre-TOPs
Post-TOPs decrease in total PFASs due to removal of Functional Group from 5:3 FTCA and lack of other precursors
Significant increase in Total Post-TOPs PFASs;
No EOF
No NTA
Not from landfill leachate

## Slide 26
Chart: WWTP #6 Influent (Pre-TOPs) (Total PFAS 250 ng/L)
| PFPeA- | PFHxA- | PFBS- | PFBA- | PFOS- | Other
PFPeA- PFHxA- PFBS- PFBA- PFOS- Other | 0.58 | 0.3436 | 0.02764 | 0.02192 | 0.0158 | 0.01104
Chart: WWTP #6 Effluent (Pre-TOPs) (Total PFAS 655 ng/L)
| PFPeA- | PFHxA- | PFBS- | PFBA- | PFOA- | Other
PFPeA- PFHxA- PFBS- PFBA- PFOA- Other | 0.59739 | 0.3476 | 0.025581 | 0.017305 | 0.0047249 | 0.0074049
Chart: WWTP #6 Biosolids (Post-TOPs) (Total PFAS 409 µg/Kg)
| PFBA- | PFPeA- | PFHxA- | PFHpA- | PFOA- | Other
PFBA- PFPeA- PFHxA- PFHpA- PFOA- Other | 0.35477 | 0.31563 | 0.1265 | 0.054807 | 0.03719 | 0.11111
Chart: WWTP #6 Biosolids (Pre-TOPs) (Total PFAS 59 µg/Kg)
| 5:3 FTCA- | PFDA- | PFOS- | PFHxA- | PFDoDA- | Other
5:3 FTCA- PFDA- PFOS- PFHxA- PFDoDA- Other | 0.48248 | 0.095649 | 0.080074 | 0.077366 | 0.049941 | 0.21449
Wastewater Treatment Plants (WWTP #6)
AOF =
2,000 ng/L
AOF =
1,600 ng/L
EOF =
892 µg/Kg
Total Post-TOPs PFASs similar to Total Pre-TOPs
AOF >10X higher than predicted;
NTA: Excess AOF = Ultrashorts?
Significant increase in Total Post-TOPs PFASs;
EOF 2X higher than predicted;
NTA: Excess EOF = Ultrashorts?
EOF =
892 µg/Kg

## Slide 27
Chart: Landfill #1 Leachate E-6 (Pre-TOPs) (Total PFAS 66,664 ng/L)
| 5:3 FTCA- | PFBS- | PFHxA- | PFPeA- | PFOA- | Other
5:3 FTCA- PFBS- PFHxA- PFPeA- PFOA- Other | 0.40208 | 0.2165 | 0.14846 | 0.068044 | 0.049487 | 0.11543
Chart: Landfill #1 Leachate 4-B (Pre-TOPs) (Total PFAS 40,618 ng/L)
| 5:3 FTCA- | PFHxA- | PFBA- | PFPeA- | PFBS- | Other
5:3 FTCA- PFHxA- PFBA- PFPeA- PFBS- Other | 0.20927 | 0.15264 | 0.14279 | 0.10833 | 0.078783 | 0.30819
Chart: Landfill #1 Leachate ASH (Pre-TOPs) (Total PFAS 12,970 ng/L)
| PFHxA- | PFPeA- | PFBA- | 5:3 FTCA- | PFBS- | Other
PFHxA- PFPeA- PFBA- 5:3 FTCA- PFBS- Other | 0.36237 | 0.23901 | 0.10794 | 0.10023 | 0.067078 | 0.12336
Landfill Leachate
(specifically reported PFASs)
100X increase in reported Total PFASs;
Significant concentration of 5:3 FTCA- in municipal waste cell leachate;
Reduced 5:3 FTCA- in cell storing incinerated municipal waste ash;
Total Post-TOPs PFASs similar to Total Pre-TOPs PFASs (minimal additional precursors);
AOF 2X higher than predicted based on identified PFASs (additional PFASs);
Ultrashort & NTA data: Pending.
AOF =
83,000 ng/L
AOF =
13,000 ng/L
AOF =
51,000 ng/L

## Slide 28
Chart: AFFF Site #1 Soil DU-2 (Pre-TOPs) (Total PFAS 144 µg/Kg)
| 6:2 FTS- | PFHxA- | PFBA- | PFPeA- | PFOA- | Other
6:2 FTS- PFHxA- PFBA- PFPeA- PFOA- Other | 0.83513 | 0.098824 | 0.038973 | 0.012527 | 0.0090473 | 0.0054979
AFFF Release Site #1 (Fuel Storage): Impacted Soil
Chart: AFFF Site #1 Soil DU-2 (Post-TOPs) (Total PFAS 23,839 µg/Kg)
| PFPeA- | PFBA- | PFHxA- | PFHpA- | 6:2 FTS- | Other
PFPeA- PFBA- PFHxA- PFHpA- 6:2 FTS- Other | 0.49498 | 0.26888 | 0.2089 | 0.026972 | 9.9416e-05 | 0.00016636
Release of AFFF concentrate in 2022 (“Modern” AFFF);
45-Increment Multi Increment samples collected;
Pre-TOPs missed 99.9% of PFASs in soil (NTA = 6:2 FtTAoS);
TOF (EOF) not analyzed.
Indicator of post-2005 AFFF and likely presence of 6:2 FtTAoS
High concentration of 6:2 FtTAoS oxidized to PFBA-, PFPeA- and PFHxA-

## Slide 29
800 ft
1977-1997: Unlined
Post 1997: Lined
paved
Pre-TOPs: 878 µg/Kg
Post-TOPs: 1,051 µg/Kg
Post-TOPs Total PFASs slightly higher than Pre-TOPs Total PFASs (low concentration of additional precursors);
Likely related to past releases of PFOS-based AFFF.
AFFF Release Site #2 (Fire Training Area): Impacted Soil

## Slide 30
Total PFAS: 49 µg/L
AOF: 190 µg/L
Total PFAS: 1,200 µg/L
AOF: 2,400 µg/L
Total: 0.16 µg/L
AOF: <2.0 µg/L
Total PFAS: 8.0 µg/L
AOF: 18 µg/L
5% PFOS-
Very high concentration of Total PFASs;
Total Post-TOPs PFASs similar to Total Pre-TOPs PFASs (minimal additional precursors);
AOF 3-6X higher than predicted based on identified PFASs (Excess Fluorine PFASs);
No NTA data (ultrashorts?).
AFFF Release Site #2 (Fire Training Area): Impacted Groundwater (µg/L)
Notes: 6:2 FTS- remained in source area;
PFOS- stays with plume in migration directions
More mobile PFASs diffuse laterally (e.g., PFHxA-, PFBS-, PFHxS-).

## Slide 31
Relative PFAS Makeup and Hypothetical Risk
WWTP
Effluent?
Landfill
Leachate?
Fire Training
Areas?
WWTP
Biosolids?
?
Direct
Exposure
Crop
Uptake
Groundwater Impacts
Leaching
Aquatic
Habitats

## Slide 32
Chart: Example PFAS Group Relative Makeup
| WWTP Effluent | Landfill Leachate | AFFF Groundwater
Pre-TOPs Primary PFASs | 0.016889 | 0.25774 | 0.30209
Post-TOPs Precursor PFASs | 0.0052223 | 0.037953 | 0.14789
Excess Fluorine PFAS | 0.97789 | 0.70431 | 0.55002
Comparison of Relative PFAS Group Makeup
- Effluent vs Leachate vs AFFF-Impacted Groundwater -
Primary
PFASs
Secondary
PFASs
Only in Source Area

## Slide 33
Chart: Example PFAS Group Relative Risk
| WWTP Effluent | Landfill Leachate | AFFF Groundwater
Pre-TOPs Primary PFASs | 0.35239 | 0.67086 | 0.90612
Post-TOPs Precursor PFASs | 0.0072452 | 0.017826 | 0.052043
Excess Fluorine PFAS | 0.64037 | 0.31132 | 0.041838
Comparison of Relative PFAS Group Risk
- Effluent vs Leachate vs AFFF-Impacted Groundwater -
Secondary
PFASs
Primary
PFASs

## Slide 34
Comparison of Relative PFAS Group Makeup
- Biosolids vs Compost vs AFFF-Impacted Soil -
Pre-TOPs
PFAS 0.1%
EOF Not Tested
Primary
PFASs
Secondary
PFASs
Example

## Slide 35
Comparison of Relative PFAS Group Risk
- Biosolids vs Compost vs AFFF-Impacted Soil -
Pre-TOPs
PFAS 1.0%
EOF Not Tested
Primary
PFASs
Secondary
PFASs
Example

## Slide 36
Effluent
Landfills
AFFF-Impacted Groundwater
Chart: 
| WWTP #1 EFFL | WWTP #2-EFFL | WWTP #6-EFFL | Landfill #1 E-6 | Landfill #1 4B | Landfill #1 ASH | AFFF #2 MW-1 | AFFF #2 MW-2 | AFFF #2 MW-3 | AFFF #2 MW-4 | AFFF #2 MW-5 | AFFF #2 MW-7 | AFFF #2 MW-8 | AFFF #2 MW-9
 | 7.2 | 6.8 | 4.6 | 622.5773 | 1040.921 | 84.275 | 109473.6514 | 124456.3954 | 52643.917 | 23569.5933 | 20316.209 | 18651.491 | 21.7304 | 683.5163
Hazard Index
Study Site
Relative “Source Strength” in Terms of Risk (noncancer Hazard)
-WWTP Effluent vs Landfill Leachate vs AFFF-Impacted Groundwater-

## Slide 37
Chart: Study Site
| WWTP #1 Biosolids | WWTP #2 Biosolids | WWTP #6 Biosolids | WWTP #6 Compost | AFFF #1 DU-2 | AFFF #1 DU-3 | AFFF #1 DU-4a | AFFF #1 DU-4b | AFFF #1 DU5F
Total PFAS Risk | 2.5751 | 2.0639 | 1.7083 | 0.73506 | 5.919 | 6.075 | 0.38905 | 0.41427 | 38.113
Biosolids/Compost
AFFF-Impacted Soil
(Hazard Indices in un-remediated
release areas will be much higher)
Relative Source Strength in Terms of Risk (noncancer Hazard)
-Biosolids vs Compost vs AFFF-Impacted Soil-
Hazard Index
Low Heath Risk
Low to Very High Risk

## Slide 38
Study Takeaway Points: General
(based primarily of Hawai‘i Study data)
Testing of initial samples for full suite of PFASs is important in initial stages of an investigation to understand PFAS makeup and estimate Total PFAS Risk:
  Primary Terminal PFASs (pre-TOPs),
  Secondary Terminal PFASs (post-TOPs), and
  Excess Fluorine PFASs (Total Organic Fluorine).
Possible reduction in analyses based on initial data and apparent risk-drivers;
Better understanding of “Excess Fluorine PFASs” needed;
Non-Targeted Analysis is partially useful for identification of compounds associated with excess organic fluorine in a sample;
Ultrashorts (e.g., PFEtA-/TFA) might not be captured by current Absorbable Organic Fluorine methods (excess organic fluorine underestimated?).

## Slide 39
PFASs in WWTP Influent & Effluent
Primary sources include washing of textiles (e.g., water and stain resistant clothing, tablecloths, bed linens, carpet, etc.), + dietary, pharmaceuticals;
TOF analysis required to identify apparent presence of complex mixtures of ultrashort PFASs (risk driven by Excess Fluorine PFASs and Primary Terminal PFASs);
Low to moderate toxicity in comparison to drinking water action levels;
Low to moderate risk to drinking water aquifers if used for irrigation (e.g., depending on irrigation method and hydrogeology);
Potential uptake into food crops requires additional research (HIDOH 2025 field study).
No significant acute or chronic toxicity risk to aquatic organisms and habitats (well below published action levels);
Bioaccumulation in aquatic food chain requires additional research (focus on filter feeders and freshwater fish);
Concentration and toxicity of PFASs in wastewater from operations that use PFASs-based media (e.g., AFFF) could be significantly higher.

## Slide 40
PFASs in WWTP Biosolids & Compost
Primary sources include washing of textiles (e.g., water and stain resistant clothing, tablecloths, bed linens, carpet, etc.);
TOPs processing required to identify precursor compounds in biosolids (risk driven by Secondary Terminal PFASs);
Precursors oxidized during curing of compost (risk driven by Primary Terminal PFASs);
Low toxicity in comparison to risk-based, soil action levels;
Disposal of biosolids at municipal landfills not anticipated to pose significant health risk to workers or significantly add to PFAS burden in leachate;
Risk posed by uptake of PFASs into produce from fresh biosolids likely low to moderate but requires additional research (mobile PFASs quickly taken up or leached to groundwater?).

## Slide 41
PFASs in Landfill Leachate
Primary sources include textiles, carpet, furniture, treated paper, etc.
TOF analysis required to identify apparent presence of complex mixtures of ultrashort PFASs (moderate contribution to potential health risk);
High toxicity in comparison to drinking water action levels (risk driven by Primary Terminal PFASs +/- Excess Fluorine PFASs?);
Threat to underlying aquifers low provided that permit-required, engineering controls to prevent leakage of leachate from landfill are maintained;
Investigation of potential PFASs in groundwater at retired, unlined landfills recommended;
Disposal of landfill leachate at municipal WWTPs not anticipated to significantly affect total PFASs burden or toxicity provided that controls are in place to limit maximum daily disposal volume (e.g., <0.1% of total daily influent).

## Slide 42
PFASs in AFFF-Impacted Soils
Pre-2005 AFFF dominated by PFOS (risk driven by Primary Terminal PFASs);
Post-2005 AFFF dominated by precursor-related PFASs (risk driven by Secondary Terminal PFASs);
Potential high toxicity in comparison to risk-based, soil action levels;
Ongoing leaching of PFASs from soil can pose long-term threat to groundwater.

## Slide 43
PFASs in AFFF-Impacted Groundwater
Impacts by pre-2005 AFFF likely dominated by PFOS- and PFHxS-;
Impacts by post-2005 AFFF likely dominated by short-chain compounds associated with breakdown of PFAS precursors (PFBA-, PFPeA-, PFHxA-);
Potential high toxicity in comparison to HIDOH drinking water action levels (risk driven by Primary Terminal PFASs in source area, Excess Fluorine PFASs in downgradient areas???);
Comparison of data to currently promulgated MCLs for long-chain PFASs only night not be adequate for post-2005 releases;
TOF analysis required to identify apparent presence of complex mixtures of ultrashort PFASs (dominate in leading edges of plumes???);
Low to potentially high acute or chronic toxicity risk to aquatic organisms and habitats from discharges to water bodies (requires additional research);
Bioaccumulation in aquatic food chain from discharges to water bodies requires additional research (e.g., filter feeders, freshwater fish).

## Slide 44
Ultrashorts | Ultrashorts | Ultrashorts | Ultrashorts ???
HFPO DA- | HFPO DA- | HFPO DA- | 
PFHxA- | PFHxA- | PFHxA- | 
PFPeA- | PFPeA- | PFPeA- | 
PFBS- | PFBS- | PFBS- | 
PFHpA- | PFHpA- | PFHpA- | 
PFBA- | PFBA- | PFBA- | 
PFOA- | PFOA- |  | 
PFHxS- | PFHxS- | PFHxS-? | 
PFDA- | PFDA- |  | 
6:2 FTS- | 6:2 FTS- |  | 
PFNA- | PFNA- |  | 
PFOS- | PFOS- |  | 
PFHpS- | PFHpS- |  | 
PFUnDA- |  |  | 
6:2 FTOH- |  |  | 
PFDS- |  |  | 
PFOSA- |  |  | 
6:2 FtTAOS- |  |  | 
PFDoDA- |  |  | 
PFTrDA- |  |  | 
PFTeDA- |  |  | 
Ultrashort PFASs at Margins and Leading Edges of Plumes?
(plume separation based on predicted sorption and mobility)
Leading Edge
Source
Area
High sorption PFASs concentrated in and near source area;
Low sorption PFASs at leading edge of plume (including precursor short chain and ultrashort chain breakdown products);
Monitor for ultrashorts and Excess Organic Fluorine in margins and downgradient areas of plumes.
Decreasing Mobility
GW
Moderate sorption coefficient but common in groundwater with no apparent nearby source
Midplume
Near
Source
TFA-, PFPrA-, etc.?

## Slide 45
Chart: 
| PFBA- | 6:2 FTOH | PFPrA- | PFHxA- | 6:2 FTTAoS | PFPeA- | 6:2 FTS- | PFBS- | ADONA- | PFTeDA- | PFHpA- | PFOSA | PFHpS- | PFDS- | PFDoDA- | PFTrDA- | PFUnDA- | PFOA- | PFNA- | HFPO-DA- | PFDA- | PFOS- | PFHxS-
PFBA- 6:2 FTOH PFPrA- PFHxA- 6:2 FTTAoS PFPeA- 6:2 FTS- PFBS- ADONA- PFTeDA- PFHpA- PFOSA PFHpS- PFDS- PFDoDA- PFTrDA- PFUnDA- PFOA- PFNA- HFPO-DA- PFDA- PFOS- PFHxS- | 0.21111 | 1 | 2.9231 | 7.6 | 7.6 | 7.6 | 9.5 | 9.7436 | 12.6667 | 12.6667 | 57 | 190 | 316.6667 | 380 | 380 | 570 | 570 | 760 | 1266.6667 | 1266.6667 | 1266.6667 | 1900 | 1900 | 1900
Potential Passage of Ultrashorts Through GAC?
(granulated activated carbon)
PCBs
Arsenic
DDT
TCE
CrVI
PCE
Benzene
Dioxins = 1,000X PFOS
Increasing Toxicity
Naphthalene
PFEtA-
PFBA-
6:2 FTOH-
Anticipated Removal
of PFASs by GAC
Ultrashorts?
PFPrA-
?

## Slide 46
Questions? Ideas?
Ongoing Research:
Additional WWTP sample collection;
Uptake of PFASs into food crops;
Leaching of PFAS from soil/biosolids (action levels, SPLP batch test, modified Soil Column test);
Bioavailability of PFASs in soil & biosolids;
PFAS vapor intrusion risks;
Edits? Suggestions? Send to John Jacob, PhD (State Toxicologist; john.jacob@doh.Hawaii.gov)
All models are wrong, but some are useful.
George Box
It’s better to be roughly right than precisely wrong.
John Maynard Keynes

## Slide 47
Mahalo and Aloha!
tosbrewer@yahoo.com